## Slide 1
EDMG PHY Header-A for DCM SQPSK Over Two Channel Aggregation in 11ay
Date: 2017-01-15
Authors:

## Slide 2: Motivation
    The contributions of [2] proposed DCM SQPSK over two aggregated channels and the following motion has been passed[1]:
          -In the Single Carrier mode in 11ay, DCM SQPSK signals transmitted over two aggregated channels may be supported.
It was agreed that DCM SQPSK may be supported in the single carrier mode for two contiguous or non-contiguous channel aggregation. [1][2].
      So, we consider that including related bit for DCM SQPSK over two aggregated channels in EDMG-header-A for EDMG SU PPDU is necessary.

## Slide 3: Additional EDMG-Header-A fields
To indicate whether DCM SQPSK over two aggregated channels is applied or not, “DCM SQPSK over two aggregated channels field (1bit)” is needed in the EDMG-Header-A for EDMG SU PPDU .
Field name | Number of bits | Description
DCM SQPSK over two aggregated channels field | 1 | A value of 1 indicates that DCM SQPSK over two aggregated channels is applied. A value of 0 indicates that DCM SQPSK over two aggregated channels is not applied.

## Slide 4: Summary
Regarding DCM SQPSK over two aggregated channels, the following motion of the contribution [2] has been passed:
      In the Single Carrier mode in 11ay, DCM SQPSK signals transmitted over two aggregated channels presented in page 6 may be supported.
In this contribution, additional EDMG-Header-A field for EDMG SU PPDU are proposed:
  DCM SQPSK over two aggregated channels field (1 bit)

## Slide 5: Straw Poll
Do you agree to add the following field ‘DCM SQPSK over two aggregated channels field (1 bit)’ in the EDMG-header-A for an EDMG SU PPDU to the SFD:
  A value of 1 indicates that DCM SQPSK over two aggregated channels is applied.
  A value of 0 indicates that DCM SQPSK over two aggregated channels is not applied.
  Reserved if either TX or RX does not support DCM SQPSK over two aggregated channels.
  Yes
  No
  Abstain

## Slide 6: References
[1] 11-16-1556-00-00ay-tg-ay-november-2016-san-antonio-meeting-minutes
[2] 11-16-1490-00-00ay, DCM SQPSK for Channel Aggregation in 11ay,Huawei