## Slide 1: Packet Design for Wake-up Receiver (WUR)
Date: 2017-01-10
Authors:
Name | Affiliation | Address | Email
Ning Wei | ZTE Corp. | No.9 XiFeng road, Xi’an, China | 
Kaiying Lv |  |  | lv.kaiying@zte.com.cn
Bo Sun |  |  | 

## Slide 2: Background
The solution of making low power wake-up receiver (LP-WUR)[1] as a companion radio has been proposed enabling low power consumption and low latency of 802.11 devices
In [1][2][3], AP transmits an independent WUR packet compatible to legacy protocol to awaken sleeping main module (radio) of a STA
  Also, OOK and OFDM are considered to modulate the payload portion of wake-up packet ; OFDM modulates the legacy preamble .
Figure1 wake-up packet format in [1][2][3]

## Slide 3: Use Case
11ax will be a dominate wi-fi technology used in dense environments in the future with its new multi-user transmission feature.
It’s predictable that 11ax will be deployed to support various applications, including IoT applications.
WUR can help a deployed 11ax network to support IoT applications with ultra low power requirements.
The challenge is to enable WUR even during 11ax’s multi-user transmission

## Slide 4: Issue Analysis
  In dense environment, WUR STAs and 11ax STAs should be able to coexist and share the medium to improve spectrum efficiency
  Simultaneous transmission in wide bandwidth is supposed to be an optimum option due to reduced channel contention
  A very low data rate comparing to 802.11 devices makes it unnecessary to allocate considerable spectrum resources to WUR module, therefore wide bandwidth will be wasted if only transmit a WUR packet at a time.
Presented wake-up packet format with legacy preamble in [1][2] needs to solve EIFS issue
  802.11 STAs can not recognize WUR portion of a wake-up packet, which prevents all 802.11 STAs from a normal channel access operation until waiting for an EIFS time.

## Slide 5: Proposal
Empowering AP to transmit one wireless frame carrying both wake-up and WLAN messages to sleeping and working STAs simultaneously in OFDMA
  Wireless frame includes two segments, i.e. preamble and payload.
  The preamble refers to the preamble of HE DL MU PPDU format without preamble puncturing
    legacy preamble + RL-SIG + HE-SIG-A + HE-SIGB (+ HE-STF + HE-LTF)
    Note, the preamble can contain the legacy preamble only with affordable change complexity to ax transmitter.
  The payload carries both wake-up and WLAN messages over different RUs
  Modulating preamble and WLAN messages in OFDM and wake-up messages in OFDM + OOK or OOK only
Figure 2 proposed frame structure for an 80MHz transmission

## Slide 6: Proposal (cont.)
  AP assigns 2046 to STA-ID field in HE SIG-B corresponding to RU allocated to WUR
    An 802.11ax STA won’t decode messages over RU allocated to WUR
    No EIFS issue due to correct decoding of the PPDU
  Wake-up message can occupy one or multiple RUs in payload of wireless frame
    The location of RUs where wake-up message lies can be predefined or negotiated between a WUR STA and its associated AP or announced by its associated AP
  The null RUs can protect the demodulation for wake-up messages from interference
    The spectrum leakage of each subcarrier in OFDM systems may influence the demodulation performance of energy detection in time domain for wake-up messages

## Slide 7: Proposal (cont.)
Pros
  Low implementation complexity considering supporting OFDMA being a mandatory feature in 802.11ax
  Improving utilization efficiency of spectrum resource within a fixed period of time due to more frequency resources being utilized for transferring WLAN and wake-up messages
  Low latency and low overhead due to less frame transmission and less channel contention
  No EIFS issue for 802.11ax STAs
Cons
  Requiring AP to support 802.11ax (i.e. OFDMA)
  Not suitable in scenarios where the coverage is limited by power.

## Slide 8: Conclusion
In dense environment, presented way to deliver wake-up packet independently can not nearly guarantee a low cost and high utilization efficiency of spectrum resource
In this contribution, we propose that capable AP transmits a wireless frame with wake-up and WLAN messages in OFDMA to awaken sleeping STAs and respond to working STAs simultaneously

## Slide 9: References
[1] 11-16-0341-00-lrlp-low-power-wake-up-receiver-follow-up
[2] 11-15-1307-01-0wng-low-power-wake-up-receiver-for-802-11
[3] 11-16-1144-00-0wur-further-investigation-on-wur-performance