## Slide 1: Explanations for CR on 27.5.2.7 NDP feedback report
Date: 2017-03-06
Authors:

## Slide 2: Background (1)
It is well accepted that being able to get a very short simultaneous feedback from a high number of STAs (all STAs) improve the 11ax system and power efficiencies [1], [3]
  Many feedbacks require 1 bit: PS-Poll (power efficiency), Channel Availability (collisions avoidance)
  Other feedbacks could be 2 bit. For example: “How many buffered Bytes for transmission: 0, 1 to 1000, 1000 to 5000, > 5000 ?”
  A short simultaneous resource request feedback (1 or several bits) capable of supporting a high number of STAs is needed for an efficient UL MU simultaneous scheduling in addition to the existing (or enhanced) piggybacked buffer information
  Less overhead for resource request feedback than polling method
  Low and stable latency for resource request feedback, compared to possibly high and unpredictable latency with CSMA-CA in dense environments

## Slide 3: Background (2)
In Nov. 2016, added subclause 25.5.2.7 to the spec: 25.5.2.7 NDP feedback report procedure The NDP feedback report is a mechanism for an HE AP to collect short feedbacks from a very high number of HE STAs, in an efficient manner. The feedbacks (e.g. resource requests) are sent without data payloads in response to a Trigger frame. The feedbacks are not for channel sounding. This mechanism is optional for non-AP STA.
But details of the NDP feedback mechanism are TBD
Contribution 44r1 proposes a signaling technique for the NDP feedback mechanism that can handle a high number of STAs and is power and air time efficient
This contribution proposes to define a new trigger type for NDP feedback report and the procedure for an HE non-AP STA to know, based on the trigger frame, if it can respond and what parameters to use to respond

## Slide 4: Trigger frame proposal
We propose to define a new trigger type for NDP feedback report
  This is the cleanest solution, as specific common info field parameters are needed for this mechanism and as this mechanism should be generic and work for multiple types of feedbacks
We propose that this trigger type contains all the information so that:
  STAs can know if they are scheduled
  STAs can know on which allocation they can transmit their response, that allocation being unique
  STAs can know what is the type of feedback that is requested and how many bits for the feedback

## Slide 5: Proposed design for the trigger frame
Use information in common info field and trigger dependent common info field.
 | Feedback type | Feedback size | Scheduling Type | GroupID | Starting STA | Probe request option | Target RSSI | Number of users per set of tones | Duplicate | Ressource request buffer threshold
Bits: | 4 | 8 |  | 6 | 11 | 1 | 7 | 2 | 1 | 4
Trigger dependent common info field

## Slide 6: Feedback types
We propose to define types of feedback, and a field to identify the type
  We define the resource request type
  We can then easily define others
For each feedback type, we can define and limit the modes of operation:
  number of bits of feedback
    For instance, if feedback type is resource request, it has to be a 1-bit feedback and the mapping is the following
    For a 1-bit feedback, PHY design allows to have 3 states
      a state with no-response
      A state with a bit received with a value of 0
        Defines a resource request for a small payload
      A state with a bit received with a value of 1
        Defines a resource request for a larger payload
  Mode for selecting the scheduled users
    Range of AIDs
    GroupID
b0 Value | Description
0 | Resource request with buffered bytes for transmission between 1 and “resource_request_buffer_threshold”
1 | Resource request with buffered bytes for transmission above “resource_request_buffer_threshold”

## Slide 7: Feedback types
With this solution, it is also possible to define multiple feedbacks
  Some feedback type indexes are associated with a single pre-defined feedback
  Some feedback type indexes can be associated with multiple pre-defined feedbacks
For each index, there is a clear spec sub-section that describes how the bits are assigned to each feedback (including the number of bits) and how to encode them

## Slide 8: Scheduling the STAs with range of AID
If Scheduling type field is set to zero, the STAs are scheduled with a range of AIDs
The trigger frame identifies the group of STAs that can respond:
This is done by defining a range of consecutive AIDs, by using:
  Starting STA field in the trigger frame
  And the parameters to know how many AIDs are scheduled (NAIDs)
The STAs whose AID is between Starting STA and Starting STA + NAIDs are scheduled
  The index of the STA AID compared to Starting STA is used to know the allocation
This allows:
  Unique allocation per AID
  No need for assigning the allocation in a static manner with any other frame exchanges
  Starting STA field allows to define different groups of STAs and target the AID range that associated STAs are using

## Slide 9: Scheduling the STAs with groupID
If Scheduling type field is set to 1, the STAs are scheduled with groupID
The trigger frame identifies the group of STAs that can respond:
  The groupID field is set to a predefined group ID
  The Starting STA field indicates at which index in the group the range of STAs are scheduled
  STAs that belong to the group and whose index is between Starting STA and Starting STA + NAIDs are scheduled
  The index of the STA in the groupID compared to Starting STA is used to know the allocation

## Slide 10: GroupID management
We propose to enable group management as in 11ac
  Frame unicasted to a STA to indicate to which group it is a member and the position of that STA in these groups.
  9 bits to indicate groups positions (instead of 2 with 11ac)
For this, we propose to define a new HE Group ID Management frame (HE action frame)
  It replicates 11ax groupID management
  It includes Membership status array field already defined in 9.4.1.54
  It includes a new HE user Position Array field (see below with the changes compared to User Position Array field used in 11ac)
B0 | B1 |  | B63 | 
Membership Status In Group ID 0 | Membership Status In Group ID 1 | … | Membership Status In Group ID 63 | 
1 | 1 |  | 1 | 
Membership Status Array field |  |  |  | 
 | B0 B1 | B2 B3 |  | B126 B127
 | User Position In Group ID 0 | User Position In Group ID 1 | … | User Position In Group ID 63
Bits: | 2 9 | 2 9 |  | 2 9
HE User Position Array field |  |  |  | 

## Slide 11: Deriving parameters for transmission of the response (allocation)
The response follows the UL MU operation
The parameters of the trigger-based PPDU are derived from the trigger frame, and each AID has a unique combination of:
  242 RU allocation
  Tone sets allocations within each RU
  NUM_STS
These are calculated based on:
  AID range option: index “AID-AID start” and parameters from trigger frame: feedback size, BW, number of users per set of tones
  Group ID: index “STA position in the group – Index start” and parameters from trigger frame: feedback size, BW, number of users per set of tones

## Slide 12: Deriving parameters for transmission of the response (allocation)
STAs are assigned in order depending on their AID or GroupID index, starting from Starting STA:
  Assign all frequency allocations on the whole bandwidth using SS1 first
    18 first STAs for a 20MHz BW
    36 first STAs for a 40MHz BW (if duplicate =0)
  Then assign the following STAs using incremented SSs.
    Next 18 STAs are assigned the same allocations but with SS2
For BW > 20MHz:
  If duplicate field is equal to 0, allocations in frequency are done in order on the whole bandwidth
    18 first STAs in the first 20MHz, 18 following STAs in the second 20MHz…
  If duplicate field is equal to 1, the same set of users are assigned the same allocation in each 20MHz

## Slide 13: Example of user mapping
 |  | Pm-c1 | Pm-c2
242 RU1 | TS0 | 0 | 36
 | TS1 | 1 | 37
 | … | … | …
 | TS18 | 17 | 53
242 RU2 | TS0 | 18 | 54
 | TS1 | 19 | 55
 | … | … | …
 | TS18 | 35 | 71
40MHz – 2 P-matrix codes
 |  | Pm-c1 | Pm-c2
RU1 | TS0 | 0 | 72
 | TS1 | 1 | 73
 | … | … | …
 | TS18 | 17 | 89
RU2 | TS0 | 18 | 90
 | TS1 | 19 | 91
 | … | … | …
 | TS18 | 35 | 107
RU3 | TS0 | 36 | 108
 | TS1 | 37 | 109
 | … | … | …
 | TS18 | 53 | 125
RU4 | TS0 | 54 | 126
 | TS1 | 55 | 127
 | … | … | …
 | TS18 | 71 | 143
80MHz – 2 P-matrix codes

## Slide 14: Power control
TargetRSSI is included in the trigger dependent common info field
This enables power control with the same target for all STAs

## Slide 15: Specific mode for request for probe response
groupID field set to the value of a groupID
Associated STAs belonging to the signaled group ID shall respond as explained in previous slides.
If the field “probe request option” is set to 1, it indicates that the last available allocation is assigned for non-associated STAs to send single bit indicating probe request.
  This may be useful in HD/VHD deployments, such as stadiums or malls.
The AP shall make sure that there is one allocation at the end of the bitmap not assigned to the STAs belonging to the groupID
Non-zero value of the allocation assigned for probe requests in the received NDP feedback indicates that at least one STA requested a Probe Response frame.
A single Probe Response shall be transmitted by the AP with the Addr1 set to Broadcast Address allowing all the non-associated STAs that transmitted the single-bit probe request to receive the probe response, preventing multiple APs from transmitting a probe-response.

## Slide 16: Summary
We propose to progress on the definition of the NDP feedback report procedure
  New trigger type
  Parameters to identify the scheduled STAs
  Parameters for scheduled STAs to derive the parameters for the response
  Resource request type

## Slide 17: Straw Poll 2bis
Which option do you prefer?
  STAs scheduled by a NDP feedback report trigger frame variant with a feedback type set to “resource request” are identified by:
    Option 1: a single mode: a range of AIDs
    Option 2: 2 modes: a mode with a range of AIDs and a mode with groupID

## Slide 18: Straw Poll 2
Do you agree to define a new NDP feedback report trigger frame variant

## Slide 19: Strawpoll #3
Do you agree to define that the STAs scheduled by a NDP feedback report trigger frame variant with a feedback type set to “resource request” are identified by
  Option 1: one range of AIDs
  Option 2: one or multiple ranges of AIDs
  Note: A range of AIDs is defined to be between AID start and AID start + NAIDs - 1. The trigger frame includes the AID start parameter and the needed parameters to calculate NAIDs

## Slide 21: Straw Poll #3
Do you agree that the RU allocation, RU tone set allocation and starting_STS_num for the NDP feedback response from an HE non-AP STA are calculated based on common parameters in the new NDP feedback report trigger frame variant. A “duplicate” field is defined in the new NDP feedback report trigger frame variant to indicate that STAs allocation are calculated on with a 20MHz bandwidth and are duplicated on the other 20MHz channels

## Slide 22: Straw Poll #4
Do you agree that, for resource request feedback type:
  The feedback size is set to “1 bit” only
  The NDP feedback report trigger frame variant has a field called “resource request buffer threshold”
  Scheduled STAs send a 0 for the NDP feedback report to indicate a resource request with buffer size below the “resource request buffer threshold”
  Scheduled STAs send a 1 for the NDP feedback report to indicate a resource request with buffer size above the “resource request buffer threshold”

## Slide 23: Straw Poll #5
Do you agree with the mode defined in slide 20 to allocate one allocation to all unassociated STAs to make a request for a transmission by the AP of a probe response.

## Slide 24: References
[1] IEEE 802.11-16/1367r0: NDP feedback report
[2] IEEE 802.11-15/1334r1: HE-LTF sequence design
[3] IEEE 11-17-0044-00-00ax-NDP short feedback design

## Slide 25: Straw Poll #4bis
Which option do you prefer:
The “resource request buffer threshold” allows to make 2 levels of resource requests, one for a payload smaller than the threshold, one for a payload higher than the threshold
  Option 1: The “resource request buffer threshold” is indicated in the eliciting NDP feedback report poll trigger frame
  Option 2: The “resource request buffer threshold” is indicated in an IE sent by the AP

## Slide 26: Annex – PHY design currently proposed

## Slide 27: How to define the NDP feedback mechanism?
UL MU transmission in response to a trigger frame
Use frequency dimension for many small orthogonal allocations
To avoid collisions, assign orthogonal allocations to users
No data payload (NDP), STAs transmit energy on one orthogonal allocation for feedback
  with spreading gain in time domain for PHY robustness
For minimal changes to the current PHY, we propose
  to use UL MU NDP simultaneous transmissions in response to a trigger frame
  and to define orthogonal allocations (resource block RBs) to multiplex different STAs’ feedbacks
  These orthogonal allocations (RBs) are defined by using different frequency tone sets

## Slide 28: Overview of proposed signaling for Short Feedback
For each 20MHz, the 242 tones RU are divided into 18 tones sets. Each tone set is made of 12 tones that are equally distributed over the RU (2 tones adjacent to each other)
1 allocation is made of 1 tone sets and a SS
  1 or multiple allocations can be uniquely assigned to one STA
  1 bit can be transmitted using 1 allocation (1 tone sets, made of 2 subsets of 6 tones)
    1 is sent by modulating to first tone subset and not the second one
    0 is sent by modumation the second subtone set and not the first one
Channel estimation is not needed for detection
AP and STAs must have a prior agreement on allocation assignement

## Slide 29: Proposed distribution of tones over 242 tones

## Slide 30: Tone set indices for each 20 MHz: IULf
P-Matrix 1x1 | P-Matrix 2x2 | P-Matrix 4x4 | 2 bit or 1 bit high power |  |  |  | 
 |  |  | 1 bit |  |  |  | 
Tone sets | Tone sets | Tone sets | b0 = 1 | b0 = 0 |  | b1 = 1 | b1 = 0
1 | 1,2 | 1,2,3,4 | -113,-77,-41,6,42,78 | -112,-76,-40,7,43,79 |  | -95,-59,-23,24,60,96 | -94,-58,-22,25,61,97
2 | : | : | -111,-75,-39,8,44,80 | -110,-74,-38,9,45,81 |  | -93,-57,-21,26,62,98 | -92,-56,-20,27,63,99
3 | : | : | -109,-73,-37,10,46,82 | -108,-72,-36,11,47,83 |  | -91,-55,-19,28,64,100 | -90,-54,-18,29,65,101
4 | : | : | -107,-71,-35,12,48,84 | -106,-70,-34,13,49,85 |  | -89,-53,-17,30,66,102 | -88,-52,-16,31,67,103
5 | : | : | -105,-69,-33,14,50,86 | -104,-68,-32,15,51,87 |  | -87,-51,-15,32,68,104 | -86,-50,-14,33,69,105
6 | : | : | -103,-67,-31,16,52,88 | -102,-66,-30,17,53,89 |  | -85,-49,-13,34,70,106 | -84,-48,-12,35,71,107
7 | : | : | -101,-65,-29,18,54,90 | -100,-64,-28,19,55,91 |  | -83,-47,-11,36,72,108 | -82,-46,-10,37,73,109
8 | : | : | -99,-63,-27,20,56,92 | -98,-62,-26,21,57,93 |  | -81,-45,-9,38,74,110 | -80,-44,-8,39,75,111
9 | 17,18 | 33,34,35,36 | -97,-61,-25,22,58,94 | -96,-60,-24,23,59,95 |  | -79,-43,-7,40,76,112 | -78,-42,-6,41,77,113
10 | 19,20 | 37,38,39,40 | -95,-59,-23,24,60,96 | -94,-58,-22,25,61,97 |  |  | 
11 | : | : | -93,-57,-21,26,62,98 | -92,-56,-20,27,63,99 |  |  | 
12 | : | : | -91,-55,-19,28,64,100 | -90,-54,-18,29,65,101 |  |  | 
13 | : | : | -89,-53,-17,30,66,102 | -88,-52,-16,31,67,103 |  |  | 
14 | : | : | -87,-51,-15,32,68,104 | -86,-50,-14,33,69,105 |  |  | 
15 | : | : | -85,-49,-13,34,70,106 | -84,-48,-12,35,71,107 |  |  | 
16 | : | : | -83,-47,-11,36,72,108 | -82,-46,-10,37,73,109 |  |  | 
17 | : | : | -81,-45,-9,38,74,110 | -80,-44,-8,39,75,111 |  |  | 
18 | 35,36 | 69,70,71,72 | -79,-43,-7,40,76,112 | -78,-42,-6,41,77,113 |  |  | 

## Slide 31: Max # of STAs that can simultaneously send the UL Short Feedback
BW | Response = 1 bit |  |  | Response = 2 bit |  | 
 | Nss = 1 | Nss = 2 | Nss = 4 | Nss = 1 | Nss = 2 | Nss = 4
20 MHz | 18 | 36 | 72 | 9 | 18 | 36
40 MHz | 36 | 72 | 144 | 18 | 36 | 72
80 MHz | 72 | 144 | 288 | 36 | 72 | 144
160 MHz | 144 | 288 | 576 | 72 | 144 | 288

## Slide 32: Straw Poll 1
Do you agree to modify the spec following the comment resolutions in document 17-073r1?