## Slide 1: SRP-Based SR Operation
Date: 2017-01-15
Authors:

## Slide 2: Abstract
An overview of the SRP Based Spatial Reuse Mechanism
Details of the SRP Based Spatial Reuse mechanism are found in:
Document 11-16-1476r13
CID too many to mention …

## Slide 3: SRP SR Basic Operation
HE SRP Capable STA identifies an SR Opportunity from an SRP PPDU:
  RXVECTOR parameter SPATIAL_REUSE and/or
  Trigger Frame Common Info Spatial Reuse field
The HE STA is allowed to initiate an SR Transmission for the duration of the ongoing SRP PPDU (SRP Opportunity) if the following SRP conditions are met:
  within a preceding SRP Decision Window, a reverse direction PPDU is detected with the same OBSS Color
    Allowing SR Transmission interference to be estimated
  an SR PPDU is queued for transmission at the SR STA
  Backoff reaches zero during the SRP Opportunity
    To reduce the probability of SR Transmitter collisions
  Transmit power level is adjusted to meet the SRP parameter condition so that interference at the ongoing receiver location is avoided

## Slide 4: Current Status (D1.0)
SRP field exists
  In HE SIGA field of all HE PPDU formats
  In Trigger frame Common Info field
SRP field contents defined
  For just a few cases
  Need to complete the transmission content behavior description
Some SRP values undefined
  SR_DELAY, SR_RESTRICTED – mentioned, but value not defined
Recipient behavior not described
  Need definition of behavior

## Slide 5: Basic Case Description First
I.e. Trigger and trigger-based PPDU sequence
  This is the simplest, basic case
  Following description of components of SRP will refer to this case
  SRP components include:
    Transmitter SRP field contents
    Behavior for recipient of PPDU, based on SRP field contents
      Rules for determining when an SR Transmission can be made
      TX Power for SR transmitter
      Backoff for SR transmitter
      Duration of SR transmission when allowed
      Acknowledgement transmission rules

## Slide 6: SRP Field for Transmitter Trigger (1)
DSRP_PPDU
  Definition: PPDU which contains at least one Trigger MPDU
DSRP_PPDU SIGA SRP field:
  SR_DELAY = recommended value
    Let’s recipient know that a trigger MPDU with full SRP parameter values is present in the payload
  Numerical value ok
    TXPower + Acceptable Receiver Interference
    E.g. allows SRP during trigger PPDU, e.g. Trigger+DATA
  SR_DISALLOW ok, prevents SRP on the Trigger PPDU, but does not prevent SRP during the following trigger-based PPDU

## Slide 7: SRP Field for Transmitter Trigger (2)
Trigger MPDU Common Info Spatial Reuse field:
  Numerical value
    TXPower + Acceptable Receiver Interference
    AP dictates Target RSSI for Trigger-based PPDU(s) that are response(s) to the Trigger
    AP dictates the MCS for all Trigger-based PPDUs
    AP knows current interference level at the AP location
    Therefore, AP can calculate expected SINR of Trigger-based PPDU
    AP can place this “acceptable receiver interference” into the Trigger MPDU Common Info field, UL Trigger-based PPDU responders will copy the SRP value from the Trigger Common Info into the UL Trigger-based PPDU PHY SRP field
  Never SR_DELAY
  SR_DISALLOW ok

## Slide 8: SR STA SRP Check
  SR STA definition: a STA that receives DSRP_PPDU
  Must determine if an SRP Opportunity exists
  Assume that SIGA SRP = SR_DELAY
  SR STA decodes payload, finds Trigger, examines SRP field in Common Info
    Numerical value means SRP Op is possible if conditions can be met
    SR STA checks TX Power condition based on measured RSSI of DSRP_PPDU, assumes reciprocal path loss
    I.e. if AP transmitted Trigger was received at SR STA location with RSSI of X, then SR STA assumes that SR STA transmission would arrive at AP location with RSSI of X
    Therefore, SR STA can determine estimated level of interference with Trigger-based PPDU, for any given TX power
    SRP parameter in Trigger-based PPDU provides maximum interference allowed

## Slide 9: SR STA Backoff
If Interference condition can be met by SR STA upon transmission
  Backoff must be performed
  Multiple SR STA might exist, without backoff, they would transmit simultaneously
  Backoff is just continuation of existing backoff
    Simple, and reflects fact that even under non-SRP conditions, different STA will see different Medium Condition and count different backoff countdown

## Slide 10: SR STA SR Transmission
If backoff expires, SR STA transmits, provided that the transmission does not exceed the duration of the SRP PPDU
  To decode Trigger Common Info field, full PPDU has been decoded and medium is BUSY for the duration of the DSRP_PPDU
    Rules proposed make this explicit
  I.e. backoff will not expire until sometime during the Trigger-based PPDU transmission
    PHY Header of Trigger-based PPDU must be received first
    Confirmation of COLOR of DSRP_PPDU and Trigger-based PPDU occurs

## Slide 11: SR PPDU Acknowledgement
Acknowledgement of SR PPDU can cause interference
  Acknowledging STA must check local SR conditions before responding
  Normal ACK ignores all medium indications
  Responding STA must be able to distinguish SR PPDU from Normal PPDU
    Need indication within transmitted SR PPDU that it is an SR PPDU
    Provided within A-Control
  Recipient must check SR condition locally before deciding to respond with ACK to avoid causing interference to reception of original Trigger-based PPDU

## Slide 12: DSRP_PPDU and Trigger-based PPDU
SR Opportunity from DSRP_PPDU
UL STA
AP
SR initiator
OBSS
Transmission
SR responder
HE Trigger-Based PPDU
DSRP_PPDU
HE Trigger-based PPDU
Duration from Common Info field
Trigger frame MPDU
Trigger Frame
TX PowerSR Initiator < SRP – RSSItrigger frame

## Slide 13: TSRP_PPDU, Trigger not Identified
SR Opportunity from TSRP_PPDU
UL STA
AP
SR initiator
OBSS
Transmission
SR responder
HE Trigger-Based PPDU
Idle or PPDU with same Color
Trigger Frame
TX PowerSR Initiator < SRP – INTFlevel
HE Trigger-based PPDU
Duration from LSIG
If preceding PPDU detected with same Color, not identified as Trigger, e.g. SR parameter not SR_DELAY and payload not correctly decoded, INTFlevel = RSSIPPDU
If a preceding PPDU with same Color is identified as Trigger, then the case is DSRP_PPDU
If IDLE detected before TSRP_PPDU, INTFlevel = RSSENSITIVITYMINIMUM

## Slide 14: UL HE SU PPDU or HE MU PPDU
SR Opportunity identified from an uplink HE SU PPDU or HE MU PPDU
UL STA
AP
SR initiator
OBSS
Transmission
SR responder
HE UL SU PPDU or HE MU PPDU
ULSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
TX PowerSR Initiator < SRP – highest received power level of all beacons of the same BSS color received within the previous 100ms
Given that PPDU is UL, then the intended recipient is an AP – if we can identify the AP by color and if we have observed a Beacon corresponding to this AP, then we can estimate SR STA interference

## Slide 15: DL HE SU PPDU or HE MU PPDU
SR Opportunity identified from a downlink HE SU PPDU or HE MU PPDU
SR Initiator is restricted to AP only
AP
Non-AP STA
AP (SR initiator)
OBSS
Transmission
SR responder
HE SU PPDU or HE MU PPDU
DLSRP_PPDU (HE SU PPDU or HE MU PPDU)
PPDU Duration
TX PowerSR Initiator < SRP – highest received power level of all OBSS PPDUs of the same BSS color received during the previous 500 ms
Given that PPDU is DL, then the intended recipient is some unknown STA within the OBSS – the best estimate of SR STA interference to that recipient is to use the highest RSSI of all PPDU received with that color

## Slide 16: Precedence of SRP vs OBSS PD SR
OBSS PD is based on an assumption
  That the average intra-BSS path power is greater than the average inter-BSS path power
  Average assumed is not always true
  Degree of failure of assumption unknown
SRP provides measured information on an active link
  Uses measured path power to estimate interference
  Does not rely on global average assumptions
  Information is known, interference is estimable
Whenever SRP information is available and STA is capable, OBSS_PD should be DISABLED

## Slide 17: Straw Poll
Do you support the adoption of 11-16-1476r14 as the resolution for CIDs related to SRP?
  Y
  N
  A