## Slide 1: 11ax PAR Verification using UL MU-MIMO
Date: 2017-01-15
Authors:

## Slide 2: Introduction
PAR of 11ax promises Four times throughput gain over 11ac.
Many companies have provided simulation results for 4 times throughput improvement in PAR[1-5], using some features in 802.11ax, specifically, OFDMA, MU-MIMO and spatial reuse.
This presentation is to verify the four times throughput gain using UL MU-MIMO, similar to [5]
Align the results with other companies’ for PAR verification

## Slide 3: Simulation Assumptions [5]
Scenario: Indoor, single BSS
Channel model: Channel-D
Bandwidth: 20MHz @ 5GHz
Antenna number:
  AP: 4 ; non-AP STA: 1
Transmit Power:
    AP: 20dBm ; non-AP STA: 15dBm
Traffic model: full buffer, UL only
Packet size: 1460 bytes
Access protocol:
  802.11ac: EDCA
  802.11ax: Trigger + UL MU-MIMO + M-BA (EDCA disabled)
STA position: random (uniform distribution) within a certain BSS range
Simulation variable:
  STA number; BSS Range;
BSS Range

## Slide 4: UL-MU-MIMO Results Comparison with Huawei’s Results [5]
Chart: System Throughput in Mbps
| 11ac | 11ax | 11ac | 11ax | TOSHIBA | HUAWEI
5 STAs | 74.39 | 289.14 | 72.3 | 293.3
15 STAs | 63.05 | 291.4228 | 65.8 | 291.6
50 STAs | 52.64 | 291.0954 | 57.5 | 293.3
100 STAs | 46.89 | 289.1901 | 48.7 | 292.4
200 STAs | 40.23 | 289.8839 | 41.5 | 292.4
500 STAs | 31.72 | 289.1901 | 33.1 | 292.4
Setting:
  BSS range = 10 m
  Number of STAs range from 5 to 500
  Random scheduling
  Packet Aggregation (Max AMPDU 64)
Conclusion:
  All the STAs close to AP
    Use high MCS to transmit
    11ac: Aggregate as many packets and send when channel accessed
    11ax: UL MU Padding overhead, Trigger frame +M-BA overhead

## Slide 5: 11ax = Improvement in Dense Scenarios?
11ax is envisaged to improve throughput in dense scenarios
“Density” as a parameter needs to be used to verify this claim
Setting:
  BSS range = 10 m & 40 m
  Vary Density (randomly) by varying number of STAs
  and BSS range
  Random scheduling
  Packet Aggregation ON and OFF
  Plot the throughput improvement of 11ax over 11ac
  averaged over a few ranges of Density, for 2 different
  BSS ranges , 10m and 40m respectively.
BSS Range

## Slide 6: 11ax = Improvement in Dense Scenarios?
Chart: Throughput improvement vs Density for UL MU MIMO
| 1.5915507752443827 | 4.7746523257331477 | 15.915507752443826 | 31.831015504887652 | 63.662031009775305 | 159.15507752443827 | 212.20677003258444
BSS Range =10m (Agg OFF) | 5.0151 | 5.4292 | 6.9665 | 8.6265 | 10.595 | 20.8202 | 19.1937
BSS Range = 40m (Agg OFF) | 3.1902 | 3.5061 | 4.4253 | 5.7787 | 7.2485 | 13.477 | 16.533
BSS Range = 10m (Agg ON) | 3.8868 | 4.6221 | 5.5299 | 6.0821 | 7.2057 | 8.9909 | 11.839
BSS Range = 40m (Agg ON) | 5.1 | 4.63 | 2.98 | 2.19 | 2.09 | 2.77 | 3.03

## Slide 7: Conclusion
We demonstrate 4 times throughput gain using UL MU-MIMO
AP deployments with high-density small cell size has the best performance of 11ax over 11ac
The denser the STAs are deployed, more the gain of 11ax
  Heavy Collisions in 11ac causing channel access delays
The throughput gain is more when the STAs are deployed closer to the AP
  Higher MCS and aggregation gain
Future work:
  Focus on aligning the results for OFDMA with other companies
  Consider a more realistic traffic(DL/UL) and simulation scenario (multiple BSS)

## Slide 8: References
[1] 11-15-1095-10-00ax-ofdma-performance-in-11ax
[2] 11-16-1143-01-00ax-11ax-par-verification
[3] 11-16-1198-03-00ax-preliminary-11ax-par-verification
[4] 11-16-1166-00-00ax-meeting-par-requirements-with-ul-ofdma
[5] 11-16-1414-00-00ax-Verifying PAR using UL MU MIMO

## Slide 9: Observations
  When Aggregation OFF, 11ac’s performance is poor, owing to the channel access overhead by the STAs each time while 11ax ULMUMIMO has multiplexing gain, this reflects as improved throughput gain as compared to when Aggregation is ON.
    For high dense scenarios (high density), 11ac fails miserably with collisions, 11ax uses Trigger for UL, hence no collisions , therefore there is an increase in the throughput gain as density increase
    For BSS range =40m, 11ax and 11ac performance is lower than the case of 10m. In addition when the density increase, the gap increases as well
  Throughput gain can be more than 4 times