## Slide 1: TX Masks
Date: 2017-01-16
Authors:

## Slide 2: Abstract
TX Masks for 802.11ay to cover all bandwidths are provided along with technical justification

## Slide 3: 802.11ay Masks For All Bandwidths (1)
Channel BW = 1 has the same mask as 802.11ad
Revised masks for channel bandwidths 2, 3, and 4

## Slide 4: Revised Proposal for 802.11ay Mask (2)
Levels remain the same as 802.11ad (0, -17, -22, and -30 dB)
First corner shifts by the channel spacing
Remaining corners scale with bandwidth (to accommodate spectral re-growth from amplifier non-linearity)
1 Channel (same as 802.11ad)
  First corner at 0.94 GHz
  Second corner at 1.2 GHz
  Third corner at 2.7 GHz
  Fourth corner at 3.06 GHz
2 Channels
  First corner at 2.02 GHz (i.e. 0.94 GHz+ 2.160 GHz / 2)
  Second corner at 2.40 GHz (i.e. 2 *1.2 GHz)
  Third corner at 5.40 GHz
  Fourth corner at 6.12 GHz

## Slide 5: Revised Proposal for 802.11ay Mask (3)
3 Channels
  First corner at 3.10 GHz
  Second corner at 3.60 GHz
  Third corner at 8.10 GHz
  Fourth corner at 9.18 GHz
4 Channels
  First corner at 4.18 GHz
  Second corner at 4.80 GHz
  Third corner at 10.80 GHz
  Fourth corner at 12.24 GHz

## Slide 6: Proposed 802.11ay Mask (3)
Mean ACI level across adjacent channel bandwidth is increased slightly
CB 1 = -19.2 dB
CB 2 = -16.5 dB
CB 3 = -15.0 dB
CB 4 = -13.7 dB
Wider bandwidth signal PSD will scale downward
Net interference is less

## Slide 7: PA Distortion Results (1)
New results under tighter conditions
Rapp Model from 802.11ay Evaluation Methodology
Root raised cosine beta = 0.3
Pi/2 BPSK Modulation
0.5 dB back-off from Psat

## Slide 8: PA Distortion Results (2)
CB = 1

## Slide 9: PA Distortion Results (3)
CB = 2

## Slide 10: PA Distortion Results (4)
CB = 3

## Slide 11: PA Distortion Results (5)
CB = 4

## Slide 12: References
Draft 802.11 RevMC, D8.0
IEEE 802.11-15-0866r4 11ay Evaluation Methodology