## Slide 1: Signaling for 11ay Spatial Sharing
Date: 2017-01-13
Authors:
Name | Company | Address | Phone | Email
Kyungtae Jo | LG Electronics |  |  | kyungtae.jo@lge.com
SungJin Park |  |  |  | allean.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
JinMin Kim |  |  |  | jinmin1230.kim@lge.com
Saehee Bang |  |  |  | saehee.bang@lge.com
Sang G. Kim |  |  |  | sanggook.kim@lge.com
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com

## Slide 2: Introduction
The following text was incorporated into SFD :
  “11ay shall provide means to extend the DMG spatial sharing mechanism for operation in a multi-channel configuration.”
  “The Directional Channel Quality Request and Report measurement types shall be modified to support:
    Request and report for measurements on multiple channels, and
    Measurements reports averaged over multiple channels”
  “The EDMG spatial sharing mechanism shall enable an EDMG STA to perform concurrent measurements employing multiple RX antenna configurations as are used for receiving multiple streams from the target EDMG STA based on the same measurement configuration.”
  “The EDMG spatial sharing mechanism shall enable an EDMG STA to report the average of the results of concurrent measurements using multiple RX antenna configurations in order to reduce the overhead of the measurement report.”
Based on above, this contribution intends to suggest concrete signaling for 11ay spatial sharing.

## Slide 3: Recap on Draft 0.1 (1/3)
Directional Channel Quality Request frame
 | Description
Measurement Channel Bitmap | Indicates one or multiple channels for which spatial sharing applied.
Channel Measurement Report Method | 0: The results of measurements for the requested measurement channels during a measurement time block are individually reported. 1: The average of the results of measurements for the requested measurement channels during a measurement time block is reported.
Antenna Measurement Report Method | 0: The results of concurrent measurements during a measurement time block are individually reported. 1: The average of the results of concurrent measurements during a measurement time block is reported.
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time | Measurement Duration | Number of Time Blocks | Optional Sub-elements
Octets: | 1 | 1 | 1 | 1 | 1 | 8 | 2 | 1 | Variable
Subelement ID | Name | Extensible
0 | Reserved | 
1 | Directional Channel Quality Reporting | Yes
2 | Measurement Configuration | Yes
3-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 
 | Measurement Channel Bitmap |  | Channel Measurement Report Method | Antenna Measurement Report Method
Bits: | 6 | 1 |  | 1
Measurement Configuration sub-element data field

## Slide 4: Recap on Draft 0.1 (2/3)
Directional Channel Quality Report frame
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time | Measurement Duration | Number of Time Blocks | Measurement for Time block 1 | … | Measurement for Time block M | Optional sub-elements
Octets: | 1 | 1 | 1 | 1 | 1 | 8 | 2 | 1 |  |  |  | Variable
Subelement ID | Name | Extensible
0 | Measurement Configuration | Yes
1 | Extended Measurement Report | Yes
4-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 
 | Measurement Channel Bitmap |  | Channel Measurement Report Method | Antenna Measurement Report Method
Bits: | 6 | 1 |  | 1
Measurement Configuration sub-element data field
 | Description
Measurement Channel Bitmap | Indicates one or multiple channels for which spatial sharing applied.
Channel Measurement Report Method | 0: The results of measurements for the requested measurement channels during a measurement time block are individually reported. 1: The average of the results of measurements for the requested measurement channels during a measurement time block is reported.
Antenna Measurement Report Method | 0: The results of concurrent measurements during a measurement time block are individually reported. 1: The average of the results of concurrent measurements during a measurement time block is reported.

## Slide 5: Recap on Draft 0.1 (3/3)
Extended Measurement Report data field in Report frame
 | Number of Rx Antennas for 1st Requested Channel (NRX,1) | Measurement Results for 1st Requested Channel | Number of Rx Antennas for 2nd Requested Channel (NRX,2) | Measurement Results for 2nd Requested channel |  | Number of Rx Antennas for Nch-th Requested Channel (NRX,Nch) | Measurement Results for Nch-th Requested channel
Octets: | 1 | N1*(NRX,1-1) | 1 | N2*NRX,2 |  | 1 | NNch*NRX,Nch
 | Measurement Results for 2nd Reported Channel | Measurement Results for 3rd Reported Channel |  | Measurement Results for Nch-th Reported Channel | 
Octets: | N2 | N3 |  |  | NNch
 | Number of Rx Antennas (NRX) | Measurement Results for 1st Rx Antenna | Measurement Results for 2nd Rx Antenna |  | Measurement Results for NRX Rx Antenna
Octets: | 1 | N | N |  | N
Subelement ID | Name | Extensible
0 | Measurement Configuration | Yes
1 | Extended Measurement Report | Yes
2-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 
Optional Sub-elements
    Case 1. When both the Channel Measurement Report Method subfield and the Antenna Measurement Report Method subfield set to 0
    Case 2. When the Channel Measurement Report Method subfield sets to 0 and the Antenna Measurement Report Method subfield sets to 1
    Case 3. When the Channel Measurement Report Method subfield sets to 1 and the Antenna Measurement Report Method subfield sets to 0

## Slide 6: Signaling for Multi-channel/antenna SPSH (1/2)
Modification of Directional Channel Quality Request frame
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time | Measurement Duration | Number of Time Blocks | Optional Sub-elements
Octets: | 1 | 1 | 1 | 1 | 1 | 8 | 2 | 1 | Variable
Subelement ID | Name | Extensible
0 | Reserved | 
1 | Directional Channel Quality Reporting | Yes
2 | Measurement Configuration | Yes
3 | Extended Measurement Configuration | Yes
4-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 
 | Measurement Start Time for 2nd Requested Channel | Measurement Duration for 2nd Requested Channel | Number of Time Blocks for 2nd Requested Channel (N2) | … | Measurement Start Time for Nch-th Requested Channel | Measurement Duration for Nch-th Requested Channel | Number of Time Blocks for Nch-th Requested Channel (NNch)
Octets: | 8 | 2 | 1 |  | 8 | 2 | 1
Extended Measurement Requset sub-element data field
  The Extended Measurement Configuration subelement contains measurement timing information for the requested 2.16GHz channels excluding the first 2.16GHz channel.
  The measurement timing information for all the requested 2.16GHz channel except for the first channel is indicated in the Measurement Start Time field, the Measurement Duration field and Number of Time Blocks field.

## Slide 7: Signaling for Multi-channel/antenna SPSH (2/2)
Modification of Directional Channel Quality Report frame
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time | Measurement Duration | Number of Time Blocks | Measurement for Time block 1 | … | Measurement for Time block M | Optional sub-elements
Octets: | 1 | 1 | 1 | 1 | 1 | 8 | 2 | 1 |  |  |  | Variable
Subelement ID | Name | Extensible
0 | Measurement Configuration | Yes
1 | Extended Measurement Configuration | Yes
2 | Extended Measurement Report | Yes
3-220 | Reserved | 
221 | Vendor Specific | 
222-255 | Reserved | 
 | Measurement Start Time for 2nd Requested Channel | Measurement Duration for 2nd Requested Channel | Number of Time Blocks for 2nd Requested Channel (N2) | … | Measurement Start Time for Nch-th Requested Channel | Measurement Duration for Nch-th Requested Channel | Number of Time Blocks for Nch-th Requested Channel (NNch)
Octets: | 8 | 2 | 1 |  | 8 | 2 | 1
Extended Measurement Requset sub-element data field

## Slide 8: Summary
We suggest that signaling for multi-channel/antenna SPSH modified by using Optional sub-elements of existing Directional Channel Quality Request/Report frame.

## Slide 9: Straw poll/motion #1
Do you agree to add the signaling for multi-channel and multiple RX antenna SPSH using Optional Sub-elements in Directional Channel Quality Request/Report frame (shown on slide 6-7) into the SFD?