## Slide 1: Discussions on Signaling for UL HE MU PPDU
Date: 2017-01-16
Authors:

## Slide 2: UL HE MU PPDU
In 11ax Draft 1.0, UL HE MU PPDU is defined
  An HE non-AP STA may transmit UL HE MU PPDU to an HE AP
    If the HE AP sent an HE Capabilities element with the UL HE MU PPDU Payload Support field equal to 1
  UL HE MU PPDU can be transmitted in full bandwidth or partial bandwidth (106-tone RU within 20MHz)
  HE-SIG-B’s STAID in user field indicates the transmitting non-AP STA
UL HE MU PPDU is beneficial in that the transmitter can reveal its STAID in preamble part, and that it can utilize the 106-tone RU.
However, since the HE-SIG-B field is designed for DL MU communication, it may incur unnecessary overhead when used for UL HE MU PPDU

## Slide 3: LB225 CIDs on Signaling for UL HE MU PPDU
CID | Page.line | Comment | Proposed Change
5412 | 285.55 | An HE MU PPDU with the UL/DL field set to 1 is intended to one STA and the HE-SIG-B design is not efficient. | Please refine the HE-SIG-B design for the UL case to reduce the length of the HE-SIG-B field.
6194 | 84.26 | For UL HE MU PPDU transmission from an STA to an AP, the current SIG-A/B design incurs overhead because the current format is designed for DL MU signaling. SIG-B's RU allocation and User specific fields can be redundant overheads for UL HE MU PPDU. | Please specify UL HE MU PPDU's SIG-A/B signaling detail.
7032 | 84.28 | For the current HE-SIG-B design which is designed for DL MU signalling, it is inefficient to signal full-BW UL HE MU PPDU transmission. RU allocation field is not required in full-BW UL HE MU PPDU, since SIG-A's BW subfield signals the PPDU BW and the signaling of RU allocation is not needed. | Please clarify SIG-A/B signalling method for full bandwidth (20/40/80/160(80+80) MHz) UL HE MU PPDU transmission with the minimal overhead.
7033 | 84.28 | For the current HE-SIG-B design which is designed for DL MU signalling, it is inefficient to signal partial bandwidth transmission (left or right 106tone/20MHz) of UL HE MU PPDU transmission. For example, it requires signalling of RU allocation (106, -, 106) and two User specific information fields where one user information field would be useless. | Please clarify SIG-A/B method for partial bandwidth (left/right 106-tone RU within 20MHz) UL HE MU PPDU transmission with the minimal overhead.

## Slide 4: Full-BW UL HE MU PPDU example
For example, if a non-AP STA transmits 80MHz UL HE MU PPDU to an AP
  HE-SIG-A’s BW field indicates 80MHz
  HE-SIG-B’s common block field in each content channel indicates redundantly
    Two 8-bit RU Allocation fields indicating “996(1-STA)”
    One 1-bit Center 26-tone RU field indicating “0”
    10-bit CRC/Tail
In each HE-SIG-B content channel, 18/18/27/43 bits of overhead respectively for 20/40/80/160(80+80)MHz UL HE MU PPDU
Therefore, it is not required to transmit the Common Block field in HE-SIG-B for the full-BW UL HE MU PPDU case
L-STF
L-LTF
L-
SIG
PSDU
S
V
C
T
A
I
L
RL-
SIG
HE-
SIG-A
HE-
SIG-B
HE-
STF
HE-
LTF
L-STF
L-LTF
L-
SIG
RL-
SIG
HE-
SIG-A
HE-
SIG-B
L-STF
L-LTF
L-
SIG
RL-
SIG
HE-
SIG-A
HE-
SIG-B
L-STF
L-LTF
L-
SIG
RL-
SIG
HE-
SIG-A
HE-
SIG-B
Field | Bit | Descriptions
UL/DL | 1 | 1: UL
Bandwidth | 3 | 2: 80MHz
... | ... | ...
User
RA
C/T
C/T
padding
C
26
RA
User
RA
C/T
C/T
padding
C
26
RA
HE-SIG-B
Content CH 1
HE-SIG-B
Content CH 2
signaling
overhead

## Slide 5: Partial-BW UL HE MU PPDU example
For example, if a non-AP STA transmits right 106-tone RU in Primary 20MHz to an AP using UL HE MU PPDU
  HE-SIG-A’s BW field indicates 20MHz
  HE-SIG-B indicates
    One 8-bit RU Allocation field indicating “106(1-STA), -, 106(1-STA)”
    10-bit CRC/Tail
    Two User specific info fields while the first includes STAID 2046 indicating RU carries no data
In HE-SIG-B, 39 bits of overhead for 106-tone/20MHz UL HE MU PPDU
Therefore, more efficient signaling is needed for the partial-BW UL HE MU PPDU
L-STF
L-LTF
L-
SIG
PSDU
S
T
RL-
SIG
HE-
SIG-A
HE-
SIG-B
HE-
STF
HE-
LTF
User
(Null
STAID)
RA
C/T
C/T
padding
User
RA (8bits) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9
0110 0000 | 106 (1-STA) |  |  |  | - | 106 (1-STA) |  |  | 
HE-SIG-B
Content CH
signaling
overhead
Field | Bit | Descriptions
UL/DL | 1 | 1: UL
Bandwidth | 3 | 2: 20MHz
... | ... | ...

## Slide 6: Proposed signaling for UL HE MU PPDU
HE-SIG-B’s Common Block field is redundant for UL HE MU PPDU
  For the full-BW UL HE MU PPDU
    PPDU’s bandwidth is signaled in SIG-A’s BW field
    Then RU Allocation field is not needed
  For the partial-BW UL HE MU PPDU
    Simple indication of left/right 106-tone RU in primary 20MHz can be signaled in HE-SIG-A’s BW field (similar to the 106-tone signaling in HE ER SU PPDU)
Proposal
  For UL HE MU PPDU, the Common Block field of HE-SIG-B is not present
  For the partial-BW UL HE MU PPDU, the left/right 106-tone RU within the primary 20MHz is signalled in HE-SIG-A’s BW field (reusing the preamble puncturing bit ranges in DL)

## Slide 7: Summary
A non-AP HE STA may transmit UL HE MU PPDU to an HE AP if it is allowed
However, the current SIG-B design incurs signaling redundancy
  18~43 bits of SIG-B overhead in full-BW PPDU
  39 bits of SIG-B overhead in partial-BW PPDU
For UL HE MU PPDU, we propose that Common Block field of HE-SIG-B is not present and bandwidth options are signaled in SIG-A

## Slide 8: Strawpoll #1
Do you agree with the following?
  When the UL/DL field in the HE-SIG-A field of an HE MU PPDU is set to 1 (indicating UL HE MU PPDU), the Common Block field is not present and the content channel consists of only the User Specific field.
  Y/N/A

## Slide 9: Strawpoll #2
Do you agree with the following?
  When the UL/DL field in the HE-SIG-A field of an HE MU PPDU is set to 1 (indicating UL HE MU PPDU), the Bandwidth field in the HE-SIG-A field of an HE MU PPDU is defined as follows:
    Set to 0 for full 20 MHz
    Set to 1 for full 40 MHz
    Set to 2 for full 80 MHz
    Set to 3 for full 160 MHz and 80+80 MHz
    Set to 4 for lower 106-tone RU within the primary 20MHz
    Set to 5 for higher 106-tone RU within the primary 20MHz
    Values 6-7 are reserved
  Y/N/A