## Slide 1: Link Transmit Power
Date: 2017-01-16
Authors:

## Slide 2: Abstract
TX EVM defined in standard was low bar for receiver design expectations a few years ago
Modern receivers can typically handle increased EVM
Also, for example, LDPC requires less stringent EVM requirements
Additional receiver design improvements are likely in the future
TX Power is typically conservative due to implementation variance
Link Transmit Power signaling mechanism allows
  Increase in TX Power per MCS to allow higher MCS use
  Reduction in TX Power to aid in system wide spatial reuse

## Slide 3: CID 8098
Add a mechanism to set the transmit power per direction per link in order to achieve an increase in performance due to improved receiver design since the original EVM specification was written. | Add a mechanism to set the transmit power per direction per link in order to achieve an increase in performance due to improved receiver design since the original EVM specification was written. Expect a submission detailing some changes.

## Slide 4: Basic Scheme
Add capability of a receiver to request transmitter power per MCS for this link
  Within regulatory limits
  Not to affect transmitter power on other links with the same STA
  Hence, Link Transmit Power
  A STA requests a higher power per MCS at its own estimate/risk
    LTP requester
  Power can be re-adjusted at any time
    Per new request from LTP requester
    Per LTP responder initiative accompanied by unsolicited LTP response to inform LTP requester of the change
  Use a new LTP Request / LTP Response exchange

## Slide 5: Add a capability indication
Extended Capability information element (IE)
  Existing location for dot11 type-independent features
  E.g. this feature can be used by any letter designation
    E.g. 11n, 11ac, 11ax, 11afuture
  Link Transmit Power capability bit
  Not clear that this bit is really needed
    No reason why a STA could not send the new element to anyone and if they do not recognize it, they do nothing
    If they do recognize it, they could still refuse to cooperate
    If they do recognize it, they will respond

## Slide 6: Add an information element
Link Transmit Power (LTP) information element
Used to communicate request from receiver to transmitter
  Increase/decrease TX Power per MCS
New element can be included in various management frames
  Most likely a new Public or Protected Dual of Public Action
No response requierd (other than ACK)
  Transmitter either complies with request or does not comply
  If Transmitter makes changes, then it must inform the receiver by sending an LTP element as a response

## Slide 7: Add a management action frame
Add to Public and Protected Dual of Public
  To avoid type-specific categories

## Slide 8: LTP Requester Behavior
STA which transmits an LTP IE request
  Does not know exactly how much change in EVM might result at a given MCS for a given amount of TX power change
    Estimate is possible if LTP requester sees transmissions from LTP responder at various MCS and power combinations to allow it to make measurements
    Otherwise, LTP requester might have to try a few times to find a comfortable value
Desirable to include a test frame
  NDP included in specific exchanges (see later slides)
If LTP request is not accepted, then no new request allowed for X ms

## Slide 9: LTP Responder Behavior (1)
LTP responder (LTP IE recipient) can choose to use or ignore the LTP IE information
  LTP responder might not be able to raise TX power – it might already be at the regulatory or TPC limit
  LTP responder might not desire to raise TX power in order to manage spectrum
    E.g. cooperative arrangement with neighbors for spatial reuse/interference management
    E.g. in a managed environment
If LTP responder chooses to change transmit power, it must inform the LTP requester (LTP IE sender)
  Sends an LTP response if raising or lowering TX power

## Slide 10: LTP Responder Behavior (2)
TX EVM excursions limited to DATA-bearing frames
TX EVM excursions not allowed for CTRL subtypes
  e.g. RTS, CTS, BA, ACK

## Slide 11: Proposed Changes Summary (1)
Add a capability bit
  Extended Capability IE – preferred location for generic features
Add a new LTP IE
  To carry a list of requested or used PABOMCSn values
  Allow the LTP IE to be transmitted within various management frames
    E.g. Association Request, Association Response, Action, etc
Add a new Management Action frame
  To allow post-association requests/changes to be communicated
No requirement for recipient to obey the request
  But LTP responder must inform LTP requester if LTP responder makes any TX power changes, requested or self-initiated

## Slide 12: Proposed Changes Summary (2)
Change TX EVM rules
  Allow transmitter to exceed TX EVM requirements when LTP requester sends LTP request that would cause EVM limits to be violated
    LTP requester is specifically indicating that it has no problem with the expected increase in EVM
No change to other TX power related rules
  Jurisdictional regulatory limits still apply
  TPC limits still apply
  AP self-imposed limits apply
Recommend addition of test frame transmissions
  E.g. NDP before Beacons

## Slide 13: Straw poll #1
Do you support the concept of Link Transmit Power as outlined in the previous slides, without the requirement to send an NDP?
  Y
  N
  A

## Slide 14: Straw poll #2
Do you support the requirement that an NDP is transmitted by an LTP as outlined in the previous slides?
  Y
  N
  A

## Slide 15: Straw poll #3
Do you support to resolve CID 8098 by adopting the text of 11-17-0123-00-00ax-Link-Transmit-Power-Text?
  Y
  N
  A

## Slide 16: Straw Poll PHY #1
Do you support the concept of allowing a transmitter, per request of a receiver, to violate existing TX EVM by increasing the TX Power for transmissions to that requester?
  Y
  N
  A

## Slide 17: Annex 1
Link Transmit Power Specific Proposed Changes

## Slide 18: Ext Cap IE: add a capability indication
Extended Capability information element (IE)
  Link Transmit Power capability bit
  Ext Cap IE is the location for dot11 type-independent features
  i.e. this feature can be used by any letter designation
    E.g. 11n, 11ac, 11ax, 11future
  Set by AP and by non-AP STA that support LTP
  Acts as implicit NDP request
    See next slide

## Slide 19: Implicit NDP Request
When Ext Cap LTP bit is set by an AP
  AP should transmit NDP, SIFS before each DTIM Beacon
    Using TX Power indicated in the Beacon
      E.g. TPC Report, Power Capability, LTP IE
    NDP transmitted using all TX antennas
When Ext Cap LTP bit is set by non-AP STA and AP also has the bit set
  Non-AP STA should transmit an NDP SIFS following the ACK of its Association Request transmission
    Using TX Power indicated in the Association Request
      E.g. TPC Report, Power Capability, LTP IE
    NDP transmitted using all TX antennas

## Slide 20: Add an information element
Link Transmit Power (LTP) information element
  Used to communicate request from receiver to transmitter
  Used to communicate actual values from transmitter to receiver
New element can be included in various management frames
  Public Action and Protected Dual of Public Action
    New Public Action LTP
  (Re)Association request, (Re)Association response, Beacon, Probe Response
LTP Response is only required when changing PA Backoff (PABO) values
  In response to LTP Request and when unilaterally changing PABO values

## Slide 21: Link Transmit Power Parameters
Link Transmit Power IE contents:
  Transmit power suggestion or report per MCS
    Value of dB [-23, 40.5]
Transmitting STA can provide as many or as few constellation/coding combinations as it desires per request
Transmitting STA can change values as frequently as it desires
Receiving STA can use the information or ignore it

## Slide 22: LTP IE Format
Uses Element ID Extension
  Element ID = 255
  Element ID Extension assigned by ANA
Link Transmit Power Information field contents:
  Series of one-octet transmit power values
    One octet per Constellation/encoding (i.e. one per MCI)
      MCI = MCS Index
    Not necessary to include an octet for every constellation/encoding value
 | Element ID (= 255) | Element Length | Element ID Extension (=<ANA>) | LTP Control | LTP Information
Octets: | 1 | 1 | 1 | 4 | variable

## Slide 23: LTP control field
LTP Report
  LTP Report = 0 indicates a request for the LTP responder to modify TX Power settings according to the accompanying LTP Information
  LTP Report = 1 indicates employed values at the LTP responder
LTP MCI Bitmap
  Bitmap of MCI (MCS Index) values, e.g.
    Value of 1 in bit position B3 means MCI value 2 transmit power information field is present
    Value of 0 in bit position B3 means MCI value 2 transmit power information field is absent
TXBF Present, NTXBF Present
  Indicates if MCI power values are present for TXBF case, Non TXBF case – entries are in MCI pairs when both are present
Supported Modes
  Bitmap of SU, OFDMA (non-MU MIMO), Reserved, when the LTP is a request
  Reserved when the LTP is a Report
Reserved -> requested MCS, Ntx for LTP response
  Alternative = copy the request LTP PPDU parameters, except for NTX
Absolute
  Indicates if MCI TX Power field encoding represents Absolute dBm or Relative dBm (see later slide)
Transmit Power
  Same as the field in the TCP Report IE
 | B0 | B1 B15 | B16 | B17 | B18 B20 | B21 | B22 B23 | B24 B31
 | LTP Report | LTP MCI Bitmap | TXBF Present | NTXBF Present | Supported Modes | Absolute | Reserved | Transmit Power
Bits: | 1 | 15 | 1 | 1 | 3 | 1 | 2 | 8

## Slide 24: MCI Encoding
Independent of BW
MCI Value | Constellation, Encoding
0 | BPSK, ½, DCM
1 | BPSK, ½
2 | QPSK ½
3 | QPSK ¾
4 | 16QAM ½
5 | 16 QAM ¾
6 | 64QAM 2/3
7 | 64 QAM ¾
8 | 64 QAM 5/6
9 | 256 QAM ¾
10 | 256 QAM 5/6
11 | 1024 QAM ¾
12 | 1024 QAM 5/6
13 – 14 | Reserved

## Slide 25: LTP Information field
LTP Power Entry field
  LTP Information field contains 0 or more octets
  Each octet is an LTP Power Entry field
One octet per constellation/encoding-transmit power pair
  As many octets present as needed, as indicated in the LTP MCI Bitmap
MCI TX Power
  See next slide
 | B0 B6 | B7
 | MCI TX Power | Reserved
Bits: | 7 | 1

## Slide 26: MCI TX Power Field Encoding
Maximum transmit power per MCI in dBm
Absolute = 1
  Unsigned integer (range [0,127])
    TXPMCI in dBm = MCI TX Power / 2 – 23
      i.e. MCI TX Power = [-23, 40.5] dBm, 0.5 dB steps
Absolute = 0 (i.e. relative)
  Unsigned integer (range [0,127])
    TXPMCI in dBm = TXPMCS0 – (MCI TX Power / 2 – 23)
      i.e. MCI TX Power = TXPMCS0 - [-23, 40.5] dBm, 0.5 dB steps

## Slide 27: Bidirectional LTP Exchange
A single MPDU may contain two LTP IE
  Provided that:
  One LTP IE has Request = 0
    i.e. response to previous LTP IE Request = 1
  One LTP IE has Request = 1
    i.e. request to STA to which it is sending a response
  Allows fewer frames in exchange to establish bidirectional LTP setup
    E.g. during Association Request/Response exchange sequence

## Slide 28: Add LTP Action to Public Category
Category is Public (=4) or Protected Dual of Public (=9)
  To avoid type-specific categories
Action (=<ANA>)
  LTP
Body is LTP Information IE
 | Category (=4) | Public Action = <ANA>) | LTP Information IE
Octets: | 1 | 1 | Variable

## Slide 29: TX EVM Rules
Change existing standard language TX EVM rule
  Current language includes mandatory EVM requirements
  LTP IE TX power increase request is an indication that the recipient can handle increased EVM
    Third party receivers might have trouble with the increased EVM
      But these devices are usually unlikely to successfully decode the PPDU payload anyway because of MCS mismatch to their path
      These devices are more and more likely to sleep during the PPDU payload portion when the PPDU is not for them
  Allow transmitter to exceed EVM requirement when recipient explicitly allows it through the LTP IE
  TX EVM excursions limited to DATA-bearing frames
    Not allowed for RTS, CTS, BA, ACK

## Slide 30: Reporting Baseline TX Power
LTP Request can be written to express either:
  Relative TX Power Requested
    Stateful, requires requester to know and remember what transmitter has done with TX Power setting
  Absolute TX Power Requested
    Stateless = preferred
In order for an LTP Requester to be able to request an absolute TX Power level, the requester needs to know:
  What was the TX Power level of the PPDU that the requester examined in order to determine that a new TX Power level is desired?
Requires element for reporting – make the following mandatory:
  TX Power Capability Element
  TPC Report Element (and the transmission of this element in response to a request)
Additionally, STAs should be able to interpret:
  TX Power Constraint Element
  Transmit Power Envelope Element
Require that MCS0 power corresponds to the reported TX Power

## Slide 31: Annex 2
Link Transmit Power

## Slide 32: LTP effect on MCS Selection
Depends on how MCS selection is implemented
  E.g. MCS selection is based on SINR estimate vs family of SINR-PER curves
    Choose “a good PER” from all curves at a given SINR estimate
    Can treat TX power changes as a shift in the SINR-PER curve for each MCS which has an adjusted PABO value
In general
  Transmitter must be aware that SINR of link is MCS dependent

## Slide 33: Identifying the Source of the PPDU
When TX Power has been adjusted higher
It is necessary to identify the source of a PPDU at the receiver location at the beginning of the reception
  To adjust the receiver to accommodate the specific EVM of the transmitter
    I.e. to differentiate PPDUs from transmitters employing LTP and those not employing LTP
    E.g. an AP that receives PPDUs from many sources, some of which are using LTP and some of which are not
  It is important to NOT adjust the receiver for a transmission when the transmission is not utilizing a higher LTP for a given MCS

## Slide 34: RTS-CTS Based Source Information
Transmitter uses RTS-CTS exchange before the transmission of the LTP DATA PPDU
  Based on the RTS TA value, the intended recipient knows the source of the upcoming DATA PPDU before the reception begins
    E.g. recipient assumes that DATA PPDU source is the same as the RTS source
    E.g. DATA PPDU source = STA corresponding to RTS TA value
    E.g. LTP is NOT applied to the RTS
      Or the CTS
This should be the standard method for determining the source of a DATA frame transmitted using LTP
  Source “estimate” is possible when RTS-CTS is not present (See Annex)

## Slide 35: Association Exchange Example
      Non-AP STA has measured EVM from AP using the NDP preceding the Beacon reception
        Allows non-AP STA to request modified AP TX Power within Association Request by including LTP IE
      AP measures EVM of non-AP STA using the NDP following the Association Request ACK
        Allows the AP to request modified non-AP STA TX Power within the Association Response by including LTP IE
      Bidirectional exchange allowed (LTP Request and Response in one frame)
      Optional exchange completes bidirectional setup (non-AP STA response)
DTIM Beacon
AP Transmissions
AssReq
ACK
ACK
AssRep
NDP
Non-AP STA Transmissions
LTP Action
ACK
Optional exchange
NDP

## Slide 36: TX Power Reporting
LTP Element
Power Capability Element
TPC Report Element
Transmit Power Envelope Element

## Slide 37: References
[1] 11-17-0123-00-00ax-Link-Transmit-Power-Text.docx
[2] 802.11-2016.pdf
[3] Draft P802.11ax_D1.0.pdf