## Slide 1: Link Transmit Power (LTP)
Date: 2017-04-21
Authors:

## Slide 2: Abstract
Transceivers can benefit from increased EVM when compared to EVM requirements in the spec
  Due to Tx Beamforming, delay spread, Doppler, receiver design, expected variation in operating conditions, e.g. temperature, voltage, ageing, etc.
  Existing EVM spec targeted to SISO, CDD
We show both simulation results and measurement data to justify our proposal
Proposal provides a means for TX Power modification per link
  Per request of the recipient and approval of the transmitter
  Signaling through elements and management frames

## Slide 3: CID 8098
Add a mechanism to set the transmit power per direction per link in order to achieve an increase in performance due to improved receiver design since the original EVM specification was written. | Add a mechanism to set the transmit power per direction per link in order to achieve an increase in performance due to improved receiver design since the original EVM specification was written. Expect a submission detailing some changes.

## Slide 4: Rationale
Reasons to expect that EVM can be increased over EVM in the spec:
  LDPC requires less stringent EVM requirements
  TX EVM varies over operating condition, but TX PA set for worst case
  Beamforming (NTX > NSS) accommodates relaxed EVM
  TX Power is typically conservative due to implementation variance and measurement precision
  Channel delay spread is not known at transmitter
  Doppler is not known at transmitter
TX EVM defined in standard was low bar for receiver design expectations a few years ago
  Modern receivers can typically handle increased EVM due to LDPC, etc.
  Additional receiver design improvements are likely in the future
TX EVM defined in standard was based on SISO, CDD

## Slide 5: LTP Benefits
Link Transmit Power signaling closes the loop with the receiver
  Allowing accuracy in TX Power setting to match (or exceed) TX EVM, receiver capability, channel condition, etc, which transmitter cannot determine
Link Transmit Power signaling mechanism allows:
  Increase in TX Power per MCS to allow higher MCS use
  Reduction in TX Power to aid in system wide spatial reuse

## Slide 6: Transmitter Self Adjustment
Transmitter may be able to make TX power adjustments to account for:
  Precoding Scenario (8x2, 4x2, 2x2, using beamforming or spatial expansion)
  PA characteristic, e.g. non-linearity, with margin for uncertainty in measurement and for dynamic operating condition changes, e.g. voltage, temperature, ageing
    A typical implementation shows an average of 1.5 dB of margin
However, transmitter cannot make adjustments to account for channel condition (Doppler and Delay Spread) and receiver characteristics
Receiver can measure channel effect and request power increase or decrease to optimize link and system gain

## Slide 7: Simulation Conditions, Gain Metric
TSIM = Theoretical simulation model, not an architectural model
  E.g. ideal channel estimates, floating point math
PA simulated is lab measured Skyworks PA (SKY85302-11)
Using Channel B NLOS 80MHz, and D NLOS 80MHz
For NSS=2: tested scenarios are Precoding NTX=4 x NRX=2 and NTX=8 x NRX=2.
For NSS=1: tested scenarios are Precoding NTX=4 x NRX=2 and NTX=8 x NRX=2.
Reference scenario is nominal OBO: power that yields standard specified TX EVM with 1.5dB margin.
  1.5 dB margin based on practical Tx power accuracy used in APs
For each scenario we mark the OBO which optimizes link budget for 10% PER
The optimal OBO is achievable in a closed loop system that controls Tx power based on measured distortion at the receiver
The difference between the optimal OBO and nominal OBO minus the sensitivity change is the LTP gain we could achieve by letting receiver request transmit power.

## Slide 8: Simulation Configuration
NTX=4 and NRX=2
Channel configured for an average attenuation of 0dB
  A particular channel draw can have different attenuation
Receiver noise power, PRX_NOISE , is fixed for a desired SNR range around sensitivity
  Using the predefined average channel attenuation
Receiver signal power, PRX, is random according the channel draw
Beamforming gain depends on channel draw too
The simulation sweeps on transmitted power PTX , at a given OBO and finds the PER threshold of 10%
Actually, the channel is considered as black box and the simulation controls PTX(OBO) and PRX_NOISE
Channel
PTX
PTX
PTX
PTX
PRX
PRX
+
+
PRX_NOISE
PRX_NOISE

## Slide 9: Simulation Results
  For each MCS we plot
    SNR threshold (i.e. required for 10% PER with 1.7kB packets) as function of OBO
    EVM as a function of OBO (green curve)
  EVM is computed and plotted for 2x2 MIMO case, Nss=2, using direct mapping (measurement described in IEEE Std 802.11-2016 21.3.17.4.3)
  Allowed relative constellation error (EVM Spec) is also marked as a black vertical line
  Precoder is normalized to have same power for all antennas, thus precoded signal also obeys same OBO to EVM (green) curve
  OBO setting marked by diamond is the OBO value which maximizes system gain min (Psat/N0)=min (OBO+SNR).

## Slide 10: Theoretical sim vs Lab measurements Chan D 80 MHz MCS6
SNR_th is receiver’s SNR measured at Modem input
  Noise term is AWGN
Dashed curves are from lab
EVM whitening in TSIM improves match
TSIM discards RF impairments except for PA distortion
TSIM uses ideal CE
Curves were scaled according to TSIM vs. ASIM
  4.8dB for BF
  3dB for CDD
  * ASIM = architectural model
    E.g. fixed point math using system component modules
Dashed lines are MEASURED results

## Slide 11: Theoretical sim vs Lab measurements Chan D 80 MHz MCS7
SNR_th is receiver’s SNR measured at Modem input
  Noise term is AWGN
Dashed curves are from lab
EVM whitening in TSIM improves match
TSIM delay diversity in CDD is larger than that of chip which improves TSIM
TSIM discards RF impairments except for PA distortion
TSIM used ideal CE
Curves were scaled according to TSIM vs. ASIM
  4.8dB for BF
  3dB for CDD
Dashed lines are MEASURED results

## Slide 12: LTP Gain Summary
LTP Gain is based on simulated SVD-BF system at optimal OBO vs. OBO of standard EVM + 1.5dB (practical margin for Tx power control accuracy)
BW=80MHz, NRX=2
Max value
Min value

## Slide 13: Conclusion
Link budget increase of 2~7dB for a beamformed system based on LTP
“EVM rejection” of beamforming allows Tx power increase
  Tx EVM isn’t beamformed as opposed to the desired signal
  Beamformed system tolerates relaxed EVM
1.5dB of the Tx power control margins are regained (which are practically taken to assure standard EVM compliance)
  Close loop established by EVM measurements at the receiver eliminate these margins
Optimal Tx power isn’t visible to the transmitter
  Depends on PA nonlinear response
  Depends on channel
LTP based on EVM estimation and Rx performance controls Tx power and increase link budget

## Slide 14: Proposed Draft Changes
Link Transmit Power

## Slide 15: LTP Signaling
Add capability of a receiver to request transmitter power per MCS for this link
  Within regulatory limits
  Not to affect transmitter power on other links with the same STA
  Hence, Link Transmit Power
  A STA requests a higher power per MCS at its own estimate/risk
    LTP requester
  Power can be re-adjusted at any time
    Per new request from LTP requester
    Per LTP responder initiative accompanied by unsolicited LTP response to inform LTP requester of the change
  Use a new LTP Request / LTP Response exchange

## Slide 16: Add a capability indication
Extended Capability information element (IE)
  Existing location for dot11 type-independent features
  E.g. this feature can be used by any letter designation
    E.g. 11n, 11ac, 11ax, 11afuture
  Link Transmit Power capability bit
  Not clear that this bit is really needed
    No reason why a STA could not send the new element to anyone and if they do not recognize it, they do nothing
    If they do recognize it, they could still refuse to cooperate
    If they do recognize it, they will respond

## Slide 17: Add an information element
Link Transmit Power (LTP) information element
Used to communicate request from receiver to transmitter
  Increase/decrease TX Power per MCS
New element can be included in various management frames
  Most likely a new Public or Protected Dual of Public Action
No response required (other than ACK)
  Transmitter either complies with request or does not comply
  If Transmitter makes changes, then it must inform the receiver by sending an LTP element as a response

## Slide 18: Add a management action frame
Add to Public and Protected Dual of Public
  To avoid type-specific categories

## Slide 19: LTP Requester Behavior
STA which transmits an LTP IE request
  Does not know exactly how much change in EVM might result at a given MCS for a given amount of TX power change
    Estimate is possible if LTP requester sees transmissions from LTP responder at various MCS and power combinations to allow it to make measurements
    Otherwise, LTP requester might have to try a few times to find a comfortable value
Desirable to include a test frame
  NDP included in specific exchanges (see later slides)
If LTP request is not accepted, then no new request allowed for X ms

## Slide 20: LTP Responder Behavior (1)
LTP responder (LTP IE recipient) can choose to use or ignore the LTP IE information
  LTP responder might not be able to raise TX power – it might already be at the regulatory or TPC limit
  LTP responder might not desire to raise TX power in order to manage spectrum
    E.g. cooperative arrangement with neighbors for spatial reuse/interference management
    E.g. in a managed environment
If LTP responder chooses to change transmit power, it must inform the LTP requester (LTP IE sender)
  Sends an LTP response if raising or lowering TX power

## Slide 21: LTP Responder Behavior (2)
TX EVM excursions limited to DATA-bearing frames
TX EVM excursions not allowed for CTRL subtypes
  Transmitted in non_HT format
  e.g. RTS, CTS, BA, ACK

## Slide 22: Proposed Changes Summary (1)
Add a capability bit
  Extended Capability IE – preferred location for generic features
Add a new LTP IE
  To carry a list of requested or used PABOMCSn values
  Allow the LTP IE to be transmitted within various management frames
    E.g. Association Request, Association Response, Action, etc
Add a new Management Action frame
  To allow post-association requests/changes to be communicated
No requirement for recipient to obey the request
  But LTP responder must inform LTP requester if LTP responder makes any TX power changes, requested or self-initiated

## Slide 23: Proposed Changes Summary (2)
Change TX EVM rules
  Allow transmitter to exceed TX EVM requirements when LTP requester sends LTP request that would cause EVM limits to be violated
    LTP requester is specifically indicating that it has no problem with the expected increase in EVM
No change to other TX power related rules
  Jurisdictional regulatory limits still apply
  TPC limits still apply
  AP self-imposed limits apply
Recommend addition of test frame transmissions
  E.g. NDP before Beacons

## Slide 24: Straw poll #1
Do you support the concept of Link Transmit Power as outlined in the previous slides, without the requirement to send an NDP?
  Y
  N
  A

## Slide 25: Straw poll #2
Do you support the requirement that an NDP is transmitted by an LTP as outlined in the previous slides?
  Y
  N
  A

## Slide 26: Straw poll #3
Do you support to resolve CID 8098 by adopting the text of 11-17-0123-01-00ax-Link-Transmit-Power-Text?
  Y
  N
  A

## Slide 27: Straw Poll PHY #1
Do you support the concept of allowing a transmitter, per request of a receiver, to violate existing TX EVM by increasing the TX Power for transmissions to that requester?
  Y
  N
  A

## Slide 28: Annex 1
Link Transmit Power Specific Proposed Changes

## Slide 29: Ext Cap IE: add a capability indication
Extended Capability information element (IE)
  Link Transmit Power capability bit
  Ext Cap IE is the location for dot11 type-independent features
  i.e. this feature can be used by any letter designation
    E.g. 11n, 11ac, 11ax, 11future
  Set by AP and by non-AP STA that support LTP
  Acts as implicit NDP request
    See next slide

## Slide 30: Implicit NDP Request
When Ext Cap LTP bit is set by an AP
  AP should transmit NDP, SIFS before each DTIM Beacon
    Using TX Power indicated in the Beacon
      E.g. TPC Report, Power Capability, LTP IE
    NDP transmitted using all TX antennas
When Ext Cap LTP bit is set by non-AP STA and AP also has the bit set
  Non-AP STA should transmit an NDP SIFS following the ACK of its Association Request transmission
    Using TX Power indicated in the Association Request
      E.g. TPC Report, Power Capability, LTP IE
    NDP transmitted using all TX antennas

## Slide 31: Add an information element
Link Transmit Power (LTP) information element
  Used to communicate request from receiver to transmitter
  Used to communicate actual values from transmitter to receiver
New element can be included in various management frames
  Public Action and Protected Dual of Public Action
    New Public Action LTP
  (Re)Association request, (Re)Association response, Beacon, Probe Response
LTP Response is only required when changing PA Backoff (PABO) values
  In response to LTP Request and when unilaterally changing PABO values

## Slide 32: Link Transmit Power Parameters
Link Transmit Power IE contents:
  Transmit power suggestion or report per MCS
    Value of dB [-23, 40.5]
Transmitting STA can provide as many or as few constellation/coding combinations as it desires per request
Transmitting STA can change values as frequently as it desires
Receiving STA can use the information or ignore it

## Slide 33: LTP IE Format
Uses Element ID Extension
  Element ID = 255
  Element ID Extension assigned by ANA
Link Transmit Power Information field contents:
  Series of one-octet transmit power values
    One octet per Constellation/encoding (i.e. one per MCI)
      MCI = MCS Index
    Not necessary to include an octet for every constellation/encoding value
 | Element ID (= 255) | Element Length | Element ID Extension (=<ANA>) | LTP Control | LTP Information
Octets: | 1 | 1 | 1 | 4 | variable

## Slide 34: LTP control field
LTP Report
  LTP Report = 0 indicates a request for the LTP responder to modify TX Power settings according to the accompanying LTP Information
  LTP Report = 1 indicates employed values at the LTP responder
LTP MCI Bitmap
  Bitmap of MCI (MCS Index) values, e.g.
    Value of 1 in bit position B3 means MCI value 2 transmit power information field is present
    Value of 0 in bit position B3 means MCI value 2 transmit power information field is absent
TXBF Present, NTXBF Present
  Indicates if MCI power values are present for TXBF case, Non TXBF case – entries are in MCI pairs when both are present
Supported Modes
  Bitmap of SU, OFDMA (non-MU MIMO), Reserved, when the LTP is a request
  Reserved when the LTP is a Report
Reserved -> requested MCS, Ntx for LTP response
  Alternative = copy the request LTP PPDU parameters, except for NTX
Absolute
  Indicates if MCI TX Power field encoding represents Absolute dBm or Relative dBm (see later slide)
Transmit Power
  Same as the field in the TCP Report IE
 | B0 | B1 B15 | B16 | B17 | B18 B20 | B21 | B22 B23 | B24 B31
 | LTP Report | LTP MCI Bitmap | TXBF Present | NTXBF Present | Supported Modes | Absolute | Reserved | Transmit Power
Bits: | 1 | 15 | 1 | 1 | 3 | 1 | 2 | 8

## Slide 35: MCI Encoding
Independent of BW
MCI Value | Constellation, Encoding
0 | BPSK, ½, DCM
1 | BPSK, ½
2 | QPSK ½
3 | QPSK ¾
4 | 16QAM ½
5 | 16 QAM ¾
6 | 64QAM 2/3
7 | 64 QAM ¾
8 | 64 QAM 5/6
9 | 256 QAM ¾
10 | 256 QAM 5/6
11 | 1024 QAM ¾
12 | 1024 QAM 5/6
13 – 14 | Reserved

## Slide 36: LTP Information field
LTP Power Entry field
  LTP Information field contains 0 or more octets
  Each octet is an LTP Power Entry field
One octet per constellation/encoding-transmit power pair
  As many octets present as needed, as indicated in the LTP MCI Bitmap
MCI TX Power
  See next slide
 | B0 B6 | B7
 | MCI TX Power | Reserved
Bits: | 7 | 1

## Slide 37: MCI TX Power Field Encoding
Maximum transmit power per MCI in dBm
Absolute = 1
  Unsigned integer (range [0,127])
    TXPMCI in dBm = MCI TX Power / 2 – 23
      i.e. MCI TX Power = [-23, 40.5] dBm, 0.5 dB steps
Absolute = 0 (i.e. relative)
  Unsigned integer (range [0,127])
    TXPMCI in dBm = TXPMCS0 – (MCI TX Power / 2 – 23)
      i.e. MCI TX Power = TXPMCS0 - [-23, 40.5] dBm, 0.5 dB steps

## Slide 38: Bidirectional LTP Exchange
A single MPDU may contain two LTP IE
  Provided that:
  One LTP IE has Request = 0
    i.e. response to previous LTP IE Request = 1
  One LTP IE has Request = 1
    i.e. request to STA to which it is sending a response
  Allows fewer frames in exchange to establish bidirectional LTP setup
    E.g. during Association Request/Response exchange sequence

## Slide 39: Add LTP Action to Public Category
Category is Public (=4) or Protected Dual of Public (=9)
  To avoid type-specific categories
Action (=<ANA>)
  LTP
Body is LTP Information IE
 | Category (=4) | Public Action = <ANA>) | LTP Information IE
Octets: | 1 | 1 | Variable

## Slide 40: TX EVM Rules
Change existing standard language TX EVM rule
  Current language includes mandatory EVM requirements
  LTP IE TX power increase request is an indication that the recipient can handle increased EVM
    Third party receivers might have trouble with the increased EVM
      But these devices are usually unlikely to successfully decode the PPDU payload anyway because of MCS mismatch to their path
      These devices are more and more likely to sleep during the PPDU payload portion when the PPDU is not for them
  Allow transmitter to exceed EVM requirement when recipient explicitly allows it through the LTP IE
  TX EVM excursions limited to DATA-bearing frames
    Not allowed for RTS, CTS, BA, ACK

## Slide 41: Reporting Baseline TX Power
LTP Request can be written to express either:
  Relative TX Power Requested
    Stateful, requires requester to know and remember what transmitter has done with TX Power setting
  Absolute TX Power Requested
    Stateless = preferred
In order for an LTP Requester to be able to request an absolute TX Power level, the requester needs to know:
  What was the TX Power level of the PPDU that the requester examined in order to determine that a new TX Power level is desired?
Requires element for reporting – make the following mandatory:
  TX Power Capability Element
  TPC Report Element (and the transmission of this element in response to a request)
Additionally, STAs should be able to interpret:
  TX Power Constraint Element
  Transmit Power Envelope Element
Require that MCS0 power corresponds to the reported TX Power

## Slide 42: Annex 2
Link Transmit Power

## Slide 43: LTP effect on MCS Selection
Depends on how MCS selection is implemented
  E.g. MCS selection is based on SINR estimate vs family of SINR-PER curves
    Choose “a good PER” from all curves at a given SINR estimate
    Can treat TX power changes as a shift in the SINR-PER curve for each MCS which has an adjusted PABO value
In general
  Transmitter must be aware that SINR of link is MCS dependent

## Slide 44: Identifying the Source of the PPDU
When TX Power has been adjusted higher
It is necessary to identify the source of a PPDU at the receiver location at the beginning of the reception
  To adjust the receiver to accommodate the specific EVM of the transmitter
    I.e. to differentiate PPDUs from transmitters employing LTP and those not employing LTP
    E.g. an AP that receives PPDUs from many sources, some of which are using LTP and some of which are not
  It is important to NOT adjust the receiver for a transmission when the transmission is not utilizing a higher LTP for a given MCS

## Slide 45: RTS-CTS Based Source Information
Transmitter uses RTS-CTS exchange before the transmission of the LTP DATA PPDU
  Based on the RTS TA value, the intended recipient knows the source of the upcoming DATA PPDU before the reception begins
    E.g. recipient assumes that DATA PPDU source is the same as the RTS source
    E.g. DATA PPDU source = STA corresponding to RTS TA value
    E.g. LTP is NOT applied to the RTS
      Or the CTS
This should be the standard method for determining the source of a DATA frame transmitted using LTP
  Source “estimate” is possible when RTS-CTS is not present (See Annex)

## Slide 46: Association Exchange Example
      Non-AP STA has measured EVM from AP using the NDP preceding the Beacon reception
        Allows non-AP STA to request modified AP TX Power within Association Request by including LTP IE
      AP measures EVM of non-AP STA using the NDP following the Association Request ACK
        Allows the AP to request modified non-AP STA TX Power within the Association Response by including LTP IE
      Bidirectional exchange allowed (LTP Request and Response in one frame)
      Optional exchange completes bidirectional setup (non-AP STA response)
DTIM Beacon
AP Transmissions
AssReq
ACK
ACK
AssRep
NDP
Non-AP STA Transmissions
LTP Action
ACK
Optional exchange
NDP

## Slide 47: TX Power Reporting
LTP Element
Power Capability Element
TPC Report Element
Transmit Power Envelope Element

## Slide 48: Annex 3
Simulation Summary

## Slide 49: Distortion related SNR Loss Estimation
We show that SNR loss due to distortion is reduced in precoding scenarios, this allows working at lower OBO (achieving higher system gain)
Where
- Receive SNR thresh (e.g. 10% PER) required by the uncompressed link
is the beamforming gain on the signal
is the beamforming effect on distortion.

## Slide 50: References
[1] 11-17-0123-01-00ax-Link-Transmit-Power-Text.docx
[2] 802.11-2016.pdf
[3] Draft P802.11ax_D1.2.pdf