## Slide 1: TXBF FB Vector Sanctity
Date: 2017-01-16
Authors:

## Slide 2: Abstract
TX Beamformer is not aware of TX Beamformee receiver implementation
TX Beamformee can create and send Transmit Vector V that will work best with receiver architecture
TX Beamformer is tempted to modify FB Vector V
Need ability of TX Beamformee to dictate the use of the unaltered FB Vector V
  i.e. enforce the sanctity of the FB Vector for SU PPDU
Add support indication at TX Beamformer
Add ability of TX Beamformee to signal sanctity of FB vector

## Slide 3: CID 8100
Transmit beamformer is sometimes inclined to modify a steering vector that is fed back by the beamformee, and that is often ok, but sometimes, the beamfomee needs to ensure that the beamformer does not alter the vector - so add a Vector Sanctity indication in the HE MIMO control field and describe its use, i.e. somewhere within 27.6 where TXBF for HE specifics appear | Add a bit "Vector Sanctity" to the HE MIMO Control field and a support bit to indicate support for the bit, and add a description of the use of the bit in 10.32 - also consider expanding its use backwards to VHT - expect a submission with detailed changes

## Slide 4: Basic Scheme
Add capability indication for TX Beamformer
  Capability to accept a dictated TXBF FB Vector V
Add indication in TXBF FB frame that indicates “FB sanctity”
  i.e. “do not alter this FB Vector during SU transmissions*”
  * See next slide
Sanctity indication is non-negotiable
  TX Beamformer agreed to accept it, so when it happens, it must obey
Need a mechanism to disable previously indicated sanctity

## Slide 5: Exception to Vector Sanctity
Transmitter is allowed to make steering vector modifications for:
  Corrections to account for the difference in the transfer functions of the TX filters used for the sounding exchange and the SU transmission
  Corrections to balance TX Power per antenna

## Slide 6: Add a capability indication
Extended Capability information element (IE)
  Existing location for dot11 type-independent features
  E.g. this feature can be used by any letter designation
    E.g. 11n, 11ac, 11ax, 11afuture
  TXBF FB Vector Sanctity Support
    When set to 1, indicates that the STA obeys TXBF FB Vector Sanctity in SU PPDU transmissions
  An HE STA that indicates support supports FB Vector Sanctity for every supported TXBF mode
    E.g. if VHT FB is supported, then FB Vector Sanctity is supported for VHT FB
    E.g. if HE FB is supported, then FB Vector Sanctity is supported for HE FB
    E.g. if both VHT and HE FB supported, then FB V S supported for both

## Slide 7: Signal Vector Sanctity With Reserved Bit in VHT FB Frame
VHT Action Frame
  VHT Compressed Beamforming Category (0)
    VHT MIMO Control field
      Bit 16 Reserved
        Change to “Steering Vector Sanctity”
        When Vector Sanctity = 1, TX Beamformer is not allowed to modify the provided vector when it transmits VHT PPDUs to this destination (limited to formats specified in LTP IE)

## Slide 8: Signal Vector Sanctity With Reserved Bit in HE FB Frame
HE Action Frame
  HE Compressed Beamforming And CQI Category (0)
    HE MIMO Control field
      Bit 36 Reserved
        Change to “Steering Vector Sanctity”
        When Vector Sanctity = 1, TX Beamformer is not allowed to modify the provided vector when it transmits HE PPDUs to this destination (limited to formats specified in LTP IE)

## Slide 9: Add a management action frame??
Do we need to have a separate ability to signal vector sanctity outside of the FB frame?
  E.g. when disabling a previous sanctity dictate
Could we simply send a FB frame without the vector?
  i.e. unsolicited FB frame with MIMO control field, but no compressed FB field?
    Field is implicitly missing based on MPDU length - preferred
  i.e. no need to wait for a sounding exchange
Alternative:
  Use another reserved bit in each of the VHT and HE MIMO control fields to indicate that no Matrix or CQI is present
  I.e. change another reserved bit in each of VHT and HE MIMO Control fields to be “No FB Matrix or CQI Present”

## Slide 10: Tone Information Interpolation
TX Beamformer shall use linear interpolation when creating the actual steering vector from the compressed FB steering vector
  When the sanctity bit = 1

## Slide 11: Straw poll #1
Do you support the concept of TXBF FB Vector Sanctity for SU PPDU as outlined in the previous slides?
  Y
  N
  A

## Slide 12: Straw poll #2
Do you support to resolve CID 8100 by adopting the text of 11-17-0122-00-00ax-Steering-Vector-Sanctity-Text?
  Y
  N
  A

## Slide 13: References
[1] 11-17-0122-00-00ax-Steering-Vector-Sanctity-Text.docx
[2] 802.11-2016.pdf
[3] Draft P802.11ax_D1.0.pdf