## Slide 1: TWT Schedule Bitmap
Date: 2017-01-17
Authors:

## Slide 2: Abstract
Selected TWT times might need to change
  Dynamic OBSS interference
  Change in traffic pattern requiring more or less time
  Change in channel requiring more or less time
Desire a mechanism for change in TWT timing
  More convenient than sending a new TWT request
Would be nice if this mechanism could also be used to communicate Inter-BSS information on “network time slots” utilized by OBSS TWT
  Assuming some sort of quantization of network time that is relatable to local TSF

## Slide 3: CID 8097
The TWT negotiation process can be improved. Specifically, if a timeslot bitmap were added to the process then a STA could more concisely indicate its preferred TWT SP times and it could observe the allocated TWT SP times of OBSS neighbors and request time slots that avoid those times. | Add a time slot bitmap to allow simpler negotation of TWT SP times and to allow a simple method of determining when OBSS interference is more likely. Expect a submission detailing some changes.

## Slide 4: Requested/Utilized Time Slots
Need a TWT Time Slot Bitmap (TTSB)
  Bits to indicate time slots of a request, assignment or report
Need a field to indicate channel of reference
  Accompanying TTSB
If the AP schedules any SP then it advertises the schedules to all STA using TTSB
  I.e. AP sends consolidated scheduling information to all STA
  Non-AP STA shall be capable of interpreting TTSB
TTSB can be observed by OBSS
TTSB can be requested/reported between any two STA

## Slide 5: TWT Time Slot Info Present Indication
TWT IE Control Field is modified to include a TWT Time Slot Info Present bit
If TWT Time Slot (TTS) Info Present = 1, TWT Time Slot Info field is present
  If TWT TIM Present = 1 and TWT Time Slot Info Present = 1, then TWT TIM fields precede TWT Time Slot Info fields
 | B0 | B1 | B2 | B3 | B4 | B5 | B6 B7
 | NDP Paging Indicator | Responder PM Mode | Broadcast | Wake TBTT Negotiation | TWT TIM Present | TWT Time Slot Info Present | Reserved
Bits: | 1 | 1 | 1 | 1 | 1 | 1 | 2

## Slide 6: Time Slot Info field in TWT IE
Optionally present in TWT IE
  TWT Time Slot Control describes the TTSB
    Request, Assignment, Report
    Resolution of bitmap time slots
    Bitmap Address Present, Address Type
 | Element ID | Length | Control | Request Type | Target Wake Time | TWT Group Assignment | Nominal Minimum Wake Duration | TWT Wake Interval Mantissa | Broadcast TWT ID | TWT Channel | NDP Paging (optional) | TWT Time Slot Info
Octets: | 1 | 1 | 1 | 2 | 8 or 0 | 9 or 3 or 0 | 1 | 2 | 0 or 1 | 1 | 0 or 4 | 0 or variable
 | TWT Time Slot Bitmap Length | TWT Time Slot Control | TWT Time Slot Bitmap | TWT Bitmap Address | TX TSF | Zero Slot Alignment
Octets: | 1 | 3 | variable | 0 or 6 | 0 or 8 | 0 or 8

## Slide 7: TWT Time Slot Control Field (1)
Request Slots
  Request Slots = 0 means the Time Slot Bitmap indicates either an assigned set of time slots or a report of used time slots
  Request Slots = 1 means the Time Slot Bitmap indicates requested time slots
    Request is for the STA identified by the TA of the MPDU
Assignment
  Assignment = 0 when the Time Slot Bitmap indicates a request or a report of used time slots
  Assignment = 1 when the Time Slot Bitmap indicates an assignment of time slots to the STA identified by the RA of the MPDU
I.e. Request Slots =0, Assignment=0, this is a Report
 | B0 B3 | B4 | B5 | B6 | B7 | B8 B12 | B13 | B14 | B15 | B16 B22 | B23
 | Time Slot Resolution | Bitmap Address Present | BSS Address | Request Slots | Assignment | Max Slots Requested | Report Request | TX TSF Present | Zero Slot Alignment Present | Assigned STA Count | Reserved
Bits: | 4 | 1 | 1 | 1 | 1 | 5 | 1 | 1 | 1 | 7 | 1

## Slide 8: TWT Time Slot Control Request Slots and Assignment bits
Request Slots and Assignment bits encode TWT Time Slot commands Report, Assignment, Request
Request Slots | Assignment | Meaning
0 | 0 | Report - Time Slot Bitmap indicates the slots that have been assigned
0 | 1 | Assignment - Time Slot Bitmap contains slots assigned to the recipient STA
1 | 0 | Request - Time Slot Bitmap contains slots requested by the transmitting STA
1 | 1 | Reserved

## Slide 9: TWT Time Slot Control Field (2)
Time Slot Resolution
  Resolution of each bit in the bitmap is equal to the value of the Time Slot Resolution field (interpreted as an unsigned integer) + 1
    E.g. Time Slot Resolution field value of 0 means resolution value of 1
  The units of the resolution are TBD, e.g. 500 us, 512 us, 1000 us, 1 TU, 2 TU, etc (e.g. base 2 vs base 10 multiples of 1 us)
Bitmap Address Present
  When the field = 1, indicates that a 48-bit 802.1 address is present (see next slides)
  No Bitmap Address present if field has value 0
Max Slots Requested
  Contains the total maximum number of slots requested divided by 2 and truncated (i.e. resolution of 2 slots)
  This might not match the number of slot bits set in the bitmap
    Bitmap likely to contain the BEST choice slots

## Slide 10: TWT Time Slot Control Field (3)
BSS Address
  If BSS Address field = 1 in a report, the report is for an entire BSS:
    And if Bitmap Address Present is 1, the BSS address is provided in the Bitmap Address field
    And if Bitmap Address Present is 0, the BSS is the BSS value of the MPDU containing the TWT Time Slot Info
  When the BSS address field = 0, report is for a single STA
    If Bitmap Address Present is 1, the individual STA address is provided
    If Bitmap Address Present is 0, the individual STA address is the TA of the MPDU containing the TWT Time Slot Info
  In an assignment, the address field is not used
  In a request, the address field is not used
    Protocol could be extended to allow for negotiation between BSSs

## Slide 11: Bitmap Address and BSS Address
Bitmap Address | BSS Address | TWT Time Slot Command | Meaning, assuming Report Request = 0
0 | 0 | Report | TTSB indicates slots used by the STA with the address indicated in the TA field of the MAC header of the MPDU
0 | 1 | Report | TTSB indicates slots used within a BSS, where the BSS address is indicated in the BSS field of the MAC header of the MPDU
1 | 0 | Report | TTSB indicates slots used by the STA with the address indicated in the TWT Bitmap Address field
1 | 1 | Report | TTSB indicates slots used within a BSS, where the BSS address is indicated in the TWT Bitmap Address field
0 | 0 | Assignment | TTSB indicates slots being assigned to the STA with the address indicated in the TA field of the MAC header of the MPDU
0 | 1 | Assignment | Reserved
1 | 0 or 1 | Assignment | Reserved
0 | 0 | Request | TTSB indicates slots requested by the STA with the address indicated in the TA field of the MAC header of the MPDU
0 | 1 | Request | Reserved
1 | 0 or 1 | Request | Reserved
0 or 1 | 0 or 1 | Reserved | Reserved
When Report Request = 0

## Slide 12: TWT Time Slot Control Field (4)
TX TSF Present
  When set to 1, indicates that a TX TSF Field is present
  When set to 0, indicates that no TX TSF Field is present
    E.g. TSF is found somewhere else in the frame
    E.g. A Beacon contains Broadcast TTS Information field, and Beacon already contains a timestamp
  This field would primarily be used when transmitting a TWT Slot Time Bitmap report to an OBSS
Report Request
  Set to 1 to request a report from another STA or BSS
    Use BSS Address=1, Bitmap Address=1 to include requested BSS address

## Slide 13: Bitmap Address and BSS Address
When Report Request = 1
Bitmap Address | BSS Address | TWT Time Slot Command | Meaning, assuming Report Request = 1
0 | 0 | Report | TTSB indicates slots used by the STA with the address indicated in the TA field of the MAC header of the MPDU, individual STA report is requested from the STA indicated in the RA field of the MAC header of the MPDU
0 | 1 | Report | TTSB indicates slots used within a BSS, where the BSS address is indicated in the BSS field of the MAC header of the MPDU, BSS report is requested from the STA indicated in the RA field of the MAC header of the MPDU, for the BSS of which the recipient STA is a member
1 | 0 | Report | TTSB indicates slots used by the STA with the address indicated in the TWT Bitmap Address field, individual STA report is requested from the STA indicated in the RA field of the MAC header of the MPDU
1 | 1 | Report | TTSB indicates slots used within a BSS, where the BSS address is indicated in the TWT Bitmap Address field, BSS report is requested from the STA indicated in the RA field of the MAC header of the MPDU, for the BSS of which the recipient STA is a member
0 or 1 | 0 or 1 | Assignment | Reserved
0 or 1 | 0 or 1 | Assignment | Reserved
0 or 1 | 0 or 1 | Reserved | Reserved

## Slide 14: TWT Time Slot Control Field (5)
Assigned STA Count
  The total number of STA for which the report includes slots that have been assigned
    Set to appropriate value when the report is for a BSS
    Set to 1 when the report is for a single STA
  Note that some slots might be assigned to more than one STA
    An individual STA reporting its own slots will still report a value of 1, because it is unaware of multiple assignments
  When the report is for a BSS
    Value of max representation for the field means that value or greater
      E.g. for a 7-bit Assigned STA count field, 0x7F means a STA count of 127 or more

## Slide 15: Time Slot Bitmap Zeroth Slot Time reference
The start of the zeroth slot of the TWT Time Slot Bitmap is the TSF time corresponding to:
  The value of the Zero Slot Alignment field if present, otherwise:
  The value of the Target Wake Time field if present, otherwise:
  The TBTT of the Beacon in which the TWT Time Slot Bitmap appears

## Slide 16: Time Slot Bitmap Description OpA
Option a) 3 bits per time slot:
  000 = occupied SU UP
  001 = occupied SU Down
  010 = occupied SU Up and Down
  011 = Unallocated slot (i.e. unoccupied)
  100 = occupied MU UP
  101 = occupied MU Down
  110 = occupied MU Up and Down
  111 = PAD (i.e. not a valid slot)
    I.e. 111 is used at the end of the bitmap to pad to a whole octet, if needed
    Any remaining bits would also be set to 1

## Slide 17: Time Slot Bitmap Description More Options
Option b) 1 bit per time slot:
  0 = not occupied
  1 = occupied
  First invalid slot is marked with 0, all slots after first invalid slot are marked with 1
    Implies that minimum number of bits in the bitmap is equal to the number of bits required for slot signaling + 2
Option c) 2 bits per time slot:
  00 = Unallocated slot
  01 = occupied SU
  10 = occupied MU
  11 = not a valid slot (i.e. PAD)

## Slide 18: TX TSF Field
Contains TSF value at time of transmission of the MPDU containing the TWT IE
  Present only when TX TSF Present = 1

## Slide 19: Broadcast TWT SP Example
Using option b:
AP transmits TWT IE with Broadcast setting inside of a Beacon
TWT IE includes the TWT Time Slot bitmap with resolution equal to 2 TU
Broadcast TWT SP Start Times are indicated by the 0 to 1 transitions in the bitmap
Broadcast TWT SP durations are indicated by the uninterrupted sequences of ones in the bitmap

## Slide 20: Time Slot Bitmap Length
Bitmap is variable length
  Length indicated in Time Slot Bitmap Length field
    As number of octets, i.e. up to 255
  Bitmap is rounded up to nearest whole octet
  Bitmap is padded as needed as indicated in bitmap description
    For the single bit per slot case, the bitmap must end with a pad in order to definitively differentiate pad vs non-pad information
    Ending pad must be at least one zero followed by one one
    Additional one bits can follow the initial pad, as needed in order to reach the next octet boundary
    Multi-bit per slot options include specific pad values
      If the identified octet length ends without a pad, any non-complete slot indication is by definition, pad

## Slide 21: Periodicity of Time Slot Bitmap Information
All Time Slot Bitmaps are periodic
  A Time Slot Bitmap repeats with periodicity determined by Number of Active Slots in the bitmap times the resolution of the bitmap slot
  Does not necessarily match the Beacon Interval or an integer multiple of the Beacon Interval or an integer division of the Beacon Interval
  Hence the need for the zeroth slot time reference

## Slide 22: Time Slot Address
Contains a 48-bit address
Optionally present
See previous slides

## Slide 23: Use of Time Slot Report (1)
Used by AP to indicate allocated Time Slots in the BSS
  Requesting STAs can avoid these time slots (or not)
  AP can assign STA anyway, in order to encourage MU use
  Non-requesting STA know to avoid these time slots
    i.e. perform EDCA outside of occupied time slots
    Optionally operate with modified EDCA parameters within occupied time slots, as dictated by the AP
  AP can send unsolicited Time Slot Report, unicast or broadcast
Used by AP and by non-AP STA
  To inform associated AP of OBSS time slot use
  To inform OBSS of this BSS time slot use
  To assist in channel use coordination

## Slide 24: Use of Time Slot Report (2)
AP and non-AP STA can send Time Slot reports
  Showing all occupied slots for the BSS
  Showing all occupied slots for another BSS
  Showing only occupied slots for a single STA
  Unsolicited
  Solicited by associated STA
  Solicited by unassociated STA

## Slide 25: TWT Time Slot Bitmap Periodicity
Periodicity is specified in TWT IE Implicit bit
  Implicit = 0 => not periodic
    When not periodic, then Broadcast Triggered TWT SP applies only to the current Beacon Interval
    Zero time reference should be signaled as the TBTT
  Implicit = 1 => periodic
    Applies until canceled with “reject” command
      In unsolicited Broadcast TWT IE
      Could create advance notification signaling mechanism
    Zero time reference as indicated

## Slide 26: Straw Poll 1
Do you support to include an option for a Time Slot Bitmap within the TWT IE?
  Yes
  No
  Abstain

## Slide 27: TWT Bitmap Information IE
Within a Beacon, the TWT Bitmap Information field can be included within a Broadcast TWT IE
TWT Bitmap Information IE should be available for individual Bitmap-based TWT negotiation
  I.e. TWT Bitmap Information fields can be conveyed outside of Beacon
  E.g. for TWT bitmap time slot request/assignment/report
  Reduces overhead vs using TWT Setup frame
  I.e. eliminates many TWT IE fields

## Slide 28: TWT Time Slot Info IE
TWT Time Slot Info can be sent as a report
  E.g. to inform OBSS of time slot utilization in this BSS
Need an element that does not include other TWT fields
 | Element ID | Element ID Extension | Element Length | TWT Time Slot Bitmap Length | TWT Time Slot Control | TWT Time Slot Bitmap | TWT Bitmap Address | TX TSF | Zero Slot Alignment
Octets: | 1 | 1 | 1 | 1 | 3 | variable | 0 or 6 | 0 or 8 | 0 or 8

## Slide 29: Straw Poll 2
Do you support to create a new element for conveyance of the TWT Bitmap Information fields?
  Yes
  No
  Abstain

## Slide 30: New Action Frame
To send TWT Bitmap

## Slide 31: Straw Poll 3
Do you support to include a new Action frame for conveyance of the TWT Bitmap IE?
  Yes
  No
  Abstain

## Slide 32: Bits to Indicate Support
TWT support mandatory at the AP
  AP must accept at least one Individual Implicit TWT request
Interpretation of Broadcast TWT mandatory at non-AP STA
  Including TWT TIM Bitmap
  Including TWT Slot Bitmap
Bits to indicate the support of these features within Extended Capabilities IE

## Slide 33: Straw Poll 4
Do you support the proposed signaling of various TWT options as described for the Extended Capability IE?
  Yes
  No
  Abstain

## Slide 34: Unsignaled PS Wake
STA with TWT SP agreement promise to be awake at TWT SP times
  i.e. no trigger frame needed by AP
    Wake state is assumed at appropriate time
  i.e. no PS-Poll frame needed by AP
    Wake state is assumed at appropriate time

## Slide 35: Straw Poll 5
Do you support to have an unsignaled PS Wake mode for TWT STA?
  Yes
  No
  Abstain

## Slide 36: References
[1] 802.11-2016.pdf
[2] Draft P802.11ax_D1.0.pdf