## Slide 1: Mandated Response MCS
Date: 2017-01-16
Authors:

## Slide 2: Abstract
Desire to have transmitter dictate response MCS
  Because the link can be asymmetric due to TX power:
    a) e.g. mobile devices have lower TX power
    b) different modulation can have different TX power
  If response rate is higher than reverse link can support, then response frame gets lost at transmitter side and causes retransmission (packet loss and/or data rate drops)

## Slide 3: CID 8099
Due to power differences and other considerations, a situation can arise when the transmitter of a response frame using the standard required response MCS value is employing an MCS that will not work for the link because of the asymmetry, e.g. tx power asymmetry. Allow a STA to dictate the response PPDU MCS to avoid this problem. | Allow the transmitter of a response eliciting MPDU to include an indication of an appropriate MCS for the response MPDU. Expect a submission detailing some changes.

## Slide 4: New A-control ID
Table 9-18a – Control ID subfield values
Add a new A-control field value
Control ID value | Meaning | Length of the Control Information subfield (bits) | Content of the Control Information subfield
0 | UL MU response scheduling | 26 | See 9.2.4.6.4.2 (UL MU response scheduling)
1 | Operating Mode(#2209) | 16 | See 9.2.4.6.4.3 (Operating Mode(#2209))
2 | HE link adaptation | TBD | See 9.2.4.6.4.4 (HE link adaptation)
3 | Buffer Status Report (BSR)(#824) | 26 | See 9.2.4.6.5 (Buffer Status Report (BSR)(#824))
4 | UL Power Headroom(#340) | 8 | See 9.2.4.6.5.1 (UL power headroom)
5 | Response MCS Index | 4 | MCS Index that is used for the frame that is a response to the frame containing this A-control field
5-15 | Reserved |  | 

## Slide 5: MCS Index Encoding
BW Independent
MCI Value | Constellation, Encoding
0 | BPSK, ½
1 | QPSK ½
2 | QPSK ¾
3 | 16QAM ½
4 | 16 QAM ¾
5 | 64QAM 2/3
6 | 64 QAM ¾
7 | 64 QAM 5/6
8 | 256 QAM ¾
9 | 256 QAM 5/6
10 | 1024 QAM ¾
11 | 1024 QAM 5/6
12 – 15 | Reserved

## Slide 6: Recipient Behavior
Recipient shall respond with acknowledgement that uses the modulation and coding specified in the A-Control field

## Slide 7: Straw Poll 1
Do you support adding a new A-control subfield ID and interpretation which includes the ability for a soliciting frame to dictate the response MCS, as outlined in the previous slides?
  Yes
  No
  Abstain

## Slide 8: References
[1] 802.11-2016.pdf
[2] Draft P802.11ax_D1.0.pdf