## Slide 1: WUR MAC and Wakeup Frame
Date: 2017-01-16
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Wakeup Frame Based on BSS Color
12-bit BSS color is long enough to avoid color collision.
AID can indicate broadcast/multicast/unicast receivers.
  AID may not needed, e.g. if multiple BSSID is not supported
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type combined AID can indicate different type of wakeup signals
  Unicast data/management frame wakeup,
  Broadcast data frame wakeup,
  Broadcast management frame wakeup or management info announcement, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
BSS Color
AID
FCS
Bits:
3
10 or 12
11
4
TBD
Payload (Optional)

## Slide 3: Wakeup Frame Based on MAC Address Option 1
Address field with the help of Type identifies the unicast/broadcast receivers:
  The unicast frame uses destination STA’s MAC address. The broadcast frame uses AP’s MAC address.
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type can indicate different type of wakeup signals
  Unicast data/management frame wakeup,
  Broadcast data frame wakeup,
  Broadcast management frame wakeup or management info announcement, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
Address
(AP MAC address)
FCS
Bits:
3
48
4
TBD
Payload (Optional)
Type
Address
(STA MAC address)
FCS
Bits:
3
48
4
TBD
Payload (Optional)
Unicast Wakeup
Broadcast Wakeup

## Slide 4: Wakeup Frame Based on MAC Address Option 2
AID can indicate broadcast/multicast/unicast receivers.
Address field indicates the AP’s MAC address.
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type can indicate different type of wakeup signals
  Unicast data frame wakeup,
  Broadcast data frame wakeup,
  Unicast management frame wakeup,
  Broadcast management frame wakeup or management info announcement, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
Address
(AID MAC address)
FCS
Bits:
3
48
4
TBD
Payload (Optional)
11
AID

## Slide 5: Wakeup Handshake and Frame Exchange
Option 1: PS-Poll or other trigger frame announces STA’s readiness after the STA receives Wakeup frame
  Option 1 is used for unicast frame transmission
LP Wakeup Req
.11PHY Header
Lower Power PPDU
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
TXOP
.11PHY Header
PS-Poll
TXOP
Option 2: AP and STA agree on the preparation period through association or other method.
  Option 2 is used for unicast or broadcast/multicast frame transmission
LP Wakeup Req
.11PHY Header
Lower Power PPDU
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
TXOP
TXOP
Preparation period

## Slide 6: EDCA for Wakeup STA
If the wakeup STAs use normal EDCA parameters to transmit PS-Poll frame, the STA may waste its energy.
The AP can defines a new EDCA parameter set for wakeup STA’s medium access whose default values have higher priority.
  The AP can broadcast the EDCA parameter set for wakeup STA’s medium access.
LP Wakeup Req
.11PHY Header
Lower Power PPDU
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
TXOP
.11PHY Header
PS-Poll
TXOP

## Slide 7: Summary
Different Wakeup frames are discussed
  Wakeup frame per BSS color (BSS identifier) is shorter; Wakeup frame per MAC address is longer.
  Wakeup frame per BSS color (BSS identifier) may not be able to uniquely identify the BSS; Wakeup frame per MAC address always uniquely identify the BSS.
  Both can support uncast/broadcast wake up,
  Both of them can support multiple BSSID.
  Both can announce data/beacon/changed BSS operation parameter/recovery BSS (start BSS)
  BSS color method seems better
Frame exchange sequence per wakeup are discussed
  Announcement method (like U-APSD).
  Non announcement method (Like S-APSD)
  Non announcement method seems better

## Slide 8: Straw Poll 2
Do you agree that in unicast frame transmission, PS-Poll or other trigger frame announces STA’s readiness after the STA receives Wakeup frame
  Yes 16
  No 1
  Abstain 34

## Slide 9: Straw Poll 1
Which in WUR Wakeup frame do you prefer to identify transmitter and receiver:
  Option 1: Identifier of transmitter and receiver which are not MAC address,
  Option 2: MAC Address
  Option 1 32
  Option 2 0
  None of them 1
  Abstain 8

## Slide 10: Straw Poll 3
Do you agree that in group-addressed frame transmission, after the preparation period agreed by AP and STAs, AP can transmit broadcast/multicast frames?
  Yes 19
  No 0
  Abstain 31

## Slide 11: Motion 1
Move to add the following text to 11ba SFD:
  The identifier of transmitter and/or receiver in a wakeup frame shall not be the MAC address.
  Mover: Liwen Chu
  Second: Po-Kai Huang
  Y:
  N:
  A:

## Slide 12: Motion 2
Move to add the following text to 11ba SFD:
  In unicast frame transmission, after a STA receives Wakeup frame addressed to it, the STA sends PS-Poll or other trigger frame to announce STA’s readiness
  Mover: Liwen Chu
  Second:
  Y:
  N:
  A:

## Slide 13: Motion 3
Move to add the following text to 11ba SFD:
  After the transmission of broadcast wakeup frame, the AP can transmit broadcast/multicast frames through primary connectivity radio after the preparation period.
  Mover: Liwen Chu
  Second: Jianhan Liu
  Y:
  N:
  A:

## Slide 14: Reference
[1] 11-16-1460-01-wur-MAC consideration