## Slide 1: Issue of Congested Primary Channel in 802.11 WLAN
Date: 2017-01-16
Authors:

## Slide 2: Abstract
This presentation:
  raises an issue of current IEEE 802.11 wireless LAN when the primary channel is congested,
  shows a possible way to overcome this issue.

## Slide 3: Background
IEEE 802.11 wireless LAN has been widely and densely deployed, and now it still needs to enhance its system capacity to accommodate a large amount of various traffic including very-large size file transfer, real-time application, and M2M/IoT application.
If the amount of traffic in a BSS increases, the channel used by the BSS becomes congested.
Moreover, IEEE 802.11 wireless LAN is sometimes exposed to interference from OBSS and/or other wireless system such as non-802.11 system (and LAA in future).
The amount of arrival interference will vary dynamically, and it may cause instantaneous heavy congestion.

## Slide 4: Issue of congested primary channel on current IEEE 802.11 wireless LAN
However, a BSS sets one primary channel on which each STA invokes the back-off procedure to transmit its data [1].
If the primary channel is congested, the STA hardly transmits its data even if other channels are vacant [2].
Since radio resources are limited, it is important to flexibly utilize temporal vacant channels to improve effective system capacity.
ch. a
ch. b
ch. c
ch. d
ch. e
ch. f
busy
idle
idle
idle
idle
idle
primary channel
Another STA cannot transmit its data if the primary channel is busy.
…
…

## Slide 5: Issue of congested primary channel on current IEEE 802.11 wireless LAN (cont.)
A BSS can change its primary channel to increase available radio resources by using the procedure of DFS or FST in several TBTTs.
However, it is not agile so as to:
  efficiently utilize temporal vacant channels,
  provide enough QoS, especially for real-time data traffic.
ch. a
ch. b
ch. c
ch. d
ch. e
ch. f
busy
idle
idle
idle
idle
idle
primary channel
Another STA cannot transmit its data if the primary channel is busy.
…
…

## Slide 6: To overcome this issue
Available radio resources will be increased if transmission opportunity can be
obtained from another channel.
One or more vacant channels may continuously or temporarily exist in the same frequency band with the primary channel or in another frequency band.
If a STA can instantly obtain transmission opportunity from such vacant channels even when the primary channel is congested, the amount of available radio resource and effective system capacity would be increased.
ch. a
ch. b
ch. c
ch. d
ch. e
ch. f
busy
idle
idle
idle
idle
idle
primary channel
…
…

## Slide 7: Summary
In IEEE 802.11 wireless LAN, a BSS sets one primary channel on which each STA invokes the back-off procedure
If the primary channel is congested, the STA hardly transmits its data even if other channels are vacant.
This issue would be overcome if a STA could quickly obtain enough transmission opportunity from such a vacant channel. This would lead to increase the amount of available radio resources and effective system capacity.

## Slide 8: Straw Poll
Do you think that IEEE 802.11 wireless LAN should have a new way to overcome the situation that the primary channel is heavily congested?
  Y:
  N:
  A:

## Slide 9: References
[1] IEEE 802.11-2012.
[2] doc. IEEE 802.11-14/1437r1.