## Slide 1: 802.11az Negotiation
Date: 2017-01-16
Authors:

## Slide 2: Motivation/Background
Develop next level of details for the Negotiation Phase of the 802.11az Protocol
  Based on discussions in document 16/1394 which outlines a 3-step .11az protocol
  This presentation is on the second step which is Negotiation
  Some of the details in this presentation will be refined iteratively as the details of the third step, Ranging/Measurement develop
  The main focus of this presentation is to get a high level agreement on how best to represent the parameters that need to be negotiated in order to efficiently do the ranging/measurement step

## Slide 3: Terminology
  Responder and Initiator
    FTM – Initiator sends iFTMR and Responder sends FTM
    Responder provides its LCI/Location Civic information
    Initiator estimates Range/Position
  Capabilities (should this apply to all ranging protocols)
    FTM Responder – the device can play the role of a responder for all supported ranging protocols – indicated by setting bit-70 of the Extended Capabilities element
    FTM Initiator – the device can play the role of an initiator for all supported ranging protocols – indicated by setting bit-71 of the Extended Capabilities element
  Ranging Protocols – Time of Flight (ToF) measurement; may be extended for others (needs more discussion)
    REVmc D8.0 Fine Timing Measurement Prototocol (FTM)
    VHT NDP Sounding-based .11az protocol (VHTz)
    HEW NDP Sounding-based .11az protocol (HEWz)
    Ranging protocol while operating in 60 GHz (11AYz)

## Slide 4: What goes in the Beacon?
Strategy – minimal information (to prevent bloat) in the Beacon in order for Initiator(s) to determine if the AP sending the Beacon is a candidate
Propose to use these as a starting point:
  Ranging Protocol(s) Supported (e.g., VHTz, HEWz, 11AYz)
  Security (supported/not supported)
If the need for other information to be included in the Beacon becomes clear during the discussions of the Negotiation and Ranging/Measurement steps, we will revisit this.

## Slide 5: Extended Capabilities Element
 |  |  |  | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 |  |  |  | 
 |  |  |  |  |  |  | R |  |  | R | R | R | R | R | R | R | R | R | R |  |  |  | 
FTM Responder
FTM Initiator
Use the FTM Responder and FTM Initiator bits to indicator corresponding capability for any (FTM, VHTz, HEWz, etc.) Ranging protocol.
.New Bits
  VHTz Capability (describe what it means to be a VHT)
    = 1 && FTM Responder == 1 VHTz Responder
    = 1 && FTM Initiator == 1 VHTz Initiator
  HEWz Capability (what is the sounding mechanism for SU case)
    = 1 && FTM Responder == 1 HEWz Responder
    = 1 && FTM Initiator == 1 HEWz Initiator
Should we consider Responder/Initiator bits for each supported Ranging Protocol?

## Slide 6: Negotiation
From among the discovered Responders, the STA selects a subset (Rn) for negotiation
To each of the member of Rn, the STA sends an initial FTM request (iFTMR) which includes at least one of:
  A FTM Parameters element as described in REVmc D8.0 which is a set of parameters that the STA proposes to use if it executes the FTM ranging protocol with the corresponding responder,
  A NGP Parameters element which is a set of parameters that the STA proposes to use if it executes either the VHTz or the HEWz ranging protocol with the corresponding responder – NGP Parameters elements may include an optional VHTz , an optional HEWz and/or an optional 11AYz subelement(s)

## Slide 7: Negotiation (cont’d)
The initiator indicates one of the following:
  No preference for the ranging protocol (the responder selects one based on its current operating conditions)
  A preferred ranging protocol (the responder may select a different ranging protocol if it has no resources to support the preferred one)
  There is an implicit preference (operating band for a choice between 11AYz and {HEWz, VHTz and FTM}; HEWz, VHTz and FTM
The responder
  Chooses one of the ranging protocols and responds with the corresponding {FTM, NGP} parameters element in the initial FTM (in response to the initial FTM request), or
  Rejects the initial FTM request and optionally includes {FTM. NGP} parameters element indicating the parameter set that it can potentially support, if requested

## Slide 8: Initial FTM Request/Initial FTM Exchange (as specified in IEEE 802.11-2016)
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory)
Octets | 1 | 1 | 1 | variable | variable | 11
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 9: FTM Parameters Element
 | Status Indication | Value | Reserved (0) | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved (00) | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 10: .11az Negotiation: Parameters to Negotiate
Determine specific capabilities, configuration
  E.g., ASAP versus non-ASAP,, etc.
  Number of antennas
  LCI/Civic (with LCI includes offsets to individual antenna positions)
  What measurements are supported – ToF, Angular, etc
  Security – key negotiation/derivation protocols – would this be in FTM Parameters element?
  MIMO Support
Resource Allocation
  E.g., Schedule, memory
  When are results expected? (immediate/delayed depending on Initiator capabilities)
  SU or MU
  MU STA ID assignment
  SU/MU mode dynamics
Preferred Mode of Measurement Protocol execution
  E.g., Band and Channel Width to use, number of measurements in a burst, etc.
  Measurement Rate

## Slide 11: .11az Negotiation
Leverage FTM approach
  Initiator proposes, Responder approves/disapproves
  On approval by Responder, use the resulting parameters to execute the ranging protocol with the Responder
Proposed Representation
  Leave FTM Parameters element as is
  Define a new Security Parameters element that applies to all the ranging protocols proposed/approved
  Define a NGP Parameters element that includes parameters relevant to both VHTz and HEWz ranging protocols
  Do we need a schedule parameter element? Or a schedule field in the ranging protocol specific sub-element?

## Slide 12: Initial FTM Request/Initial FTM Exchange
 | Category | Public Action | Trigger+ Preference | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) (optional) | Security Parameters (optional) | NGP Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11 | <tbd> | 12
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 13: Security Parameters Element (TBD)
Applies to all ranging protocols including IEEE 802.11-2016 FTM
Define this based on proposals presented so far
  Refine as the Security Proposals become more concrete

## Slide 14: NGP Parameters Element
 | Element ID (255) | Length | Element ID Extension | NGP Parameters | VHTz specific subelement (optional) | HEWz specific subelement (optional) | 11AYz Specific subelement (optional)
Octets | 1 | 1 | 1 | 9 | <tbd> | <tbd> | 
 | Status Indication | Value | Reserved | Number of Antennas | Measurements Supported | Measurement Rate | Min Response Time
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 8
 | Max Response Time | Immediate Response Capable | Immediate Response | Reserved | Format and Bandwidth | Antenna Configuration | Reserved
bits | 8 | 4 | 1 | 5 | 6 | 4 | 12

## Slide 15: NGP Parameters element details
Number of Antennas
Measurements Supported
  ToF, AoA, AoD – Indicates support in all Ranging protocols
  If a measurement is not supported in all ranging protocols, it is disabled here, and a corresponding bit is enabled in the ranging protocol-specific sub-element
Measurement Rate
  Measurements/sec
Min Response Time
  Minimum time (TUs) to respond, reserved if Immediate Response is Enabled
Max Response Time
  Max time (TUs) to respond. Reserved if Immediate Response is Enabled
Immediate Response Capable – for each supported measurement type
  What does response meam?
Immediate Response
  Enabled/Disabled
  Reserved in Request
Antenna Configuration – Linear, Circular, etc. how to parameterize antenna configuration

## Slide 16: VHTz Specific subelement (TBD)
Measurements Supported
Immediate Response Capable

## Slide 17: HEWz Specific Subelement
Measurements Supported
Immediate Response Capable
Pre-AID assigned to the initiator
Dynamic switch between SU and MU modes Supported

## Slide 18: 11AYz Specific Subelement
<TBD>

## Slide 19: Status and Value fields (from IEEE 80211-2016)
Status: 2 bits
  0: Reserved
  1: Successful
  2: Incapable forever
  3: Incapable for the duration in Value field
Value: 6 bits
  Valid only when the Status field is set to 3
Propose to reuse these fields for the NGP Parameters element also

## Slide 20: .11az Negotiation
Initial FTM Request includes at least one of
  FTM Parameters element
  NGP Parameters element
The Trigger + Preference field (do we need to express a srt of preferences)
  Trigger set to 1
  Preference set to 0 (indicates no preference) or a value indicating the preferred Ranging Protocol
Initial FTM frame includes one of FTM, NGP Parameters element
Optionality of FTM Parameters element in iFTMR and iFTM is new in .11az
Use this exchange to pick a protocol to be used for Ranging
  In a different submission

## Slide 21: .11az Negotiation
Performed with one of more members of the subset Rn
Initial FTM Request contains:
  Trigger+Preference field describing the preferred ranging protocol
  FTM , NGP Parameters element contain proposed parameters to execute FTM, VHTz or HEWz Ranging protocols
Initial FTM frame contains
  Responder’s LCI, location civic and/or Neighbor List
  A Neighbor List from the Responder’s perspective
  Either FTM or NGP Parameters to execute the Ranging protocol chosen by the responder

## Slide 22: How does all this work? -- an example
STA discovers ranging capability of the environment (R)
  STA listens to Beacons from a set of Responders
  STA selects a subset (Rn) based on the ranging capabilities supported by each of the Responders
STA initiates Negotiation with one or more members of the set Rn
  Negotiation successfully completes with Rr (a subset of Rn)
STA executes the negotiated Ranging protocol with one or more members of Rr.
Rr ⊆ Rn ⊆ R

## Slide 23: Ranging
Once the negotiation is complete, the subset Rn is partitioned into
  A Rr which contains the set of peers with which the negotiation was successful – both the ends agreed on a set of parameters to use fot ranging
  Rn – Rr which contains the set of peers with which the negotiation failed
the range measurement protocol is executed with one of more members of the subset Rr using the parameters negotiation in the initial FTM request/initial FTM exchange
  Details in a separate submission