## Slide 1: 60GHz Additional requirements for LOS]
Date: 2017-01-15
Authors:

## Slide 2: Abstract
This presentation discusses additional functional requirements for 60GHz for dealing with the NLOS problem in location.

## Slide 3: The non Line of Sight (NLOS) issue in location
The line of sight path goes through a (human) blocker and is significantly attenuated.
A path through a reflection is much stronger.
For communication purposes, there is no problem with going through a reflection
For location purposes the reflection causes a large error in both range and direction.
  Solution – special beamforming training for LOS.

## Slide 4: Possible Solutions
Optimize beamforming for finding the LOS path:
  Change the transmit sector sweep to find the LOS path rather than the strongest path.
  Change the BRP flow to find the LOS path rather than the strongest path.
Indicate in the FTM measurement report that the receiver estimates that the measurement was performed on a non-LOS path.

## Slide 5: Additional FRD requirements
The 11az protocol shall define at least one mode in which LOS/NLOS estimation (an estimation likelihood that the measurement is performed on a LOS path) is provided as part of the measurement.
The 11az protocol shall define at least one mode in which BRP training may operate on the LOS path (rather than on the strongest path).

## Slide 6: Strawpoll
Do you agree to add the following functional requirements to the SFD:
“The 11az protocol shall define at least one mode in which LOS/NLOS estimation (an estimation likelihood that the measurement is performed on a LOS path) is provided as part of the measurement.”
“The 11az protocol shall define at least one mode in which BRP training may operate on the LOS path (rather than on the strongest path).”

## Slide 7: References