## Slide 1: EDMG-CEF Extension for SC MIMO
Date: 2017-01-17
Authors:

## Slide 2: Abstract
This presentation proposes an extension of EDMG-CEF design for SC MIMO currently defined in the SFD, [1].
The proposed extension allows accurate channel estimation in time domain for the number of spatial streams NSS greater than 2.

## Slide 3: Currently Defined EDMG-CEF
Current EDMG-CEF design:
  Allows channel estimation up to 8 spatial streams;
  It is composed of multiple repetitions of CEi subfields:
    CEi = {Gui4N, Gvi4N, -GbiN}, stream index i = 1:8;
    Gui4N = {-GbiN -GaiN GbiN -GaiN};
    Gvi4N = {-GbiN GaiN -GbiN -GaiN};
    Sequence length: N = 128, 256, 384, 512;
  The signs of the subfields CEi are selected in accordance with orthogonal matrix P definition:
  P = [+1 +1 +1 +1
  +1 -1 +1 -1
  +1 +1 -1 -1
  +1 -1 -1 +1];

## Slide 4: Problem Statement
Channel estimation in time domain combines the output of A and B branch of Golay correlator.
The channel estimation subfield CEi during time period T1 has a prefix of –GaiN sequence which is a part of EDMG-STF.
However, CEi during time intervals T2, T3, and T4 has prefix of ±GbiN. Assuming that Gui4N starts with -GbiN sequences, this causes 2 Gb sequences following each other.
This leads to the inaccuracy for channel estimation in time domain.

## Slide 5: Problem Statement
Figures below show a result of matched filtering and Ga/Gb combining for two sequences, N = 128:
  - Case #1: {-GaiN, Gui4N} = {-GaiN -GbiN -GaiN GbiN -GaiN};
  - Case #2: {-GbiN, Gui4N} = {-GbiN -GbiN -GaiN GbiN -GaiN};
  - Conclusion: absence of prefix –GaiN creates a ripple in the response, which in turn leads to inaccuracy in CIR estimation;
Case #1 response
Case #2 response

## Slide 6: Proposed Changes
To solve a problem the EDMG-CEF is modified as shown in figure below:
  - Starting from time interval T2, modified CE’i is introduced as follows:
  - CE’i = {-GaiN, Gui4N, Gvi4N, -GbiN}, stream index i = 1:8;
  - Prefix -GaiN solves the issue;
Intel Corporation
Slide 6

## Slide 7: SP/M
Do you agree to apply cyclic extension of EDMG-CEF filed as defined on slide #6?

## Slide 8: References
1. 11-15-1358-11-00ay-11ay Spec Framework