## Slide 1: TG ax DSC derived CCAeff and OBSS_PD
Date: 2017-02
Authors:

## Slide 2: Background
16/1064 and 16/1567 proposed a unified approach to optionally use DSC to derive the OBSS_PD but it did allow DSC to be used independently.
16/0947r21 introduces SRG and NON SRG PD

## Slide 3: Background to DSC and PD
Originally DSC was proposed as an independent spatial reuse scheme.
OBSS-PD and now SRG and NON-SRG PD use recognition of inter-BSS and hard couple TPC to a relaxation in PD
There is no description of any method to set PD values
DSC represents a viable method for setting PD values
  Allows simulations and a standardized method

## Slide 4: Amended Proposal for DSC and PD
The amended proposal is that
“DSC procedures shall only be used by an HE STA to set OBSS_PD, NON SRG PD, and SRG PD levels, but an HE STA may set PD levels using non-DSC procedures.”
i.e. DSC derived CCAeff, can ONLY be used for OBSS_PD, SRG PD and NON SRG PD but an HE STA may choose another scheme.
DSC cannot be used independently.
Text in 16/1063r9 has the associated text.

## Slide 5: DSC or DPD?
I have heard that there may be some concern with the term “Dynamic Sensitivity Control , DSC”
  This was original term used in 2013 and is well known.
Alternative term “Dynamic Preamble Detection, DPD”
May I ask if a preference?
DSC?
DPD?

## Slide 6: Straw Poll
Do you agree that:
DSC procedures may be used to set the PD levels for OBSS_PD, NON SRG PD, and SRG PD ?
AND
DSC procedures shall only be used by an HE STA to set OBSS_PD, NON SRG PD, and SRG PD levels, but an HE STA may set PD levels using non-DSC procedures.
Y
N
A

## Slide 7: Motion
Incorporate text in 16/1063r10 into the 11ax Draft.
Addressing comments 5203, 5204, 5205, 5483, 5494, 5495, 5503, 5691, 6761, 6762, 6768, 7122, 7123, 7129, 7230, 7405, 8725, 9540, 9947, 10031, 10033
Y
N
A