## Slide 1: MIMO Coding for SC PHY in 11ay
Date: 2017-02-13
Authors:

## Slide 2: Introduction
This presentation describes MIMO coding scheme for SC PHY in 11ay.

## Slide 3: MIMO Coding Defined in D0.1
Current status of MIMO coding definition in D0.1:
  Spec draft adopts independent MCS selection per spatial stream for 1 ≤ NSS ≤ 4 and independent modulation type selection for NSS > 4, [1];
  However, D0.1 lacks an exact definition of bits distribution across the streams and bit padding scheme to make LDPC CWs and SC symbol blocks alignment in case of MIMO;
This presentation addresses the issue of bits distribution and padding to complete MIMO coding definition.

## Slide 4: Coding Steps
Similar to the SISO coding, MIMO coding includes the following steps:
  Codewords padding: to get an integer number of CWs per spatial stream, it is performed before the LDPC coding;
  Bits distribution: input scrambled bits are distributed over the spatial streams in accordance with selected MCSs;
  LDPC coding: data bits to LDPC codewords conversion by calculated parity bits;
  SC block padding: to get an integer number of SC symbol blocks per stream and align the number of SC blocks over the streams, it is performed after the LDPC coding;

## Slide 5: LDPC CWs Padding & Bits Parsing
Example of NSS = 2:
  The main idea is to perform CWs alignment and bits distribution across the streams proportionally to the modulation order (M) and LDPC encoding rate (R);
  The number of bits per stream:
    Stream #1: Nbits,1 = N * M1 * R1 * LCW;
    Stream #2: Nbits,2 = N * M2 * R2 * LCW;
  where LCW is LDPC CW length, N and NDATA_PAD are defined as follows:
  Length defines the length of PSDU in octets;

## Slide 6: LDPC CWs Padding & Bits Parsing (Cont’d)
Example of NSS = 2 (cont’d):
  M and R:
    R = {1/2, 5/8, 3/4, 13/16, 7/8};
    M = {1, 2, 4, 6};
    LCW = 672 = 16 * 42, or 1344 = 16 * 84;
  Nbits = N * (M * R * 16) * (LCW/16);
  It is proposed to perform bits distribution on a group basis with the number of bits in the group:
    Mbits = M * R * 16, where (R * 16) = {8, 10, 12, 13, 14};
  The distribution is done in a round robin manner over the streams;

## Slide 7: LDPC CWs Padding & Bits Parsing (Cont’d)
Example of NSS = 2 (cont’d):
  Figure below shows MIMO bit parsing scheme for MIMO by example of NSS = 2;
  At the output of mapper both streams have aligned number of QAM symbols;

## Slide 8: LDPC CWs Padding & Bits Parsing (Cont’d)
General formula for NSS streams:
  The number of CWs per k-th spatial stream NCW, k and the total number of padding bits NDATA_PAD can be calculated as follows:
  where ρk defines repetition factor for k-th stream;

## Slide 9: SC Symbol Blocks Padding
SC symbol blocks padding definition:
  The number of SC symbol blocks is independent on the particular spatial stream and can be calculated as follows:
  The number of padding bits per k-th stream can be calculated as follows:
  where NSPB is the number of QAM symbols per SC block transmitted over 2.16 GHz channel and NCB k defines the number of 2.16 GHz channels per k-th stream.

## Slide 10: Straw Poll
Do you agree:
  to perform input bits parsing over the spatial streams on the round robin manner with bits grouping and padding as shown on slides #8,9?
  Specification text is proposed in 11-17-0214-00-00ay 29 5 7 27 Encoding;

## Slide 11: References
Draft P802.11ay_D0.1