## Slide 1: Quasi-deterministic Model for Doppler Spread
Date: 2017-03
Authors:
Name | Affiliations | Address | Phone | email
Camillo Gentile | NIST | Gaithersburg, MD, USA | +1 (301) 975-3685 | camillo.gentile@nist.gov
Jian Wang | NIST | Gaithersburg, MD, USA | +1 (301) 975-8012 | jian.wang@nist.gov
Peter Papazian | NIST | Boulder, CO, USA | +1 (303) 497-7078 | peter.papazian@nist.gov
Jae-Kark Choi | NIST | Gaithersburg, MD, USA | +1 (301) 975-6049 | jae-kark.choi@nist.gov
Jelena Senic | NIST | Boulder, CO, USA | +1 (303) 497-6166 | jelena.senic@nist.gov

## Slide 2: Abstract
This document presents a parameterized model for Doppler spread in mmWave systems. The model is based on measurements with our 83 GHz channel sounder. The model is linked to the Quasi-deterministic (QD) propagation channel model adopted by this work group

## Slide 3: Doppler Frequency Shift
Doppler frequency shift is equivalent to the observed rate of the phase rotation at the RX
This rate is what our channel sounder can measure
RX
TX

## Slide 4: 83 GHz Channel Sounder
CHANNEL SOUNDER:
  1 omnidirectional antenna at TX
  16-element horn antenna array at RX
    Can measure AoA (azimuth and elevation)
SIGNAL CAPTURE:
  1 time sample consists of 16 measured CIRs from TX to each RX element
    Requires 65.5 µs to capture
  1 channel acquisition consists of 128 time samples with interval = 0.52 ms
    Yields maximum measurable Doppler shift of = 961.5 Hz
RX ROBOT:
  RX mounted on a mobile robot which moves around a 7 m x 7m x 6 m basement
  Total of 24 acquisitions with varying RX heading and speed collected in LOS
    Laser-guided navigational system can record RX speed and heading
    Robot accelerates to max speed of 3 km/h

## Slide 5: Ray Doppler Frequency Shift
Channel sounder extract channel rays and indexes them according to (, , )
Doppler shift of ray is a function of azimuth AoA, , w.r.t. the orientation of the RX heading
  Not a function of elevation AoA,, because RX movement only in azimuthal plane
Measured Doppler shift validated against ground-truth Doppler shift for rays extracted
  Ground-truth shift based on measured and recorded speed
Despite good match-up, sources of error between measured and ground-truth shifts:
  Measured shift bound to 128 quantized values due to finite number of time samples
  Ground-truth shift susceptible to estimation errors in
RX

## Slide 6: Doppler Frequency Spread
The MPC will have a corresponding signal spectrum scaled by and shifted by
The combination of MPCs will give rise to a Doppler spread, which creates a distorted spectrum
An estimation of the Doppler spread is useful in designing channel equalization schemes
RX
Distorted spectrum

## Slide 7: Ray Clustering
Rays in single acquisition are clustered based on Quasi-deterministic (QD) channel model*
  Each cluster is composed of a base ray and diffuse rays
  Base ray has AoA, (,
Between 5 and 8 clusters identified per acquisition
1 CHANNEL ACQUISITION
P
base ray
diffuse
rays
*“Quasi-deterministic Approach to mmWave Channel Modeling in Non-stationary Environment,” Maltsev, Pudeyev, Karls, Bolotin, Morozov, Weiler, Peter, Keusgen, Globecom 2014.
QD CLUSTER MODEL

## Slide 8: Doppler Spread Computation
RMS Doppler spread is computed from rays within cluster:
where is the mean Doppler shift of the cluster:
Because will be scaled by , in order to combine the spreads from all the clusters from the 24 acquisitions, we compute the coefficient of variation:

## Slide 9: Quasi-deterministic K-factor
K-factor of QD model* measures the relative strength of the base ray w.r.t. the diffuse rays
Clusters with high K-factors have narrower spread because the diffuse rays are much weaker compared to base ray
Cluster with low K-factors have wider spread because the diffuse rays are comparable in strength to base ray
Measured
Model
P
base ray
diffuse
rays

## Slide 10: Doppler Spread Model
Plot of CDFs of measured vs. CDFs of model show good match-up
*“Quasi-deterministic Model for Doppler Spread in Millimeter-wave Communication Systems,” J. Wang, C. Gentile, P.B. Papazian, J.-K. Choi, J. Senic, Submitted to IEEE Antennas and Wireless Propagation Letters.
Measured coefficient of variation
From measurements to model
From measurements to model
Complete Doppler model
From paper*