## Slide 1: Further Evaluations on Single Carrier Waveforms
Date: 2017-03-01
Authors:

## Slide 2: Abstract
In [1] and [2], we introduced a DFT-spread operation to 802.11ay and evaluated the throughput performance in comparison to the ones with OFDM and SC waveforms
In this contribution,
  We provide more clarifications on the receiver structures for SC waveforms in [2]
  We discuss why SC receivers degrades the PER performance
  Additional simulation results are also provided

## Slide 3: Background (1/2)
In 802.11ad [3], both OFDM and SC waveforms are adopted and similar waveforms are expected to be adopted for 802.11ay [4]
In 802.11ad, the numerologies for SC and OFDM are chosen such that both SC and OFDM can operate at the same nominal sample rate
The nominal sample rate for a single channel is 2.64 GHz

## Slide 4: Background (2/2)
RF
DAC
802.11ad OFDM TX and RX do not need to employ extra upsampling and downsampling operations [3]
On the other hand, a typical SC TX and RX for 802.11ay/ad may employ an upsampling, filtering, and a downsampling operations to match the sampling rate
SC receiver operates on a block where the channel’s impact is a circular convolution to exploit 1-tap freq. domain equalization
IDFT
(512)
P
/
S
M
a
p
Pilot
Data
336
16
0
DFT
(512)
S
/
P
Data
0
EQ
352
GI
Data
P
/
S
3
2
Filter
448
64
S
/
P
2
3
Filter
EQ
DFT
(512)
IDFT
(512)
Data
448
64
GI
RF
ADC
RF
DAC
RF
DAC
OFDM TX and RX:
SC TX and RX:

## Slide 5: Equivalent Representation of SC (1/2)
Upsampling, filtering, and downsampling operations for single carrier can expressed in frequency. For example, the equivalent operations for single channel are given as follows:
  Upsampling: DFT of 768, repeat in frequency, IDFT of 1536 [7, p238]
  Downsampling: DFT of 1536, combine in frequency, IDFT of 512 [7, p235]
  Filtering: Windowing in frequency domain (corresponds to 1536 filter coefficients)
S
/
P
2
3
Filter
EQ
DFT
(512)
IDFT
(512)
Data
448
64
GI
DFT
(768)
Weighted Comb.
DFT
(768)
IDFT
()
DFT
()
IDFT
(512)
Filter coef.
DFT
(512)
Cancels each other
Filter
coef.
512
SC receiver
Cancels each other
Filter coef.
Output of DFT
Output of DFT
768
768

## Slide 6: Equivalent Representation of SC (2/2)
The equivalent frequency domain representation of 11ay/ad SC receiver includes for single channel
  A 768-DFT operation in front and a weighted combination before the equalization
This receiver is optimal in AWGN with a matched filter
However, one can show that this receiver is suboptimal in fading channel
Filter coef.
Output of DFT
Output of DFT
Non-coherent additions before equalization!
DFT
(768)
EQ
IDFT
(512)
Data
448
64
RS
Weighted Comb.
S
/
P
2
3
Filter
EQ
DFT
(512)
IDFT
(512)
Data
448
64
RS
SC receiver
Channel frequency response
Complex coefficients
frequency
Amplitude

## Slide 7: Simulation Assumptions
Waveforms: OFDM, SC, DFT-spread OFDM, and DFT-spread Windowed OFDM (see Appendix I)
Channel: 11ay channel model, conference room, STA-AP [5]
  The location of the STA and the rotation of the PAA around vertical axis are chosen randomly. For each drop, the boresight of the STA and AP antenna patterns are aligned on LoS
  Vertical polarization, LoS path exists
  Antenna: PAA @ AP, PAA @ STA
Numerology:
  The 8 GHz numerology for OFDM and SC is obtained based on 802.11ad [2]
  The numerology for DFT-spread OFDM is obtained based on OFDM [2]
Equalization: Single tap MMSE-FDE, CHEST: Ideal, Coding Rate: ½ and 13/16
Impairments: Rapp model [6] for power amplifier (PA), 6 dB OBO for all waveforms
Fixed location
and orientation
PAA
AP
Random location
and orientation
PAA
STA

## Slide 8: BER Results without PA Impairment
a) AWGN
b) 11ay channel
SC receiver performs
~ 1 dB worse than others in the channel
In AWGN, all waveforms are aligned with Gaussian BER bound
In fading channel, conventional SC receiver degrades BER performance approximately 1 dB due to aforementioned non-coherent combinations

## Slide 9: BER Results with PA Impairment
a) AWGN
b) 11ay channel
SC is ~1dB better than OFDM
In AWGN, SC and DFT-spread OFDM outperform OFDM due to their low PAPRs
In 11ay channel, SC receiver does not capture the PAPR advantage as compared to DFT-spread OFDM for low SNR
SC receiver loses its PAPR advantage for low SNR
1 dB

## Slide 10: PER Results in 11ay Channel
~1 dB
~0.8 dB
With or without PA impairment, the SC receiver is ~1 dB worse than DFT-spread OFDM
With PA impairment, both SC and OFDM are ~0.8 dB worse than DFT-spread OFDM for 13/16 coding rate. Throughput result is provided in Appendix II
The results for ½ coding rate is provided in Appendix III and IV
a) Without PA impairment (13/16 coding rate)
b) With PA impairment (13/16 coding rate)

## Slide 11: Conclusion
In this contribution, we discuss the upsampling-filtering downsampling operation at the SC receiver
We showed that the upsampling-filtering downsampling operation at the SC receiver is equivalent to a weighted combination in frequency domain, which is not optimal in fading channel
Simulations show that
  The SC receiver degrades the FER performance as compared to DFT-spread OFDM
  With high coding rate and PA impairments, DFT-spread OFDM is superior to OFDM

## Slide 12: References
[1] “On the Single Carrier Waveforms for 11ay”, IEEE 802.11-16/01455r0
[2] “Performance Evaluation of Multi-DFT-spread OFDM for 802.11ay ”, IEEE 802.11-17/00048r0
[3] “Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band,” IEEE Std 802.11ad-2012, pp. 1–628, Dec. 2012.
[4] “Specification Framework for TGay,” IEEE 802.11-15/01358r6]
[5] “Channel Models for IEEE 802.11ay,” IEEE 802.11-15/1150r7
[6] “11ay evaluation methodology,” IEEE 802.11-16/866r4
[7] K. R. Rao at al., “Fast Fourier Transform - Algorithms and Applications”, Signals and Communication Tech., Springer, 2010

## Slide 13: Appendix I - Waveforms
RF
DAC
IDFT
(2048)
P
/
S
M
a
p
Pilot
Data
336x4
16x4
0
DFT
(2048)
S
/
P
Data
0
EQ
352x4
GI
Data
P
/
S
3
2
RRC
448x4
64x4
S
/
P
2
3
RRC
EQ
DFT
(2048)
IDFT
(2048)
Data
448x4
RF
ADC
RF
DAC
RF
ADC
OFDM
SC
RF
DAC
IDFT
(2048)
P
/
S
DFT
GI
Data
299x4
53x4
0
DFT
(2048)
S
/
P
Data
0
EQ
352x4
RF
ADC
DFT-S-OFDM *
IDFT
RF
DAC
IDFT
(2048)
P
/
S
DFT
GI
Data
299x4
53x4
0
DFT-S-W-OFDM *
Window
DFT
(2048)
S
/
P
Data
0
Amplitude EQ
RF
ADC
IDFT
Weighted Comb.
Phase EQ
CP+
256
CP-
256
*Numerology is selected such that it has the same throughput of SC and OFDM approximately

## Slide 14: Appendix II - Throughput Results in 11ay Channel (16QAM, 13/16)
a) Without PA impairment (13/16 coding rate)
b) With PA impairment (13/16 coding rate)
~1 dB
~0.8 dB

## Slide 15: Appendix III - PER Results in 11ay Channel (16QAM, 1/2)
~1 dB
~0.9 dB
a) Without PA impairment (½ coding rate)
b) With PA impairment (½ coding rate)

## Slide 16: Appendix IV - Throughput Results in 11ay Channel (16QAM, 1/2)
a) Without PA impairment (½ coding rate)
b) With PA impairment (½ coding rate)
~1 dB
~0.9 dB