## Slide 1: Training Protocols for DL MU-MIMO in 802.11ay
Date:
Authors:

## Slide 2: Introduction
DL MU-MIMO is included in 11ay
An essential part of DL MU-MIMO operation is the obtaining of channel information (at the AP) for proper user pairing and digital precoding
Depending on the scenario, UL training may be more efficient (lower overhead etc.) than explicit (DL) training
  And vice versa
  Other 5G communities are adopting UL training for mmWave

## Slide 3: Introduction
In this presentation, we will present different training mechanisms
  In principle, one is DL based and the other UL based
  The methods are based on principles from 11ad/ay
  Feedback is appreciated - How do we proceed?

## Slide 4: Hardware Model
AP
…
antennas
…
RF chains
STA
…
antennas
…
RF chains
We consider a hybrid scenario (not fully digital)
Due to this, one needs to find good analog beams (SLS, BRP, etc.) before doing any digital precoding
The proposed UL training mechanism is useful for the digital precoding

## Slide 5: Example Scenario
In our presentation, we will (for simplicity) assume that
  AP has 2 RF chains
  Each STA has 1 RF chain

## Slide 6: Envisioned DL Training Mechanisms With Link Setup

## Slide 7: Envisioned DL training with link setup
STA
RF
Step 1 (SLS): Find best transmit and receive beams (with TRN-R) for MU-MIMO STAs
RF
AP
TRN-R
TRN-R
TRN-R
TRN-R
RF
1
2
3
4
STA
RF

## Slide 8: Envisioned DL training with link setup
Step 2: Each STA feedbacks best transmit direction (along its best TRN-R beam, assuming reciprocity [1]) via scheduling during step 1
STA
RF
2
RF
AP
RF
STA
RF
3

## Slide 9: Envisioned DL training with link setup
Step 2: Omni reception at AP could be replaced by directional reception, as introduced in [1]
STA
RF
RF
AP
RF
STA
RF
1
1
2
2
3
3
4
4

## Slide 10: Envisioned DL training with link setup
Step 3: AP transmits DL training packet in each reported direction
2
RF
AP
RF
TRN-TR
STA
RF
STA
RF
CSI
3
TRN-TR
CSI
2
3

## Slide 11: Envisioned DL training with link setup
Step 3: AP transmits DL training packet (or several training packets) in one joint direction and polls for CSI
2&3
RF
AP
RF
TRN-TR
STA
RF
STA
RF
CSI
CSI
Poll
2
Poll
3

## Slide 12: Envisioned DL training with link setup
Step 3: AP transmits DL training packet (or several training packets) in one direction and awaits CSI according to scheduling during step 1
2&3
RF
AP
RF
TRN-TR
STA
RF
STA
RF
CSI
CSI
2
3

## Slide 13: Envisioned UL Training With Link Setup

## Slide 14: Envisioned UL training with link setup
STA
RF
Step 1 (SLS): Find best transmit and receive beams (with TRN-R) for MU-MIMO STAs
RF
AP
TRN-R
TRN-R
TRN-R
TRN-R
RF
1
2
3
4
STA
RF

## Slide 15: Envisioned UL training with link setup
Step 2: Each STA feedbacks best transmit direction (along its best TRN-R beam, assuming reciprocity [1]) via scheduling during step 1
STA
RF
2
RF
AP
RF
STA
RF
3

## Slide 16: Envisioned UL training with link setup
Step 2: Omni reception at AP could be replaced by directional reception, as introduced in [1]
STA
RF
RF
AP
RF
STA
RF
1
1
2
2
3
3
4
4

## Slide 17: Envisioned UL training with link setup
Step 3: AP polls each STA to transmit training packet
RF
AP
RF
STA
RF
STA
RF
Poll
2
2
Poll
3
3

## Slide 18: Envisioned UL training with link setup
Step 3: AP transmits a joint poll (or several polls), acting as a trigger frame, that schedules all STAs
RF
AP
RF
STA
RF
STA
RF
Poll
2&3
2
3

## Slide 19: Envisioned UL training without BRP
Step 3: No polling due to scheduling during step 1 (SLS)
RF
AP
RF
STA
RF
STA
RF
2
3

## Slide 20: Envisioned Training Without Link Setup

## Slide 21: Envisioned DL training with BRP
AP transmits DL training packet in one direction
  Polling could be replaced by scheduling
2&3
RF
AP
RF
TRN-TR
STA
RF
STA
RF
CSI
CSI
Poll
2
Poll
3

## Slide 22: Envisioned UL training without BRP
Step 3: AP transmits a joint poll (or several joint polls), acting as a trigger frame, that schedules all STAs
RF
AP
RF
STA
RF
STA
RF
Poll
2&3
2
3

## Slide 23: Benefits of UL Training
Significantly less training overhead (for same channel information) in many scenarios
  Faster access to CSI estimates => more time for data transmission
Requires no CSI feedback and quantization
  The AP directly estimates digital CEF (no STA feedback needed)

## Slide 24: Reflections
Thoughts on the presented mechanisms?
Do you support including some of the mechanisms into the 11ay SFD?
  If so, which ones?

## Slide 25: References
[1] IEEE 802.11-17/0067r1