## Slide 1: BSS Load Information Element for 11ax
Date: 2017-03-15
Authors:

## Slide 2: 11ax D1.0 CID of BSS Load
CID | Commenter | P.L | Clause | Comment | Proposed Change
5917 | James Yee | 67.01 | 9.4.2.139 | With the introduction of new features such as OFDMA and UL MU MIMO, the existing BSS load elements (9.4.2.160 & 9.4.2.28), which address STA numbers, primary/secondary channel busy condition and DL MU-MIMO underutilization (11ac) are not sufficient for addressing the BSS load status in a 11ax BSS. A further enhanced BSS Load element needs to be defined. | Add a new information element to define 11ax BSS Load. The new IE shall address utilization status of OFDMA as well as UL/DL MU MIMO, as well as provisions to allow future extensions.
8165 | Ming Gan | 67.01 | 9.4.2. | BSS load element provides the channel utilization such that the unassociated STA can choose the proper AP┤+ε and extended BSS load element further provides the the spatial stream underutilization given the busy channel such that unassociated STA with MU-MIMO capability can choose the proper AP. Now 11ax introduce a OFDMA, there is the probability of frequence underutilization given the busy channel. | Define a HE BSS load element considering frequency utilization such to help unassociated STA to choose a best AP

## Slide 3: Summary
802.11 defines two BSS load information elements[1] containing
  information of current STA population and traffic level in the BSS (BSS load element)
  information of MIMO spatial stream underutilization and bandwidth utilization (Extended BSS load element)
11ax introduces MU of OFDMA and UL MIMO, but current BSS load IEs cannot reflect true loading of 11ax HE BSSs
In this presentation, we propose defining new information element contents for conveying HE BSS load information. These contents can be carried either in a new element or in the extension of the legacy BSS load element.

## Slide 4: 11ax MU BSS Load
Propose to define IE contents containing three categories of information
  11ax MU capable STA count and active STA counts
  TXOP time percentages over an observation period
  Load Report: Underutilization rate of MU TXOP to reflect potential capacity of an 11ax BSS

## Slide 5: 11ax MU BSS Load Element Contents(1/4)
STA count
Total number of MU capable STAs
  MU includes MU MIMO and OFDMA
  Let STAs know how many MU competitors are within the BSS
Active STA counts
  Some associated STA may not be active for a long time
  AP can monitor STA’s activities during an observation period
    Propose to define independent observation periods in units of beacon intervals
  An active STA: if the AP receives any MPDU from that STA during the observation period.
  Two active STA counts are proposed.
    Active STA count
    Active MU capable STA count

## Slide 6: 11ax MU BSS Load Element Contents(2/4)
Usage Example:
  Example: HE BSS1 has 100 active STAs with 5 active MU capable STAs, and HE BSS2 has 100 active STAs with 95 active MU capable STAs. An unassociated HE STA may choose HE BSS2 for more transmit and receive opportunities

## Slide 7: 11ax MU BSS Load Element Contents(3/4)
2. MU/SU TXOPs Time percentages
  Let STAs know the traffic trend of TXOPs during the observation period. STA may have specific UL/DL requirements. The report includes
    Observation period in units of beacon intervals: the time interval AP making the measurement most recently
    MU: Report UL and DL separately
    SU: Report DL
  Usage Example:
    High percentage UL TXOP means heavily MU UL loaded BSS
  Illustration

## Slide 8: 11ax MU BSS Load Element Contents(4/4)
3. Load report of MU TXOPs
  Underutilization percentage over space & frequency
    Information of available BW and SS
      Interfered and used RUs shall not be included
    Separate DL & UL reports
    Report of channel BW
    Reports of per 20 MHz BW
  Underutilization percentage formula (MU DL example)
Nmax_SS: Max supported spatial stream
RUBusy: Occupied RU weight(Used or interfered)
RUmax: RU weight of the available BW
TBusy(MUDL): Time of busy period for MU DL (MU DL TXOP)

## Slide 9: UL and DL Separation
For underutilization and TXOP percentage reports, we propose to separate UL and DL
  11ax adds UL MU MIMO as the key feature
  11ax uses trigger frames to initiate MU UL and DL transmission. AP in general controls MU UL and DL traffic. Precise statistics is available.
  STA needs specific UL/DL information according to their transmission requirement

## Slide 10: 11ax MU BSS Load Information Element Contents (1/2)
For UL/DL underutilization
  Variable length dependent on the channel bandwidth
Optional subelements carry active STA counts and legacy BSS load IEs (defined on the next page)

## Slide 11: 11ax MU BSS Load Information Element Contents (2/2)
Subelements
  Optional active STA counts
  Able to carry legacy BSS load elements
    BSS load (9.4.2.28)
    Extended BSS load (9.4.2.160)
Active STA count subelements
Subelement ID | Name | Extensible
0 | Reserved | 
1 | Active STA count | Yes
2 | Active MU capable STA count | Yes
3 | BSS load | 
4 | Extended BSS load | 
5-255 | Reserved | 
 | Subelement ID | Length | Active STA count | Observation period in units of beacon interval s
Octets: | 1 | 1 | 2 | 1
 | Subelement ID | Length | Active MU Capable STA count | Observation period in units of beacon intervals
Octets: | 1 | 1 | 2 | 1

## Slide 12: Straw poll 1
Do you support to define the 11ax BSS load content either in a new BSS load element or in the extension of the legacy BSS load element
  Y
  N
  A

## Slide 13: Straw poll 2
Do you support to add the MU capable STA count to the 11ax BSS load content?
  Y
  N
  A

## Slide 14: Straw poll 3
Do you support to separately report underutilization rates of DL and UL in the 11ax BSS load content?
  Y
  N
  A

## Slide 15: Straw poll 4
Do you support to add TXOP time percentages described on page 7 to the 11ax BSS content
  Y
  N
  A

## Slide 16: Straw poll 5
Do you support to add the load report described on page 8 to the 11ax BSS load content? The load report includes
    DL/UL underutilization rates per 20 MHz
    DL/UL underutilization rates of the channel bandwidth
  Y
  N
  A

## Slide 17: Straw poll 6
Do you support to add active STA counts described on page 5 to the 11ax BSS load content as optional subelements?
  Y
  N
  A

## Slide 18: Straw poll 7
Do you support to define 11ax BSS load content described on page 10
  Y
  N
  A

## Slide 19: Straw poll 8
Which format do you prefer to carry the 11ax BSS load content
  New information element
  Extension of the legacy BSS load element

## Slide 20: References
P802.11 2016

## Slide 21: backup

## Slide 22: Underutilization Percentage RU Weights
RU weights example of report per 20 MHz BW
  RU26: 1/9
  RU52: 2/9
  RU106: 4/9
  RU242: 9/9
  RU484: 9/9 (half on the target 20MHz)

## Slide 23: MU UL/DL Time Definitions
UL MU by TF
DL MU
Cascaded MU

## Slide 24: Legacy BSS Load IEs
BSS load element
Extended BSS load element

## Slide 25: dot11ChannelUtilizationBeaconIntervals
dot11ChannelUtilizationBeaconIntervals (50 beacon intervals default)
  May not transmitted by the AP
  Currently defined in Annex C