## Slide 1: WUR Negotiation and Acknowledgement Procedure Follow up
Date: 2017-03-12
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com

## Slide 2: Abstract
We have presented high-level MAC concepts for WUR in [5]
In this presentation, we follow up on the following two MAC concepts
  WUR negotiation procedure
  Wake-up packet acknowledgement procedure

## Slide 3: WUR Negotiation Procedure
As discussed in [5], to enable WUR negotiation procedure, we need to define WUR request/response and WUR Mode element carried in the WUR request/response to convey the essential information for the WUR negotiation
Similar to other negotiation procedures (e.g. WNM, ADDBA), the WUR request/response is expected to be Action frames (i.e., management frames with subtype 1101)
WUR Request
AP
STA
WUR Response
Primary Connectivity Radio Transmission

## Slide 4: WUR Action Frame
The format of WUR Action frame is shown below
  The Category field is defined in 9.4.1.11 Action field, and one code will be defined for WUR
  The WUR Action field identifies different WUR Actions
    WUR Mode Request, WUR Mode Response, etc.
  The Dialog Token field is chosen by the non-AP STA sending the WUR Mode Request frame to identify the request/response transaction
 | Category | WUR Action | Dialog Token | WUR Mode Element | Other Elements
Octets | 1 | 1 | 1 | TBD | TBD

## Slide 5: WUR Mode Element
The format of WUR Mode Element is shown below
WUR information that can be defined
  Required time for turning on the 802.11 radio of the STA for AP to know the earliest time that STA can receive through primary connectivity radio if STA receives wake-up packet
  Duty-cycle of the wake-up receiver (WURx) of the STA to further reduce power consumption
  Other TBD fields
 | Element ID | Length | WUR Information
Octets | 1 | 1 | TBD

## Slide 6: WUR Acknowledgement Procedure
As discussed in [5], the basic acknowledgement procedure for unicast wake-up packet is as follows
  After AP sends a wake-up packet to a STA, AP waits for a timeout interval
    If AP receives any packet from the STA within the timeout interval, the packet acknowledges the successful reception of the wake-up packet
    Otherwise, the wake-up packet transmission is considered to be failed, and the AP may retransmit the wake-up packet to the STA
    The timeout interval is larger than the required time for the STA to wake up the primary connectivity radio (i.e. 802.11)
  To increase reliability [5], AP may transmit more than one unicast wake-up packet successively, and the acknowledgement procedure is as follows
    If the same wake-up packet is transmitted within the existing timeout interval of the previous wake-up packet transmission, then a new timeout interval is established to replace the existing timeout interval

## Slide 7: WUR Acknowledgement Procedure
Example:
AP
STA
Wake-up Packet To STA
Timeout Interval
Transmission Fails
AP
STA
Wake-up Packet to STA
Timeout Interval
Transmission succeeds
Any Packet
AP
STA
Wake-up Packet to STA
New Timeout Interval replaces old Timeout Interval
Wake-up Packet to STA
Old Timeout Interval
No packet transmission from the STA
Primary Connectivity Radio Transmission
WUR Signal Transmission

## Slide 8: Conclusion
For the WUR negotiation procedure, we propose to
  Define WUR Action frame
  Define WUR Mode Element to carry WUR information
For the WUR acknowledgement procedure of unicast wake-up packet, we propose to
  Define timeout interval to identify wake-up packet transmission success/failure
  Enable successive wake-up packet transmission to increase reliability

## Slide 9: Straw Poll 1
Do you support the following:
  Define WUR Action frame to enable WUR negotiation

## Slide 10: Straw Poll 2
Do you support the following:
  STA can have Duty cycle mode for wake-up receiver (WURx)

## Slide 11: Straw Poll 3
Do you support the following:
  Define WUR Mode element that can carry following WUR information
    STA’s Duty cycle of wake-up receiver (WURx)

## Slide 12: Straw Poll 4
Do you support the following acknowledgment procedure for unicast wake-up packet
  After AP sends a wake-up packet to a STA, AP waits for a timeout interval
    If AP receives any transmission from the STA within the timeout interval, then the wake-up packet transmission is successful
    Otherwise, the wake-up packet transmission fails, and AP may retransmit the wake-up packet to the STA

## Slide 13: Straw Poll 5
Do you support the following for multiple unicast wake-up packet transmissions?
  If a wake-up packet is transmitted to the same intended STA within the existing timeout interval of the previous wake-up packet transmission, then a new timeout interval is established to replace the existing timeout interval
Deferred

## Slide 14: Reference
[1] 11-16-1445-00 Overall MAC Procedure for WUR
[2] 11-16-1460-01 WUR MAC Consideration
[3] 11-16-1470-00 Wake-up and Data Exchange Sequences
[4] 11-16-1504-00 Discussion of WUR Packets Design
        [5] 11-17-0071-00-00ba-high-level-mac-concept-for-wur