## Slide 1: WUR Frame Structure follow-up
Date: 2017-03-12
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Recap on [1]
A WUR frame structure to wake up the primary radio was proposed at previous F2F meeting.
  “Do you agree that a WUR PPDU follows the L-part (i.e. L-STF, L-LTF and L-SIG) as one way of protecting? (SP result: 26Y 1N 8A)”
To meet the goal of 11ba described in PAR[2], the proposed WUR frame structure was constructed with various part as following
  L-part
    For the coexistence with Legacy STA, the frame begins with L-part.
  WUR Preamble part
    It can be utilized for timing synch/ Packet detection.
  Control information part
    It could include the PHY header.

## Slide 3: Recap on [1]
Proposed WUR Frame Structure

## Slide 4: Overview
In this contribution, we discuss the raised issue for proposed WUR preamble structure and more considerations for WUR preamble.
  Existence of L-part
    The WUR preamble which includes L-part is supported as one of WUR frame format.
    We discuss more the pros and cons according to inclusion of L-part.
  Decision of threshold for Envelop detection
    According to channel status, the received signal power can be changed. So, the measurement of threshold of Envelop detection according to channel status should be considered.
  PHY Header
    We discuss the necessity of PHY header and we also consider how to configure the header.

## Slide 5: L-part on WUR preamble (1/2)
Discussion about the beginning with L-part
  By starting the WUR frame with L-part, we can achieve the targeted goal(i.e. legacy coexistence) as described in PAR.
  L-length protection can be utilized for protection of WUR transmission.
  The L-part is only for legacy STA. So, it minimizes the impact to conventional legacy STA. while, the WUR receiver does not need to decode it.
  It can increase the overhead of WUR preamble. But, this maybe trivial when it compares with the total number of symbols for WUR PPDU.

## Slide 6: L-part on WUR preamble (2/2)
Discussion about the beginning with WUR preamble without L-part
  It needs the transmission of certain control frame on primary radio to announce of WUR transmission before the transmission of WUR frame.
    for example, the CTStoSelf frame can be used for this purpose.
  It can reduce the overhead of WUR preamble itself. but the reduction of overhead may be tenuous.
  On the contrary, due to additional transmission of control frame on primary radio, it could aggravate the control/management overhead issue in the network.
  But, based on the feedback in the previous presentation, we’re open to discussion on other PPDU format (e.g. whole narrow band PPDU).

## Slide 7: Threshold for OOK symbol detection(1/2)
WUR signal can be generated by using a conventional Wi-Fi transmitter as described in [3].
Each symbol is consisted of ON signal or OFF signal for indication of one bit information (i.e. ‘0’ or ‘1’).
For the decoding of received OOK signal, WUR receiver can utilize the Envelop Detection as following
  Where,
    e(t) is envelop of received signal x(t)
    Threshold is envelop value to determine the bit information whether it is ‘0’ or ‘1’
The threshold is very important factor which determine the performance of WUR receiver.
Bit information

## Slide 8: Threshold for OOK symbol detection(2/2)
Because the envelop of WUR signal is dependent to channel status, we should apply the appropriate threshold according to receiving channel.
  Using a threshold which does not reflect a channel can incur the degradation of performance.
So, it is proper to apply the threshold which has reflected the channel status according to received channel.
For the purpose of this, we can use the symbols of WUR preamble to determine the threshold of envelop detection for received WUR signal.
  As described in [4], the symbols which are located right after the symbols for timing synchronization in WUR preamble (or including timing synchronization symbols) can be used for measuring a received signal power.
  By using the these symbols, WUR receiver can determine the threshold for distinction of bit information carried by WUR signal.

## Slide 9: WUR SIG field (1/2)
We discussed the various control information carried by control information part of WUR frame in [1].
And, we proposed that PHY header was placed at right after preamble part for early indication.
  By using a PHY header, we can potentially reduce the power of WUR receiver who is not the intended receiver (no need for PHY and MAC interaction further).
The PHY header is used for only early indication. So, it is desirable to carry the short and simple control information.
In the next slide, we discuss the content of PHY header (i.e. WUR SIG field).

## Slide 10: WUR SIG field (2/2)
WUR SIG field could include the some of following control information.
  BSS identification
    To distinguish whether the received WUR frame is from own BSS or not.
    To reduce the overhead, BSS color or partial BSS ID can be considered.
  Information for decoding of PPDU
    Mode indication
      It indicates the type of transmission mode of WUR signal
      Also, with this information, WUR receiver could know whether received WUR frame is for multi-user or for single user.
    Length
      Indication of WUR PPUD size
    Rate
      If WUR supports the various data rate, this information could be indicated by WUR SIG field.
  CRC

## Slide 11: Conclusion
We have checked the following considerations on WUR preamble.
First, we took look at pros and cons according to including or excluding of L-part in WUR preamble.
  On the whole, the exclusion of L-part does not have big advantage compare with the inclusion of L-part in WUR preamble.
  Also, the exclusion of L-part could cause the unnecessary overhead issues in the network due to additional transmission of control/management frame.
  So, we may think that the beginning with L-part in WUR PPDU is suitable to satisfy the coexistence with legacy device.
And, we also checked the advantage of using the PHY header (i.e. WUR SIG ) in WUR frame.
  It is helpful to early indication and to reduce the power of WUR receiver.
The envelop of received signal could be changed according to channel status. So, it needs to be apply the channel status suitably when WUR receiver performs the envelop detection. For the purpose of this, we could use the some of symbols in WUR preamble for measuring of threshold.

## Slide 12: Straw Poll 1
Do you agree to add the following into 11ba SFD?
  A WUR PPDU follows the L-part (L-STF, L-LTF, L-SIG) as one way of protecting.

## Slide 13: Straw Poll 2
Do you agree to add following into 11ba SFD?
  The WUR SIG field(i.e. PHY header) can be included in WUR Frame Structure.

## Slide 14: Straw Poll 3
Do you agree that a part of WUR preamble could be used for measurement of threshold that WUR receiver use for Envelop Detection ?

## Slide 15: Reference
[1] 11-17-0036r03-Consideration on WUR Frame Structure
[2] 11-16-1045r09-a par proposal for wake-up radio
[3] 11-16/0341r0 - LP-WUR (Low-Power Wake-Up Receiver) Follow-Up
[4]11-17/0030r0 – On the performance of Timing Synchronization and OOK Pulse Bandwidth