## Slide 1: BSS Load Information in 802.11ax
Date: 2017-05-01
Authors:
Name | Affiliation | Address | Phone | Email
Ming Gan | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-15914117462 | david.yangxun@huawei.com
Ming Gan et al. (Huawei)

## Slide 2: Load Balancing Problem
STAs normally prefer to access best AP with strongest received power.
In 802.11ax, there will be a large number of STAs and traffic in dense scenarios. Some AP may be associated with too many STAs and/or over-loaded.
  If STAs choose the busy AP, they have less opportunity of scheduled transmission.
 Load unbalancing problem is getting more serious in 802.11ax dense scenarios.

## Slide 3: Comments on Loading Balancing Problem
CID | P.L | Clause | Comment | Proposed Change
5917 | 67.01 | 9.4.2 | With the introduction of new features such as OFDMA and UL MU MIMO, the existing BSS load elements (9.4.2.160 & 9.4.2.28), which address STA numbers, primary/secondary channel busy condition and DL MU-MIMO underutilization (11ac) are not sufficient for addressing the BSS load status in a 11ax BSS. A further enhanced BSS Load element needs to be defined. | Add a new information element to define 11ax BSS Load. The new IE shall address utilization status of OFDMA as well as UL/DL MU MIMO, as well as provisions to allow future extensions.
8165 | 67.01 | 9.4.2 | BSS load element provides the channel utilization such that the unassociated STA can choose the proper AP┤+ε and extended BSS load element further provides the spatial stream underutilization given the busy channel such that unassociated STA with MU-MIMO capability can choose the proper AP. Now 11ax introduce a OFDMA, there is the probability of frequency underutilization given the busy channel. | Define a HE BSS load element considering frequency utilization such to help unassociated STA to choose a best AP

## Slide 4: BSS load information in 802.11ac
In 802.11ac, MU-MIMO spatial stream underutilization have been considered in the ‘Extended BSS Load element’ of the Beacon frame STAs use it for implementation-specific AP selection.
However, the frequency utilization is only calculated on primary 20MHz and secondary 20/40/80MHz since OFDM with SU/MU-MIMO is supported in 802.11ac.
In 802.11ax, OFDMA together with SU-MIMO on each RU and MU-MIMO on RU>=106 are supported.
t
f
t
f
802.11ac with SU/MU-MIMO
802.11ax with OFDMA+SU/MU-MIMO
2STA with 2SSs per STA
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
busy
idle
busy
busy
idle
busy
2STA with 1SS per STA on 242-RU
4STA with 2SSs per STA on 242-RU
4STA with 1SS per STA on 106-RU

## Slide 5: Objective
We propose to consider resource utilization of each 20 MHz channel and Frequency and spatial stream underutilization of OFDMA and SU/MU-MIMO on each 20 MHz channel for load balancing in 802.11ax.
  Resource dimensions {time, frequency, space}
    frequency-domain: each 20MHz-CH instead of primary 20, secondary 20/40/80MHz only
    space-domain: SU/MU-MIMO spatial streams on OFDMA RUs instead of that on whole BW

## Slide 6: 802.11ac BSS Load Element
MU-MIMO BSS load element
Tutilized: with Nss,i is utilized number of SSs during i-th busy time Ti
Nmax_SS: max Nss at AP
Tbusy: CCA busy time (us)
for primary 20MHz

## Slide 7: 802.11ax BSS Load Element
In 802.11ax, DL/UL MU OFDMA and SU/MU-MIMO are based on AP scheduling.
  Within each 20MHz, there may be OFDMA RUs with different number of MU-MIMO STAs and/or SU-MIMO streams.
  Each 20MHz has variant freq/spatial underutilization  need to be indicated respectively.
OFDMA+MU-MIMO BSS load element need to indicate
  Total number of OFDMA/MU-MIMO capable STAs associated with this BSS
  Freq/spatial underutilization ratio on each 20MHz-CH within the observation time considering the spatial number on each RU
  The observable utilization on each 20 MHz-CH, except for primary 20 MHz and second 20 MHz

## Slide 8: Indication of BSS Load Elements
AP updates/sends OFDMA+MU-MIMO BSS load information in Beacon or Probe response.
  Detailed definition of BSS load elements are as following
  The definition observable utilization is similar to that in extended BSS load element
Element ID
Length
OFDMA/MU-MIMO Capable STA Count
Freq/spatial Underutilization
for 1st 20MHz CH
Freq/spatial Underutilization
for 8th 20MHz CH
…
Observable 1st 20 MHz Subband of Secondary 80 MHz Utilization
Observable 4th 20 MHz Subband of Secondary 80 MHz Utilization
…
Observable 1st 20 MHz Subband of Secondary 40 MHz Utilization
Observable 2nd 20 MHz Subband of Secondary 40 MHz Utilization

## Slide 9: Summary
We propose to consider resource utilization of each 20 MHz channel and Frequency and spatial stream underutilization of OFDMA and SU/MU-MIMO on each 20 MHz channel for load balancing in 802.11ax.
OFDMA+MU-MIMO BSS load element need to indicate
  Total number of OFDMA/MU-MIMO capable STAs associated with this BSS
  Freq/spatial underutilization ratio on each 20MHz-CH within the observation time considering the spatial number on each RU
  The observable utilization on each 20MHz-CH, except for primary 20MHz and second 20MHz

## Slide 10: SP1
Do you support have a element to indicate BSS load info?

## Slide 11: SP2
Do you support to indicate the total number of OFDMA/MU-MIMO capable STAs associated with this BSS in BSS load element?
Y
N
A

## Slide 12: SP3
Do you support freq/spatial underutilization ratio on each 20MHz-CH within the observation time considering the spatial number on each RU?
Y
N
A

## Slide 13: SP4
Do you support to indicate resource unitization of OFDMA and MU-MIMO for each 20MHz channel for load balancing in 802.11ax?
Y
N
A

## Slide 14: References
[1] Draft P802.11REVmc_D8.0
When

## Slide 15: Back up
AP updates/sends OFDMA+MU-MIMO BSS load information in Beacon or Probe response.
Beacon
AP
BSS load information
Beacon
Probe Response
AP
Probe Request
STAs
BSS load information
Ack
Ack