## Slide 1: WUR Modulation and Coding
Date: 2017-03-08
Authors:

## Slide 2: Introduction
Multicarrier on-off keying (OOK) modulation has been proposed as the modulation in WUR [1]
To match the range of regular 802.11 the WUR data rate will likely need to be lower than 250 kb/s [2]
Waveform coding, like Manchester coding, has many advantages comparing to basic OOK with a repetition code
In this presentation we make a comparison of Manchester Code and Repetition Code
  Simulations
  Benefits of Manchester Coding

## Slide 3: Simulations
Comparison of Three Designs for DATA Field
  All designs on-off modulate the 4 µs OFDM symbols
  10 bit preamble and 100 bit payload
  The exact data rate has not yet been specified. We consider one two methods of improving receiver sensitivity (at lower data rate)
Baseline Multicarrier Multicarrier OOK (250 kb/s)
2x Repetition Code (125 kb/s)
  0 → (0, 0)
  1 → (1, 1)
Manchester Code (125 kb/s)
  0 → (0, 1)
  1 → (1, 0)

## Slide 4: Simulation Model
Applied a Third Order Butterworth Filter to remove noise beyond the signal bandwidth
Used Envelope Detector for low-power non-coherent receiver

## Slide 5: Demodulation – OOK & Manchester Coded OOK
OOK Demodulation requires calculation of detector threshold based on preamble signal
Manchester code Demodulation does not require calculation of threshold based on preamble signal

## Slide 6: Simulation – AWGN

## Slide 7: Simulation – Channel Model D

## Slide 8: Simulation – UMi Channel

## Slide 9: Benefits of Manchester Coding
Manchester coding provides multiple benefits in the WUR PHY Design
1-2 dB SNR advantage over repetition coding, in all channel conditions simulated
Simple implementation. No need to estimate detector threshold.
When there is interference, there is no bias in bit errors. There is equal number of 0 →1 and 1 →0 errors
Ensure 50% waveform duty cycle
Avoid long periods of zero waveform.
  A long period of zero waveform can cause false CCA channel availability detection
  Ensure good waveform structure for symbol clock recovery at the receiver

## Slide 10: Straw Poll
Do you support using Manchester Coding in the WUR PHY Design?
  The structure of the OFDM symbol and the data rate is TBD
  The Preamble design is TBD
Yes: 31
No: 10
Abstain: 22

## Slide 11: References
Shahrnaz Azizi, Minyoung Park and Thomas Kenney, “High Level PHY Design,” IEEE 802.11-17/84r0, January 2017
Steve Shellhammer and Bin Tian, “Regulations and Noise Figure – Impact on SNR,” IEEE 802.11-17/0365r0, March 2017