## Slide 1: WUR duty cycle mode and timing synchronization
Date: 2017-03-14
Authors:

## Slide 2: Background
As discussed in [1], keep WUR always on is not power efficient. To further save the power, a WUR duty cycle mode is needed.
  In WUR duty cycle mode, WUR STA will turn on the WUR based on a given duty cycle.
  AP will only send the wake up frame (WUF) within the STA’s WUR on window.
WUR on
WUR on
WUR off
WUR off
WUR on window
WUR off window
Time

## Slide 3: WUR timing mismatch Problem
The clock difference between AP and WUR duty cycle STA may lead to a timing mismatch problem.
  AP will send the WU frame in AP expected WUR on window of the WUR STA. However, timing of AP expected WUR on window will mismatch WUR STA’s actual WUR on window in a few seconds.
  The timing mismatch problem will increase the missing rate of WUR frames.
  Some mechanisms are needed to solve this problem.
Timing of AP
Timing of STA
WUR on windows based on STA’s clock
Complete Timing mismatch!
Time
…
…
Timing mismatch!
WUR on windows based on AP’s clock

## Slide 4: Timing error compensation
WUR STA can gradually increase its WUR on window to compensate the timing error.
  However, this will keep increasing the length of WUR on window and eventually lead to WUR always on mode.
Timing of AP
Timing of STA
WUR on windows based on STA’s clock
WUR on windows based on STA’s clock
Complete Timing mismatch!
Time
…
…
Timing mismatch!
WUR STA gradually increase the WUR on window to compensate the timing error.

## Slide 5: Timing synchronization (SYNC) signal
To solve the problem, AP can send a SYNC signal as a timing reference for a WUR STA.
  SYNC signal shall be send when WU radio is on.
  Based on the SYNC signal, WUR STA can adjust its starting time of the WUR on window to sync up with the AP.
  SYNC signal shall be some special OOK sequence to be detected by the WU radio without wake up the prime radio.
  However, per STA SYNC signal will become a big overhead if the number of duty cycle mode WUR STAs is large.
Timing of AP
Timing of STA
Time
…
…
…
…
…
New starting time for WUR on window
SYNC signal

## Slide 6: Proposed Common SYNC signal
To save the overhead, AP can periodically broadcast the SYNC signal for all WUR STAs in duty cycle mode.
  All duty cycle mode WUR STAs shall wake up prior to the common SYNC signal and timing of next SYNC signal is estimated based on current SYNC signal.
  AP and all WUR STAs in duty cycle mode shall adjust the timing of following WUR on windows based on the timing of the common SYNC signal.
  AP may assign WUR STAs different timing offset from the common SYNC signal to avoid collision of WU frames.
AP
STA1
Time
SYNC signal
STA2
Timing offset for STA1
Timing offset for STA2
SYNC detection window
WUR on windows

## Slide 7: Timing error compensation between common SYNC signals
Between common SYNC signal, there still exists some timing mismatch between AP and WUR STAs.
  To compensate the accumulating clock difference, WUR STAs can gradually increase the length of the WUR on windows.
  While receiving the common SYNC signal, WUR STAs can reset the length of its WUR on window to a default value.
  The increasing length of WUR on window for each duty cycle can be calculated based on AP’s clock accuracy and WUR STA’s own clock accuracy.
AP
STA1
Time
STA2
Increasing length of WUR on windows

## Slide 8: WUR duty cycle mode setup
To set up WUR duty cycle mode, WUR STA and AP need to negotiate on the period of WUR on windows, Timing offset etc.
  WUR STA can request to enter duty cycle mode by sending a request frame to AP.
    This WUR duty cycle request frame contains the period of WUR on windows.
  AP response WUR duty cycle request with a duty cycle response frame
    In the response frame, AP can assign the WUR STA a timing offset from the common SYNC signal.
    AP may also send the period of the common SYNC signal.
  In duty cycle mode, after each common SYNC signal, WUR STA will start WUR on window periodically after the timing offset from the SYNC.
AP
WUR STA
Time
Period of SYNC
Period of
WUR on window
Toffset
WUR duty cycle request
WUR duty cycle
response

## Slide 9: Error recovery
If a WUR STA in duty cycle mode failed to detect a common SYNC signal, it shall:
  Extend the following WUR on windows and SYNC detection windows
    The following WUR on windows and SYNC detection windows shall be long enough to cover all the possible arriving time of WU frames and common SYNC signals.
    If a number of contiguous common SYNC signals are missing, WUR STA shall enter WUR always on mode to detect the SYNC signal or even wake up the primary radio to search for the AP.
AP
WUR STA
Time
WUR failed to detect the SYNC signal

## Slide 10: SP1
Do you agree that 11ba shall define a WUR duty cycle mode?

## Slide 11: SP2
Do you agree that 802.11ba shall provide a mechanism to solve the timing mismatch problem in WUR duty cycle mode?

## Slide 12: SP3
Do you agree that 802.11ba shall define a common SYNC signal for all the WUR STAs in duty cycle mode as timing reference signal?

## Slide 13: SP4
Do you agree that AP shall assign a timing offset to each duty cycle mode WUR STA?
  The timing offset is defined as the time between common SYNC signal and the starting time of the first WUR on Window after the common SYNC signal.

## Slide 14: Reference
[1] 11-17-0043-00-WUR power save mode and problem
[2] 11-16-0974-00-0wur-wur-usage-scenarios-and-applications
[3] 11-16-1465-00-0wur-wur-usage-model
[4] 11-16-0027-00-lrlp-lp-wur-enabling-low-power-low-latency-capability-for-802-11