## Slide 1: WUR MAC issues follow-up
Date: 2017-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
The following several WUR MAC issues were discussed at the previous meetings [1] and there were some agreements among them
  Broadcast Wake-up
  Group wake-up
  Multicast Wake-up
  WUP (Wake Up Packet) contents design
This contribution discusses details of them and proposes the related SFD texts

## Slide 3: Broadcast Wake-Up (1/4)
For WUR mode STAs to receive Beacon or Group addressed BU through PCR, AP can send a broadcast wake-up packet to wake up all WUR mode STAs which are associated with the AP
Broadcast WUP should be sent early with enough time for those WUR mode STAs to receive Beacon/GA BU correctly after their wake up delay
  Because Broadcast WUP TX can be delayed if channel is busy and,
  Each STA’s wake-up delay could be different according to each STA’s capability or its environment
Broadcast Wakeup
AP
STA1
STA2
STA3
STA4
Wakeup delay
Beacon/
Group addressed BU
WLAN on
WLAN on
WLAN on
WLAN on
Waiting time

## Slide 4: Broadcast Wake-Up (2/4)
AP informs the STAs of the Wake-up Completion Time (WCT)
  WCT means the time at which WUR mode STA should finish its wake up procedure to receive the DTIM or Group addressed BU correctly
    How to set the WCT by AP is out of this standard. It’s AP’s implementation
Because the WCT value is decided when the broadcast WUP is transmitted, WCT should be included in broadcast wake-up packet
  Each WUR mode STA decides its WLAN-On start time based on the received WCT value and its wake up delay
AP sends WLAN frame (e.g., Beacon, Group addressed BU) through PCR after the WCT

## Slide 5: Broadcast Wake-Up (3/4)
Example 1 (Beacon reception): AP sets WCT to TBTT
Upon receiving Broadcast WUP, WUR mode STA finishes its wake up procedure until WCT and waits to receive Beacon frame
  In this case STA can update the system information based on the information in the received Beacon
Wake up start time of STA 3, 4
Wake up start time of STA 1, 2
Broadcast Wakeup
(WCT)
AP
STA1
STA2
STA3
STA4
Wakeup delay
Beacon
WLAN on
WLAN on
WLAN on
WLAN on
WCT

## Slide 6: Broadcast Wake-Up (4/4)
Example 2 (Group addressed BU reception): AP sets WCT to the transmission time of group addressed BU
Upon receiving Broadcast WUP, WUR mode STA finishes its wake up procedure until WCT and waits to receive Group addressed BU frame
Wake up start time of STA 3, 4
Wake up start time of STA 1, 2
Broadcast Wakeup
(WCT)
AP
STA1
STA2
STA3
STA4
Wakeup delay
Group addressed BU
WLAN on
WLAN on
WLAN on
WLAN on
WCT

## Slide 7: TF reception after WCT
The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wake-up packet to the STA(s). [Motion 3, March 2017]
In this case, AP can also include WCT (wake-up completion time) in WUP (s) before sending the Trigger frame so that STA can decide its WLAN-On start time
WUP (STA 1, 2, 3), WCT
AP
STA1
STA2
STA3
STA4
MU PPDU (STA 1, 2, 3)
PS-Polls from STA 1~3
TF
Wakeup delay
WLAN on
WLAN on
WLAN on
WCT
Wake up start time

## Slide 8: Group wake-up
Group wake up
  Group wake up (e.g., using Group ID) can be used for waking up all STAs belonging to a group but it hardly happens
  May not be efficient if it is used for waking up a part of STAs in a group  increasing false alarm
  Need complicate group management like MU-MIMO
WUP
(GID =1)
AP
STA1
STA2
STA3
STA4
WLAN on
Wakeup delay
MU PPDU (STA 1, 2, 3)
STA1, 2, 3, 4, 5 belong to Group 1 (GID=1)
STA5
PS-Polls from STA 1~5
Unnecessary power consumption
Unnecessary power consumption

## Slide 9: Multi-User Wake-Up (1/2)
Multi-User (MU) Wake Up
  WUR needs to support MU wake-up mode for waking up a part of STAs in a group
  Example 1) WUP may contain multiple receiver IDs  the WU packet size is increased according to the number of STAs
  Example 2) WUP may contain the STA’s position bitmap like TIM
    TIM size should be optimized (e.g., like 11ah hierarchical TIM or using WUR ID1) instead of AID)
A STA should also send a response frame to the AP after receiving MU wake-up packet which is sent for unicast WLAN frame
1) WUR ID can be allocated before entering WUR mode
STA4
WUP (STA 1, 2, 3)
AP
STA1
STA2
STA3
WLAN on
Wakeup delay
PS-Poll
D1
PS-Poll
D2
PS-Poll
D3
WLAN on
WLAN on

## Slide 10: Multi-User Wake-Up (2/2)
Example 1
Total length (M)
  WUR frame type = a: M= 2 (bytes)
  WUR frame type = a+1: M= 3 (bytes)
  WUR frame type = a+2: M= 4 (bytes)
Starting ID = X
Bitmap
X+1
X+2
X+n
…
Total length = M bytes

## Slide 11: WUP contents format (1/2)
Considerations on Wake-Up Packet (WUP) contents design
  WUP TX frequency as small as possible to minimize the contention with other WLANs/WUPs  Broadcast/Group/MU wake up
  WUP content size should be minimized (e.g., if OOK is used, 1 symbol (4us) is used for delivering 1 bit)  WUP optimization
  Avoid unnecessary false alarm of wake-up  MU wake-up instead of group wake up
  Including WUR operation mode (WOM) information which indicates the STA’s operation after receiving the WUP
    Whether the STA should wake up after receiving the WUP or not
      WUP may be sent for just keep alive check or synchronization(WUR beacon reception). In this case STA does not need to wake up
    Whether the STA should send a response frame (e.g., PS-Poll) based on EDCA though primary connectivity radio after turning on the main radio or not
      E.g., Sending a response for unicast WUP, not sending a response for a broadcast/multicast WUP for group-addressed data TX, may not be sending a response for a WUP for MU polling
      This information is necessary for supporting the following motion text
      A STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up packet. [Motion 1, March 2017, see [1] [6]]

## Slide 12: WUP contents format (2/2)
Various WU packet types according to different length
  Frame Type & Receiver ID
    0: WUR Beacon
    1: Broadcast wake-up, Receiver ID does not need to be included
    2: Individual wake-up, Individual ID is included
    3: MU wake-up, Multiple ID information (e.g., TIM or multiple IDs set) are included instead of individual ID
  WOM(WUR Operation Mode)
    0- No wake-up, 1- Wake-up and EDCA access, 2- Wake-up and No EDCA access
    WOM can be merged with Frame Type field
  Transmitter ID: Partial BSSID (or BSS Color)
  WCT (Wake-up completion time): the time at which WUR mode STA should finish its wake up procedure (slides 4, 5).
    AP sends a frame to STA (s) through the primary connectivity radio after the WCT
    STA can determine its WLAN On Start time based on the WCT
Frame Type
Transmitter ID
(WOM)1)
Receiver ID (optional)
FT=0
Transmitter ID
(WOM)
FT=2
Transmitter ID
FT=3
Transmitter ID
Individual ID
Multiple ID Info
WCT
Timestamp[2]
(WOM)
(WOM)
WCT
WCT
FCS
FCS
FCS
FCS
FT=1
Transmitter ID
(WOM)
WCT
FCS

## Slide 13: Conclusion
For power saving of WUR STAs, AP includes the WCT in a wake-up packet (WUP)
  WUR STA decides when it turns on the primary connectivity radio after the WUP based on the WCT and its wake-up delay
  AP sends WLAN frame to a STA through the PCR after the WCT
A multi-user wake-up packet includes the information of multiple STAs which need to wake up (e.g., multiple IDs or Bitmap type)
A STA should also send a response frame to the AP after receiving MU wake-up packet which is sent for unicast WLAN frame as well as after receiving unicast wake-up packet
Wake-up packet has different types according to its packet length and includes the frame type field for it
WU packet design contains the information for the STA’s operation after receiving WUP (e.g., WUR operation mode (WOM))
  0: No-wake up, 1: wake-up and EDCA access, 2: wake-up and waiting w/o EDCA

## Slide 14: References
[1]11-17/0054, WUR MAC issues
[2] 11-17-0343-00-00ba-wur-beacon

## Slide 15: Straw Poll 1
Do you support the following?
  A broadcast wake-up frame (B-WUF) includes the information to indicate the deadline on which WUR mode STAs should complete its wake up procedure after receiving the broadcast WUF

## Slide 16: Straw Poll 2
Do you support the following?
  A multi-user wake-up frame (MU-WUF) contain the information to identify the multiple STAs
    The detailed identification (e.g., multiple individual identifiers, group bitmap or User bitmap, etc.) is TBD.

## Slide 17: Straw Poll 3
Do you support the following?
  User bitmap is included in an MU wake-up frame as the information to identify the multiple WUR mode STAs
    The details of bitmap is TBD
    The size of the information to identify the multiple STAs will not be larger than 4 bytes

## Slide 18: Straw Poll 4
Do you support the following?
  A wake-up frame (WUF) contains the 4-bit WUF Type field to indicate the type of the WUF
    WUF Type = 0: WUR Beacon
    WUF Type = 1: Individual wake-up
    WUF Type = 2: Broadcast wake-up
    WUF Type = 3: Multi-user wake-up

## Slide 19: Straw Poll 5
Do you support the following?
  Broadcast wake-up frame (B-WUF) does not carry the receiver ID

## Slide 20: Straw Poll 6
Do you support the following?
  A wake-up frame (WUF) contains the following information to indicate the STA’s operation after the WUR mode STA receives the wake-up packet
    Whether the WUR mode STA wakes up after receiving the WUP or not
    Whether the STA sends a response frame (e.g., a PS-Poll) after waking up from WUR mode or not
    The detailed indication method (e.g., explicit or implicit like Type field) is TBD