## Slide 1: WUR Reference signal
Date: 2017-05-01
Authors:

## Slide 2: Abstract
Discussing applications of WUR beacon frame in different 11ba usage models
Considering possible behaviors of WUR STAs when no WUR beacon frame is received
Proposing that AP indicates its context (e.g., mobility, power-saving) to the associated STAs

## Slide 3: WUR Beacon
11ba has defined WUR beacon frame[1]
  Transmitted by WUR AP
    Verifying connectivity
    Delivering some management info.
      E.g., time synchronization function
    Other purpose TBD

## Slide 4: Beacon frame in existing 802.11 networks
Main purposes of beacon frame
  Announcing the presence of a WLAN
  Providing all the essential BSS information
AP consistently broadcasts beacon frame as long as the BSS exists
  Usage models of existing 802.11 standards mostly considers infrastructure BSS
    Consisting of Fixed AP and user equipped STAs with little mobility
Upon a lack of beacon frame from the associated AP, a STA might invoke the scanning procedure

## Slide 5: WUR beacon in WUR network
In case of WUR networks, the applications of WUR beacon might be different from the existing 802.11 networks[2]
  Considering the variety of network environments
    Mobile and/or power-saving APs (cattle farm, wearable, wake-up home AP)
      Service region may move
      Serving temporarily
    IoT, wearable STAs
      Power saving than performance
      Query-based data transfer
    In some models, BSS membership might be weak or not be present
      Moving goods tracking, ITS
We need to examine effective applications of WUR beacon
  Considering various usage models of 11ba with different circumstances

## Slide 6: Observation (1) – smart home (UM1)
A smartphone is connected to a fixed AP
  The smartphone is operating in WUR mode to reduce power consumption when it is not active
The AP periodically broadcasts WUR beacon frames for STAs in WUR mode
  STAs can assure the connectivity without PCR beacon
The smartphone might get out of the WUR beacon range by user
  Upon the lack of WUR beacon frame, the STA might notice that it had lost the connection from the AP
  New connection is necessary
Recommended behavior upon receiving no WUR beacon:
  The STA wakes up its PCR and invokes the scanning procedure

## Slide 7: Observation (2) – outdoor cattle farm (UM3)
Sensor STAs are equipped by cows, and a cattleman with mobile AP manages the sensors
  There might be no fixed APs that cover the outdoor farm
    The sensor are supposed to communicate only with the mobile AP
  The sensors are mostly operating in WUR mode
The Mobile AP broadcasts WUR beacon frames
As the cattle man left the farm, no WUR beacon will be received by the sensor STAs
  Cattleman is not supposed to stay in the farm all day

## Slide 8: Observation (2) – outdoor cattle farm (UM3)
In this case, however, the sensor STAs may not need to wake-up their PCR and find a new BSS
  Waste of power, if there’s no AP to connect
Recommended behavior upon receiving no WUR beacon:
  The sensor STAs stay in WUR mode and wait the next visit of the cattle man
  In order to do so, the sensor STAs must be aware of that the AP has mobility and may not serve consistently

## Slide 9: Observation (3) – wake-up home AP (UM8)
In small home/office, user equipment and sensors are connected to fixed AP
  The AP might enter to WUR mode to reduce power consumption and interference
The AP periodically broadcasts WUR beacon frames for STAs in WUR mode
As the AP starts to operate with WUR mode, no WUR beacon will be transmitted
  Some STAs might not know that the AP is operating in WUR mode
    E.g., WUR mode indication failure
  Applying the same logic from the observation (1), STAs in the area might wake up their PCR and invoke scanning, but neither PCR beacon is present

## Slide 10: Observation (3) – wake-up home AP (UM8)
Recommended behavior for Smartphone or laptop:
  It transmits WUP first, and then scanning if no response
    It is necessary to distinguish whether it had lost its connection by distance or the associated AP is in WUR mode
  In order to do so, the STA must be aware of that the AP may enter WUR mode in advance
Recommended behavior for IoT, sensor STA
  Since both the STA and AP has no mobility, it is better to stay in WUR mode, and transmit WUP if necessary
  The STA must be aware of that the AP has no mobility

## Slide 11: Summary
We have investigated the application of WUR beacon and corresponding behaviors of STAs in different usage models
It is hard to define a unified behavior regarding WUR beacon reception
  Considering the variety of WUR network environment
It seems useful for WUR STAs to understand the context of their associated AP
  E.g., mobility, power-saving
  It could help STA to optimize their behavior regarding WUR beacon reception
We propose that AP indicates its context to the associated STAs
  Few bits in WUR mode element can be assigned[3]

## Slide 12: Strawpoll
Do you support the following?
  Define a mechanism for AP to indicates its context (e.g., mobility, power-saving) in WUR mode element
  Y/N/A

## Slide 13: Reference
[1] 11-17-0575-00-00ba-spec-framework
[2] 11-17-0029-05-00ba-wur-usage-model-document
[3] 11-17-0342-04-00ba-wur-negotiation-and-acknowledgement-procedure-follow-up