## Slide 1: Spatial Reuse Group Challenges
Date: 2017-03-13
Authors:
Reza Hedayat, Newracom

## Slide 2: Background: OBSS-PD Rule
OBSS-PD rule
  Given an OBSS-PD range (OBSS-PD-min/max) announced by an AP, the associated STAs can ignore any OBSS PPDU that has RSSI less than OBSS-PD-min
Spatial reuse group (SRG)
  A set of AP/BSS together form a SRG group so that each BSS would apply potentially more aggressive OBSS-PD-min/max to any other OBSS PPDU originated from other BSS within the SRG
Given above rules, it is possible that SR STAs apply aggressive OBSS-PD thresholds to OBSS PPDUs causing increasing level of interference and more collision

## Slide 3: Spatial Reuse Group (SRG) [16/947r21]
Example: AP1/2/3 form a SRG
  AP1/BSS1 with Color C1
  AP2/BSS2 with Color C2
  AP3/BSS3 with Color C3
STAs in BSS1 use a more aggressive OBSS-PD-min/max for OBSS PPDUs with Color C2, C3 (SRG OBSSPD-MIN/MAX)
  Similarly STAs in BSS2/3 …
  Example: SRG OBSSPD-MIN = -62dBm
STAs in BSS1/2/3 use modified NON-SRG OBSS-PD for other OBSS PPDU
  Example: NON-SRG OBSSPD-MIN = -82dBm
BSS2, Color C2
AP2
BSS1, Color C1
AP1
BSS3, Color C3
AP3

## Slide 4: What Could Go Wrong?
Consider presence of an OBSS that doesn’t belong to the SRG
  BSS0/AP0 with Color C0
If C0 is different than C1/2/3
  Then SRG STAs use the intended OBSS-PD: NON-SRG OBSSPD
But if C0=C3, STAs in BSS1/2 treat BSS0 PPDUs with SRG OBSS-PD thresholds (SRG OBSSPD-MIN)
  This is an unintended behavior from SRG STAs
Chance of this happening is: the size of SRG divided by 64
  E.g. if SRG has 16 BSS, the chance of collision is 0.25
BSS2, Color C2
AP2
BSS1, Color C1
AP1
BSS3, Color C3
AP3
BSS0, Color C0
AP0

## Slide 5: What Could Go Wrong?
Similar unintended behavior could happen between two SRGs as well
In a public place e.g. airport, there could be two or more WiFi providers, each forming own SRG.
In this example, if C21=C11:
  Within BSS22 coverage, BSS11 PPDUs get treated with SRG2 OBSSPD-min
  Within BS12 coverage, BSS21 PPDUs get treated with SRG1 OBSSPD-min
  If SRG OBSSPD-min=-62dBm in both SRG, then BSS21 and BSS11 more interference/collision, which would have not existed without SRG
SRG1,BSS12
Color C12
SRG1, BSS11
Color C11
SRG2,BSS22
Color C22
SRG2, BSS21
Color C21

## Slide 6: Challenges with SRG Rules
The intention of SRG proposal is that a set of APs are grouped together by a higher entity that controls the operation of APs
  Operations such as channel and BSS Color selection of the APs
However, there is no guarantee that an AP announces SR Parameter set with the right APs/Colors; and IEEE spec and certification programs are blind about it
Example of using SRG to be aggressive in using medium:
  An unmanaged AP may announce an SRG and list several random BSS Colors within its SR Parameter Set and set an aggressive SRG OBSS-PD
  As a result, STAs associated with the AP follow the AP announcement and treat all OBSS PPDUs with the aggressive SRG OBSS-PD thresholds

## Slide 7: Challenges with SRG Rules
Applying aggressive SRG OBSS-PD thresholds to non-SRG OBSS causes additional interference and collisions to the non-SRG OBSS
Note that -82dBm ≤ SRG OBSS-PD ≤ -62dBm, hence practically it is possible that the difference in SRG and NON-SRG OBSS-PDs be as large as 20dB
  For instance: BSS0, the non-SRG BSS in slide 4, could be using PD=-82dBm while the SRG BSS use OBSS-PD-min=-72dBm or -62dBm

## Slide 8: Possible Solution - 1
To help uniquely identifying SRG PPDUs, one solution is to add a new identifier SRG ID (or ESS Color) in each SRG PPDU, which is best if it is in HE SIG-A
Solution: SRG Identifier
  Assign a multiple-bit subfields in HE SIG-A to indicate a SRG ID
Pros:
  Easiest way in identifying SRG PPDUs
  Most robust solution
Cons:
  Need allocation of several bits within HE SIG-A

## Slide 9: Possible Solution - 2
Alternatively, in order to let a STA to find out whether a PPDU is a SRG PPDU or not, one can indicate such PPDUs with a single bit in HE SIG-A
Solution: SRG Indication
  Assign a single bit in HE SIG-A to identify SRG PPDUs
Pros:
  Carrying a SRG indication in SIG-A offers an easy way in identifying SRG vs non-SRG PPDUs
Cons:
  It does not resolve the problem when there are two SRGs (slide 5)
  Need allocation of a bit within HE SIG-A

## Slide 10: Possible Solution - 3
Each SRG AP actively monitors the potential non-SRG OBSS and finds out if exists a collision between the OBSS color and the BSS colors in SR Parameter Set, removes the BSS Color from the list and resends the SR Parameter Set to its STAs
Solution:
  AP identifies potential SRG BSS Color collision and removes each instance of BSS Color collision and resend SR Parameter Set
Pros:
  It rests the responsibility of identifying such Color Collision on the AP that wants to take advantage of SRG
Cons:
  It does not resolve the problem when the collision happens at the edge of coverage (when AP cannot detect it)

## Slide 11: Possible Solution - 4
Solution: Let each SRG STA identify potential Color Collision
  SR Parameter Set need to include: BSS Color (that is part of the SRG) as well as the BSSID that is associated with the BSS Color
  An SRG STA identifies a SRG PPDU by making sure that both BSS Color and the associated BSSID matches the associated fields within a potential SRG PPDU
Pros:
  Resolves the problem robustly
Cons:
  Complicates the SRG operation because it requires a SRG STA to match BSS Color (from SIG-A) and BSSID (from PPDU MAC header) to find out whether a PPDU is a SRG PPDU

## Slide 12: Conclusion
There is a possibility that a SRG STA treats a non-SRG PPDU with SRG OBSS-PD thresholds instead of NON-SRG OBSS-PD
  This is an unintended consequence of SRG rules
  This could cause a non-SRG STA be unfairly treated by as large as 20dB in preamble-detect difference
  This could affect a unmanaged OBSS, and could affect managed OBSS that is happen to be part of another SRG
Several possible solutions are offered in this contribution to resolve this type of color collision