## Slide 1: WUR Link Budget Analysis
Date: 2017-03-13
Authors:

## Slide 2: Introduction
Previous contributions focus on the On Off Keying (OOK) with 250kbps data rate [1,2,3 and etc.]
In this contribution, we will take a top-down approach to analyze the link budget of wake-up radio (WUR)
The analysis is based on 802.11ax indoor and outdoor channel models [4]
Discuss the link margin and potential data rate options

## Slide 3: Link Budget Settings
fc = 2.4GHz and 5GHz
Tx_Power: 20dBm
Propagation Loss (PL): 802.11ax channel models [1]
Tx/Rx Antenna Gain: 0dB
Rx Noise Figure: NF=15dB [4]
Noise Floor for 20MHz channel: N0=-101dBm
Rx SNR = Tx_Power – PL – 3*Shadowing- N0 - NF

## Slide 4: Indoor Channel B
Link margin of ~30dB at 10m, ~15dB at 20m, ~5dB at 30m for 2.4G band
Link margin of ~20dB at 10m, ~10dB at 20m, ~2dB at 30m for 5G band

## Slide 5: Indoor Channel D
Link margin of ~30dB at 10m, ~15dB at 20m, ~10dB at 30m for 2.4G band
Link margin of ~20dB at 10m, ~10dB at 20m, ~2dB at 30m for 5G band

## Slide 6: Outdoor UMi LOS
Link margin of ~20dB at 50m, ~15dB at 100m, ~10dB at 150m for 2.4G band
Link margin of ~15dB at 50m, ~10dB at 100m, ~5dB at 150m for 5G band

## Slide 7: Outdoor UMi NLOS
No margin for UMi-NLOS at d>40m for 2.4G band
No margin for UMi-NLOS at d>20m for 5G band

## Slide 8: Link Margin Discussion
At close range, there may be a SNR ceiling due to low power RF design of the WUR
  The noise figure may be nonlinear
  There may be a SNR ceiling limited by RF
  The link margin may not be as large as 30dB at close range
For different application/simulation scenarios [4, 6], there is additional attenuation for floor/wall penetration loss
For narrower signal bandwidth (e.g. 4MHz [1,2]), there are some transmit power limitations due to regulatory requirements [7]

## Slide 9: Multiple Data Rates
Link budge analysis shows, for 250kbps OOK,
  There is ~30dB link margin at close distance for indoor channels
  The coverage is shorter than 30m in UMi-NLOS channels @2.4G
Multiple data rates can be beneficial to achieve either better efficiency or coverage
Higher data rate can be accommodated for close range
  Higher rates can reduce packet duration significantly, and improve 802.11 traffic, also save power
  Options: higher-rate OOK with pulse during <4us, or higher order modulations
Lower data rates can extend outdoor coverage
  Options: lower-rate OOK with pulse during >4us, or error coding

## Slide 10: Power Consideration
With more data rate options, some signaling bits and slightly more digital processing may be needed
This will not cause significant power consumption change relative to RF
Reduction of airtime for higher rate may further save power

## Slide 11: Straw Poll 1
Do you agree to have more than one data rates for the wake-up packet?
  Yes
  No
  Abstain

## Slide 12: References
[1] Eunsung Park and et al., , “Further Investigation on WUR
Performance”, IEEE 802.11-16/1144r0, Sept. 12, 2016.
[2] IEEE 802.11-16-0865-01-0wur-performance-investigation-on-wake-up-receiver
[3] Minyoung Park et al., “LP-WUR (Low-Power Wake-Up Receiver) Follow-Up”, IEEE 802.11-16/0341r0, Mar. 14, 2016.
[4] IEEE 802.11-14/882r4, IEEE 802.11ax channel model document
[5] N.M. Pletcher, S. Gambini, and J.M. Rabaey, “A 2GHz 52 μW Wake-Up Receiver with -72dBm Sensitivity Using Uncertain-IF Architecture”, IEEE Journal of Solid-State Circuits, vol. 44, No. 1, pp. 269-280, Jan. 2009
[6] IEEE 802.11-14/621r3, TGax simulation scenarios
[7] Steve Shellhammer and et al., “Regulations and Noise Figure – Impact on SNR”, IEEE 802.11-17/0365r0, Mar., 2017