## Slide 1: EDMG Capabilities for LDPC codes
Date: 2017-3-14
Authors:

## Slide 2: Introduction
  The proposal of length 1344 LDPC codes (long codes) [1] was approved and Draft IEEE802.11ay D0.2 [2] specifies in 30.3.6 regarding the long code matrices of code rates 1/2, 5/8, 3/4 and 13/16.
Considering this situation, this contribution discusses the necessity of EDMG capabilities related to LDPC codes.

## Slide 3: EDMG Capabilities Elements
    EDMG Capabilities element is specified in 9.4.250.1 of Draft IEEE802.11ay D0.2 [2].
EDMG Capabilities element format
 | Element ID | Length | Element ID Extension | Core Capabilities | Extended Capabilities 1 | … | Extended Capabilities N
Octets: | 1 | 1 | 1 | 4 | Variable | … | Variable
    A non-AP or non-PCP EDMG STA declares that it is an EDMG STA by transmitting the EDMG Capabilities element. The element is present in Announce, Association Request, Association Response, Reasspciation Request, Reassociation Response, Probe Request and Probe Response frames and can be present in DMG Beacon, Information Request, and Information Response frames.

## Slide 4: Necessity of EDMG Capabilities Related to LDPC Codes
    A transmitter needs to know whether receivers support optional capabilities or not. Therefore it is necessary for receivers to transmit EDMG capabilities in the 11ay capability exchange.
    We consider it necessary for receivers to transmit EDMG capabilities related to LDPC codes, because a transmitter needs to know whether receivers have a capability of decoding LDPC long codeword.

## Slide 5: Definition of EDMG Capabilities Related to LDPC Codes
To indicate whether receivers have a capability of decoding LDPC long codeword, long LDPC codes capability information (1bit) is needed in the EDMG capabilities element.
Name | Number of bits | Description
Long LDPC codes Supported | 1 | Set to 1 if the STA supports LDPC long cordword as specified in 30.3.6. Set to 0 otherwise.
Proposed EDMG capabilities Field
Note that, in Draft IEEE802.11ay D0.2 [2], (coding rate) 7/8 long LDPC code is not defined.

## Slide 6: Summary
It is proposed to include one bit related to LDPC codes in the EDMG capabilities element.
Long LDPC codes capability information (1bit)
7/8 long LDPC code is not yet defined and should be discussed.

## Slide 7: Straw poll
  Do you agree to add the following capability information in the EDMG capabilities element regarding LDPC codes into Draft IEEE802.11ay?
  - Long LDPC codes capability information (1bit)
  If the long LDPC codes capability field is set to 1, the STA supports
  LDPC long codeword for the supported MCSs. Otherwise, the STA
  does not support LDPC long codeword.

## Slide 8
References
11-16-0676-01-00ay-length-1344-ldpc-codes-for-11ay
Draft P802.11ay_D0.2