## Slide 1: MIMO phase in MU-MIMO Beamforming
Date: 2017-03-16
Authors:

## Slide 2: Abstract
This contribution proposes changes on MIMO phase in MU-MIMO Beamforming to reduce beamforming training overhead

## Slide 3: Background: MU-MIMO beamforming
MU-MIMO Beamforming protocol is defined in Draft 0.2
This protocol comprises following consecutive phases:
  SISO phase: an I-TXSS subphase and a setup subphase
  MIMO phase: four subphases (shown in the figure)
This protocol is designed to minimize interference among streams
Initiator
Responder
MU-MIMO BF Setup
MU-MIMO BF Training
MU-MIMO FB Poll
MU-MIMO selection
MU-MIMO FBs
STA1
STA2
STA3
MIMO phase

## Slide 4: Motivation
In some cases, signal power received by a STA might be very little unless the best sector is used
  For example, in a case where STAs create sharp beams in a LOS dominant environment
In such cases, interference at the STA in MU transmission might be small even without MU-MIMO beamforming training
That means shorter beamforming training is possible
STA (initiator)
  MU-MIMO with sharp beams in a LOS dominant environment
STA (responder)
STA (responder)
  little interference

## Slide 5: Proposal (1/2)
Enable an initiator to exclude some responders from the MU-MIMO BF Training and the MU-MIMO FB Poll subphases
  The initiator collects feedback including Sector IDs and their corresponding SNRs from responders in the SISO phase
  Based on the feedback, the initiator can estimate whether multiuser interference in MU transmission is small at each of the responders
  If the interference at some of the responders is expected to be small, the initiator may exclude them from the subphases

## Slide 6: Proposal (2/2)
In the MU-MIMO BF Setup subphase,
  a BF Setup frame includes the AIDs of only the remaining responders to indicate them performing MU-MIMO beamforming training
In the MU-MIMO BF Training and the MU-MIMO FB Poll subphases,
  the initiator sends frames to only the remaining responders
  the other responders ignore these subphases
  If all responders are excluded, these subphases are not present in the MIMO phase
Initiator
Responder
MU-MIMO BF Setup
MU-MIMO BF Training
MU-MIMO FB Poll
MU-MIMO selection
MU-MIMO FBs
STA1
STA2
STA3
including AIDs of the remaining responders
for only the remaining responders
MIMO phase

## Slide 7: Conclusions
Some responders might not need to perform MU-MIMO beamforming training in some cases
This contribution proposed to enable an initiator to exclude some responders from MU-MIMO beamforming training process

## Slide 8: STRAW POLL
Do you agree to incorporate the changes proposed in (11-17-0424-00-00ay-cr-on-mimo-phase-in-mu-mimo-bf.docx) into the draft spec?
  Yes
  No
  Abstain