## Slide 1: Throughput and Coverage Improvements with DFT-s-OFDM for 802.11ay
Date: 2017-03-16
Authors:

## Slide 2: Abstract
In [1-3], we evaluated the DFT-spread OFDM for 802.11ay from different angles (e.g., its benefit in fading, low PAPR, and channel-wise orthogonal multiple access in frequency domain)
In this contribution,
  We quantify the benefit of DFT-spread OFDM by using a majority of 11ay MCSs for two different simulation scenarios

## Slide 3: Background
A typical SC TX and RX for 802.11ad/ay may employ up-sampling, filtering, and down-sampling operations to match the sampling rate
In [3], we show that the up-sampling, filtering, down-sampling operation is equivalent to a weighted combination in frequency domain, which is not optimal in 802.11ay channels
DFT
(768)
EQ
IDFT
(512)
Data
448
64
RS
Weighted Comb.
S
/
P
2
3
Filter
EQ
DFT
(512)
IDFT
(512)
Data
448
64
RS
SC receiver (time domain representation)
SC receiver (frequency domain representation)
768

## Slide 4: SC versus DFT-spread OFDM
As shown in the appendix, SC transmitter can also be presented in frequency by using a weighted expansion block
DFT-spread OFDM basically removes the expansion and combination operations and achieves better PER and throughput performance
The references [4] and [5] show that DFT-spread OFDM can be implemented with mixed radix (e.g., radix-3 & radix-2) FFT implementation
DFT
(768)
EQ
IDFT
(512)
IDFT
(768)
512
DFT
(512)
DFT
(768)
Weighted comb.
Filter coef.
512
EQ
IDFT
(512)
IDFT
(768)
Weighted expan.
Filter coef.
512
DFT
(512)
Data
448
Data
448
Data
448
Data
448
512
Single carrier:
DFT-spread OFDM:

## Slide 5: Simulation Assumptions [11]
Waveforms: DFT-spread OFDM, SC
Phased antenna array
    Ant. 1: @ AP, @ STA, vertical polarization
    Ant. 2: 2 @ AP, @ STA, vertical polarization
    Ant. 3: @ AP, @ STA, vertical polarization
Channel: 11ay channel model (conference room (STA-AP)) [8], LoS path exists
Numerology: The 2 GHz 11ad/11ay numerology for both DFT-spread OFDM and SC [6, 7], single stream transmission
Equalization: Single tap MMSE-FDE, CHEST: Ideal, Coding: 11ad LDPC
Impairments: Rapp model [9] for power amplifier (PA), same OBO across the waveforms for the same MCS [11]
Payload: It is chosen such that the payload occupies exactly 3 symbol blocks duration to achieve maximum peak throughput (i.e., no padding for codeword and symbol block is necessary)

## Slide 6: Throughput Results (Conference Room, STA-AP, Ant. 3)
DFT-s OFDM provides more than 20% throughput gain in certain SNR ranges
On average, DFT-spread OFDM introduces approximately 15% throughput as compared to SC
The results for the aforementioned scenarios, provided in appendices, show similar improvement

## Slide 7: Coverage Range (STA-AP, Ant. 3)
Assumptions: TX power: 10 dBm; Noise figure: 5 dB; Path loss: Friis formula; Method: calculate SNR for a given link distance and find the best MCS
DFT-s OFDM improves the coverage range approximately by 10% as compared to SC

## Slide 8: Conclusion
In this contribution, we demonstrate that DFT-spread OFDM brings approximately 15% throughput gain for a given link distance and 10% coverage gain as compared to SC by using the MCS adopted in 802.11ay

## Slide 9: References
[1] “On the Single Carrier Waveforms for 11ay”, IEEE 802.11-16/01455r0
[2] “Performance Evaluation of Multi-DFT-spread OFDM for 802.11ay ”, IEEE 802.11-17/0048r0
[3] "Further Evaluation of Single Carrier Waveforms”, IEEE 802.11-17/0274r0
[4] “Software Optimization of DFTs and IDFTs Using the StarCore SC3850 DSP Core” http://www.nxp.com/assets/documents/data/en/application-notes/AN3680.pdf, 2010
[5] J. Lofgren and P. Nilsson “On Hardware Implementation of Radix 3 and Radix 5 FFT Kernels for LTE systems”, IEEE NORCHIP, Lund, 2011
[6] “Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band,” IEEE Std 802.11ad-2012, pp. 1–628, Dec. 2012.
[7] “Specification Framework for TGay,” IEEE 802.11-15/01358r6
[8] “Channel Models for IEEE 802.11ay,” IEEE 802.11-15/1150r7
[9] “11ay evaluation methodology,” IEEE 802.11-16/866r4
[10] K. R. Rao at al., “Fast Fourier Transform - Algorithms and Applications”, Signals and Communication Tech., Springer, 2010
[11] “PHY Simulations and Methodology”, IEEE 802.11-10/0431r3

## Slide 10: Appendix - Simulation Results

## Slide 11: Throughput Results (STA-AP, Ant. 1)

## Slide 12: Throughput Results (STA-AP, Ant. 2)

## Slide 13: Throughput Results (STA-AP, Ant. 3)

## Slide 14: Coverage Range (STA-AP, Ant. 2)

## Slide 15: Coverage Range (STA-AP, Ant. 3)

## Slide 16: PER Results (STA-AP, Ant. 1)

## Slide 17: PER Results (STA-AP, Ant. 2)

## Slide 18: PER Results (STA-AP, Ant. 3)

## Slide 19: Representations of Single Carrier TX and RX in Frequency
S
/
P
2
3
Filter
EQ
DFT
(512)
IDFT
(512)
P
/
S
3
2
Filter
DFT
(768)
IDFT
()
DFT
()
IDFT
(512)
Filter
coef.
DFT
(512)
Cancels each other
Cancels each other
Data
448
DFT
(768)
Weighted comb.
Filter coef.
512
EQ
IDFT
(512)
IDFT
(768)
Weighted expan.
Filter coef.
512
DFT
(512)
Data
448
Data
448
Data
448
768
DFT
(512)
IDFT
()
DFT
()
IDFT
(768)
Filter
coef.
Cancels each other
+
+
=
768
768
time
time
time
[10]
[10]
[10]
[10]