## Slide 1: Channel Allocation for SP
Date: 2017-3-13
1
Authors:

## Slide 2: Introduction
We propose channel width as well as channel number indication can be used in the STA’s SP request.
The channel number indication is the same as BW and Aggregation fields in EDMG-Header-A)
For a SP request, channel width indication is desired to support the following rule.
  “For an SP, the allocation does not have to include the primary channel”
2

## Slide 3: Why Channel Number is needed
There exists cases that s STA needs to designate a specific channel using “channel number” indication
  Case 1: Designate a channel that does not have interference
  Case 2: In order to accommodate AP’s flexible schedule, a STA may designate a channel on which BRP is not performed yet
    We assume BRP results are channel/frequency dependent.
3

## Slide 4: Why Channel Width is needed (1/2)
“Channel width” better supports the following rule than “channel number”:
  “For an SP, the allocation does not have to include the primary channel.”
“Channel width” is used to request any one channel satisfying the channel width requirement
  In comparison, “channel number” can only designate a specific channel.
For example, a pair of STAs both support 6.48 GHz may have multiple 2.16/4.32GHz channels for SP allocation.
  2.16 GHz: N, N+1, N+2
  4.32 GHz: Channel A, Channel B
4

## Slide 5: Why Channel Width is needed (2/2)
“channel width” is used for BF training/ transmission that does not need to designate the channel number:
  Enable flexible and efficient SP allocation for dense STAs: “channel width” can avoid potential channel request collisions, in which many STAs request the same channel number.
  SLS: any single channel may be enough
  BRP: if BRP was performed only on the maximum bandwidth, another BRP is required on any narrower channel to enable link adaptation/flexible SP schedule
  Link adaptation: narrower bandwidth is required
  MU-MIMO: considering the multiple users’ bandwidth capability, single channel may be required
5

## Slide 6: Proposed SP allocation
Channel number and channel width indications are proposed for two kinds of SP allocations:
  DMG ADDTS Request/Response sequences
  Poll/SPR/Grant sequences
Dynamic SP allocation: partial channel transmission may occur
  Since AP knows each STA’s available channels, AP can allocate a appropriate channel for partial channel transmission.
6
Dejian Li (Huawei)

## Slide 7: Signaling for SP Request (1/2)
Define a new IsChannelNumber field in the SP Request (SPR) and DMG ADDTS Request frames.
  The BW field is already defined in the control trailer in SFD
  IsChannelNumber indicates the BW field is channel number or channel width
Frame | Field/element | Content
SPR | Control Trailer | IsChannelNumber, BW and Channel Aggregation Note – IsChannelNumber is only valid in the control trailer of SPR; it is reserved in control trailer of other frames.
DMG ADDTS Request | DMG TSPEC element | IsChannelNumber, BW and Channel Aggregation
7

## Slide 8: Signaling for SP Request (2/2)
Definitions of the IsChannelNumber, BW and Channel Aggregation fields in the SPR/DMG ADDTS Request frame.
Field | Length | Description
IsChannelNumber | 1 bit | Indicates whether the STA requests a designated channel or not.
BW | 8 bits | If IsChannelNumber is set to 1, the BW field indicates the channel number, and the format of BW is the same as the BW field in EDMG-Header-A. If IsChannelNumber is set to 0, the BW field indicates the channel width.
Channel Aggregation | 1 bit | The same as the Channel Aggregation field in EDMG-Header-A
8

## Slide 9: Proposed signaling for SP Allocation
Define BW and Channel Aggregation fields in the Grant frame and DMG ADDTS Response frame.
The EDMG AP or PCP should allocate a channel as follows,
  If the BW field indicates the channel width, the AP or PCP may allocate a channel with channel width less than or equal to the value of the BW field.
  If the BW field indicates the designated channel number, the AP or PCP should allocate the channel as indicated by the BW field
Frame | Field/element | Content
Grant | Control Trailer | BW, Channel Aggregation fields specify the channel(s) over which the allocation is scheduled on. same as the corresponding fields in EDMG-Header-A
DMG ADDTS Response | DMG TSPEC element | 
9

## Slide 10
Conclusion
SP request
  Channel number and channel width indications are defined for SPR and DMG ADDTS Request frames.
SP allocation
  Define BW and channel aggregation fields in the Grant and DMG ADDTS Response frames.
10

## Slide 11: Straw Poll 1
Do you agree that the text given in “11-17-0434-00- Draft Text for Channel Allocation for SP” shall be included in the 11ay draft?
  Yes
  No
  Abstain
11
Dejian Li (Huawei)