## Slide 1: Channel Allocation for SP
Date: 2017-3-16
1
Authors:
Dejian Li (Huawei)

## Slide 2: Introduction
In 11ay draft, AP/PCP allocates channel(s) using BW and Channel Aggregation fields of the EDMG Extended Schedule element.
We propose that AP/PCP allocates SP over channel(s) according to the channel number or channel width indication in the SP request.
  Channel number indication: the same as BW and Aggregation fields in EDMG-Header-A)
  Channel width indication: desired to support the following rule.
    “For an SP, the allocation does not have to include the primary channel” (10.36.11.2)
2
Dejian Li (Huawei)

## Slide 3: Why Channel Number is needed
There exists cases that s STA needs to designate a specific channel using “channel number indication”
  Case 1: Designate a channel that does not have interference
  Case 2: In order to accommodate AP’s flexible schedule, a STA may intend to perform BRP on each channel
    We assume BRP training results are channel/frequency dependent.
3
Dejian Li (Huawei)

## Slide 4: Why Channel Width is needed (1/2)
“Channel width” better supports the following rule than “channel number”:
  “For an SP, the allocation does not have to include the primary channel.”
For example, a pair of STAs both support 6.48 GHz may have multiple 2.16/4.32GHz channels for SP allocation.
  2.16 GHz: N, N+1, N+2
  4.32 GHz: Channel A, Channel B
“Channel width” is used to request any one channel satisfying the channel width requirement
  In comparison, “channel number” can only designate a specific channel.
4
Dejian Li (Huawei)

## Slide 5: Why Channel Width is needed (2/2)
“channel width” can be used for BF training/ transmissions that does not need to designate the channel number:
  Enable flexible and efficient SP allocation for dense STAs: “channel width” can avoid potential channel request collisions of dense STAs.
  SLS: any single channel may be enough
  BRP: if BRP was performed only on the maximum bandwidth, another BRP is required on any narrower channel to enable following link adaptation or flexible SP schedule
  Link adaptation: any narrower bandwidth may be enough
5
Dejian Li (Huawei)

## Slide 6: Signaling for Channel Request for SP
The BW, Channel Aggregation and IsChannelNumber fields in the SP Request (SPR) and DMG ADDTS Request frames.
  IsChannelNumber indicates the BW field is channel number or channel width
Frame | Field/element | Content
SPR | Control Trailer | IsChannelNumber, BW and Channel Aggregation Note – IsChannelNumber is only valid in the control trailer of SPR; it is reserved in control trailer of other frames.
DMG ADDTS Request | DMG TSPEC element | IsChannelNumber, BW and Channel Aggregation
6
Dejian Li (Huawei)

## Slide 7: Proposed SP Allocation (1/2)
Channel number and channel width indications are proposed for two kinds of SP allocations:
  DMG ADDTS Request/Response sequence
  Poll/SPR/Grant sequence
Dynamic SP allocation: partial channel transmission may occur
  Since AP knows each STA’s available channels, AP can allocate a appropriate channel for partial channel transmission.
7
Dejian Li (Huawei)

## Slide 8: Proposed SP Allocation (2/2)
AP/PCP uses the BW and Channel Aggregation fields in the Grant frame and DMG ADDTS Response frame for SP allocation.
The EDMG AP or PCP allocates channel(s) as follows,
  If the BW field indicates the channel width, the AP or PCP may allocate a channel with channel width less than or equal to the value of the BW field.
  If the BW field indicates the designated channel number, the AP or PCP should allocate the channel as indicated by the BW field
Frame | Field/element | Content
Grant | Control Trailer | BW, Channel Aggregation fields specify the channel(s) over which the allocation is scheduled on. same as the corresponding fields in EDMG-Header-A
DMG ADDTS Response | DMG TSPEC element | 
8
Dejian Li (Huawei)

## Slide 9
Conclusion
Channel allocation according to channel number indication (BW and channel aggregation fields) or channel width is proposed for the following two kinds of SP requests/allocations.
  DMG ADDTS Request/Response
  Poll/SPR/Grant
9
Dejian Li (Huawei)

## Slide 10: Straw Poll 1
Do you agree that the text in contribution 17/0434r1 (Draft Text for Channel Allocation for SP) shall be incorporated in the 11ay draft?
  Yes
  No
  Abstain
10
Dejian Li (Huawei)