## Slide 1: LB225, CR for CID3222
Date: 2017-03-12
Authors:
Reza Hedayat, Newracom

## Slide 2: LB225, CID 3222 27.9.2.1, P190L30

## Slide 3: Background: Legacy CCA Rule
Legacy CCA rule is a simple medium sensing mechanism that:
  Only considers the signal strength from the frame’s transmitter
  Is ignorant to the interference caused to the intended recipient
    The intended recipient could be closer or further to observing STA
    Hence, the intended recipient is not necessary protected
OBSS-PD rule is inherently based on
legacy CCA and only adjusts the
OBSS-PD threshold
Hence, OBSS-PD suffers from the
same problem as legacy CCA
AP1
STA2
AP0
STA1
AP0 defers to AP1 transmission not knowing whether the recipient is STA1 (which is close to AP0) or STA2 (which is far enough)
Legacy PD = -82dBm
coverage wrt AP0

## Slide 4: Background: Legacy CCA Rule
Legacy CCA is ignorant to the interference caused to the intended recipient.
  In below figure three regions are identified
    The region that an observing/SR STA is not allowed to transmit; rightfully so
    The region that an observing/SR STA causes not much interference yet not allowed to transmit
    The region that an observing STA cause interference yet it is allowed to transmit
  (2) STA don’t causes much interference
  to RX; yet not allowed to transmit
  (3) STA is allowed to transmit. causes interference to RX
Response frame
TX
Data frame
RX
  (1) STA is not allowed to transmit

## Slide 5: Background: OBSS-PD Rule
OBSS-PD rule
  Given an OBSS-PD range (OBSS-PD-min/max) announced by an AP, the associated STAs can ignore any OBSS PPDU that has RSSI less than OBSS-PD-min
  A set of AP/BSS form a SRG group so that each BSS would apply potentially more aggressive OBSS-PD to any other OBSS PPDU originated from other BSS within the SRG
  OBSS-PD and SRG are expected to work well in scenarios where OBSSs are have less cross-coverage
Given above rules, it is possible that SR STAs apply OBSS-PD thresholds to OBSS PPDUs that are up to 20dB higher than a neighboring OBSS, potentially causing interference and collision and leading to unfairness

## Slide 6: OBSS-PD Rule
Using OBSS-PD rule, an 11ax STA discards inter-BSS PPDUs below the OBSS-PD-min threshold
OBSS-PD rule is based on measured RSSI of the transmitting STA, it is ignorant to the intended recipient of the PPDU
Example: consider AP1 sends frames to STA1 or STA2
  AP0 uses OBSS-PD rule
  AP0 causes little interference at STA2
  AP0 causes interference/collision at STA1
AP1
STA2
AP0
STA0
OBSS-PD-min
Coverage wrt AP0
STA1
OBSS-PD rule causes interference or collision at STA1
OBSS-PD rule not likely to cause significant interference or collision at STA2
OBSS-PD-min-default
Coverage wrt AP0

## Slide 7: OBSS-PD Rule
Legacy BSS
  Among legacy BSS, the unfairness due to preamble-detect (PD) does not exist since all legacy STAs are expected to follow the same PD=-82dBm
Mixed 11ax/legacy BSS
  11ax STAs discard OBSS PPDUs using OBSS-PD threshold that can be up to 20dB different with neighboring 11ax/legacy STAs

## Slide 8: Proposed solution
To protect intended recipients of data frames from potential interference/collision use a more relaxed OBSS-PD for response frames: instead of OBSS-PD-min, use the OBSS-PD-min-default
Example: as long as AP0 receives a response frame from STA1 with RSSI≥ OBSS-PD-min-default, AP0 sets its NAV accordingly and the remaining frames for STA1 (within ongoing TXOP) would be protected from AP0’s SR attempt
  But no SR restriction if STA2 is the intended recipient
If an SR STA detects the response only but did not the
data frame, the SR STA is restricted from OBSS-PD SR
AP1
STA2
AP0
STA0
OBSS-PD-min
Coverage wrt AP0
STA1
AP0 receives response frame from STA1 and would set NAV accordingly. No more interference from AP0 during TXOP remainder
AP0 does not receives any response frame from STA2; hence no change in its SR behavior
OBSS-PD-min-default
Coverage wrt AP0

## Slide 9: Proposed solution
AP1
AP0
STA0
OBSS-PD-min
Coverage wrt AP0
STA1
OBSS-PD-min-default
Coverage wrt AP0
AP1
data
data
data
BA
BA
STA1
AP0
(SR STA)
AP0 compares RSSI1 with OBSS-PD-min and may ignore the data frame and start back-off …
RSSI1
RSSI2
AP0 compares RSSI2 with OBSS-PD-min-default. AP0 would not discard the frame and sets the NAV ...
Remaining of the TXOP is respected and would not see interference from AP0
TXOP
BA

## Slide 10: Proposed text to resolve CID3222
TGax Editor: Change the following after 27.9.2.1
If the PHY of a STA issues a PHY-CCA.indication with a value equal to BUSY followed by an RXSTART.indication due to a PPDU reception then the STA’s MAC sublayer may a) issue a PHYCCARESET. request primitive and b) not update its NAV timers based on frames carried in the PPDU if all the following conditions are met:
— The received PPDU is an Inter-BSS PPDU (see 27.2.1 (Intra-BSS and inter-BSS frame detection))
— The received PPDU is not a non-HT PPDU carrying a response frame and the RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the NON SRG OBSS_PD level (defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power)). Or, the received PPDU is a non-HT PPDU carrying a response frame and the RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the OBSS_PD_min_default level (defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power))
— The PPDU is not one of the following:
A non-HT PPDU that carries an individually addressed Public Action frame where the RA field is equal to the STA MAC address
A non-HT PPDU that carries a group addressed Public Action frame
A non-HT PPDU that carries an NDPA

## Slide 11: Strawpoll
Do you accept the Revised resolution for CID 3222 with the proposed text in slide 10 of 17-0452r1?
- Accepted without objection.

## Slide 12: Appendix

## Slide 13: Unfairness: Case 1
PD mismatch causes unfairness
  STA1 receives AP0’s PPDUs with RSSI above PD=-82dBm, hence it does not ignore the frame and saves the NAV
  AP0 receives STA1’s PPDUs with RSSI below its OBSS-PD-min, hence it ignores the frame and does not update the NAV
    Subsequent frames destined to STA1 are subject to possible collision by frames sent by AP0.
STA1
AP1
AP0
STA0
OBSS-PD-min
Coverage wrt AP0
PD = -82dBm
Coverage wrt STA1
BSS1/AP1/STA1: Legacy, PD = -82dBm
BSS0/AP0/STA0: OBSS-PD-min = -62dBm
Either BSS could be a mobile BSS

## Slide 14: Unfairness: Case 2
OBSS-PD mismatch causes unfairness
  STA1 receives AP0’s frames with RSSI above its OBSS-PD-min (e.g. -62dBm), hence it does not ignore the frame
  AP0 receives STA1’s frames with RSSI below its OBSS-PD-min (e.g. -76dBm), hence it ignores the frame and does not update the NAV
STA1
AP1
AP0
STA0
OBSS-PD-min
Coverage wrt AP0
OBSS-PD-min
Coverage wrt STA1
BSS1/AP1/STA1: OBSS-PD-min = -76dBm
BSS0/AP0/STA0: OBSS-PD-min = -62dBm
Either BSS could be a mobile BSS

## Slide 15: Unfairness: Case 1 & 2
This problem is a side effect of unequal OBSS-PD-min (and of the same nature as hidden node problem)
A Solution is RTS/CTS, however:
  Avoiding this problem by RTS/CTS may not by something that deployed legacy STAs have been designed for
    Legacy STAs may not use RTS/CTS, or use infrequently
  An HE STA has to often use RTS/CTS in order to protect its recipient from a potential nearby OBSS
    Increasing overhead
STA1
AP1
AP0
STA0
OBSS PD
Coverage wrt AP0
PD/OBSS PD
Coverage wrt STA1
BSS1/AP1/STA1: OBSS-PD-min = -76dBm
BSS0/AP0/STA0: OBSS-PD-min = -62dBm
Either BSS could be a mobile BSS

## Slide 16: Unfairness: Case 3
In this situation:
  Both STA1 and AP0 are out of each other OBSS-PD-min coverage, hence they ignore each other frames and no NAV is set
  But due to proximity, each STA receives high interference from another STA
In long-term the SR STAs converge to low MCS due to interference, but …
  This either causes rate adaptation to fluctuate often, or
  Causes rate adaptation to be too conservative and stick with low MCS, despite the fact that the traffic is bursty and using low MCS is not always needed
STA1
AP1
AP0
STA0
OBSS-PD-min
Coverage wrt AP0
OBSS-PD-min
Coverage wrt STA1
BSS1/STA1: OBSS-PD-min = -72dBm
BSS2/STA2: OBSS-PD-min = -72dBm
Either BSS could be a mobile BSS