## Slide 1: Some clarifications on the current OBSS_PD SR spec text
Date: 2017-03-08
Authors:

## Slide 2: Background
Intention is to better explain the current spec text for OBSS_PD SR (D1.1) to help improve the understanding and clarify the spec

## Slide 3: Clarification of the proportional rule figure
OBSS_PDmin and OBSS_PDmax define the upper bound of the allowable zone (stripped zone).
A STA that operates under OBSS_PD SR can only choose OBSS_PDlevel and TxPower so that they are in the allowable zone.

## Slide 4: Clarification of the proportional rule figure
21dBm
STAs
-62dBm
-72dBm
-82dBm
OBSS_Pdmin_default=-82dBm
OBSS_Pdmax_default=-62dBm
PWRref
OBSS_PDlevel
TX_PWR
25dBm
APs

## Slide 5: Example
STAs with static selection of TxPower and OBSS_Pdlevel
Red STA: Max TxPower equal 24dBm, STA can not raise OBSS_Pdlevel
Blue STA: Max TxPower equal 11dBm, STA chooses to not increase OBSS_Pdlevel: -82dBm
Green STA: Max TxPower equal 11dBm, STA chooses to increase OBSS_Pdlevel: -72dBm is the max it can use
21dBm
STAs
-62dBm
-72dBm
-82dBm
OBSS_Pdmin_default=-82dBm
OBSS_Pdmax_default=-62dBm
PWRref
OBSS_PDlevel
TX_PWR

## Slide 6: Example
STAs with dynamic selection of TxPower and OBSS_Pdlevel
Red STA: Max TxPower equal 24dBm, STA can not reduce its TxPower to raise OBSS_Pdlevel because it otherwise can not close the link to its destination STA
Blue STA: Max TxPower equal 24dBm, STA sets its TxPower to a level sufficient for its needs (11dBm is sufficient to close the link with its destination STA) and dynamically or statically chooses to increase OBSS_Pdlevel up to -72dBm
21dBm
STAs
-62dBm
-72dBm
-82dBm
OBSS_Pdmin_default=-82dBm
OBSS_Pdmax_default=-62dBm
PWRref
OBSS_PDlevel
TX_PWR

## Slide 7: Selection of the operating point (TxPower and OBSS_PD)
Currently, this is left to implementer’s choice
SR STA can decide to reduce it’s TxPower to raise OBSS_PD and get more reuse opportunities
  Obviously the STA needs to close the link with its receiver and get sufficient margin
  So the most logical approach is to first choose the min TxPower to close the link and then derive the OBSSPD levels (SRG and non SRG)
Logic is that:
  a STA far from its AP won’t be able to reduce its power and won’t raise OBSS_PD
  A STA close from its AP can reduce its power and raise OBSS_PD

## Slide 8: SRG and non SRG mode
Non SRG mode:
  Applicable on all PPDUs that are classified as inter-BSS
  If no SR element received from the associated AP: OBSSPDmin=-82dBm, OBSSPDmax=-62dBm
  If SR element received from the associated AP: OBSSPDmin=-82dBm, OBSSPDmax can be tuned between -82 and -62dBm. OBSSPD can also be disabled
  The parameters are not optimized for the environment and they are defined to be conservative: derived based on current CCA thresholds
SRG mode:
  The most important mode for OBSS_PD SR is its use in dense managed environments.
  For that reason, D1.1 proposes the mechanism to allow the AP to set optimally the min/max parameters for operation within a group of BSSs
  Applicable on all PPDUs that are classified as inter-BSS and as inter-SRG
  Associated AP need to send SR parameter set element to define this mode
    Including SRG OBSSPDmin, OBSSPDmax, for the proportional rule
    SRG BSS color bitmap, SRG partial BSS bitmap to define the SRG

## Slide 9: Non SRG OBSSPD parameters
HE STAs shall maintain a NON SRG OBSS_PD level, with its value selected by respecting the OBSS_PD level condition above but with NON SRG OBSS PD MIN and NON SRG OBSS PD MAX in place of OBSS_PDmin and OBSS_PDmax, respectively, where NON SRG OBSS PD MIN and NON SRG OBSS PD MAX are determined according to Table 25-1
OBSS_PD SR Disallowed | NON SRG Offset Present | Value of NON SRG OBSS_PD_MIN | Value of NON SRG OBSS_PD_MAX
Spatial Reuse Parameter Set element not received | Spatial Reuse Parameter Set element not received | -82 | -62
0 | 0 | -82 | -62
0 | 1 | -82 | -82 + NON SRG OBSS PD MAX Offset
1 | Don’t care | -82 | -82
Table 25-1 Determining NON SRG OBSS_PD_MIN and NON SRG OBSS_PD_MAX values

## Slide 10: SRG OBSSPD parameters
HE STAs shall maintain a SRG OBSS_PD level, with its value selected by respecting of the OBSS_PD level condition above but with SRG OBSS PD MIN and SRG OBSS PD MAX in place of OBSS_PDmin and OBSS_PDmax, respectively, where SRG OBSS PD MIN and SRG OBSS PD MAX are determined according to Table 25-2
OBSS_PD SR Disallowed | SRG Information Present | Value of SRG OBSS_PD_MIN | Value of SRG OBSS_PD_MAX
Spatial Reuse Parameter Set element not received | Spatial Reuse Parameter Set element not received | N/A* | N/A*
Don’t care | 0 | N/A* | N/A*
Don’t care | 1 | -82 + SRG OBSS PD MIN Offset | -82 + SRG OBSS PD MAX Offset
*Note: When SRG Information is not present, a STA cannot determine a PPDU to be SRG and so will not use SRG OBSS_PD_MIN or SRG OBSS_PD_MAX values. |  |  | 

## Slide 11: Example for SRG OBSSPD
In managed environments, APs are able to set OBSS_Pdmin and max to better optimize reuse, but only between an SRG
21dBm
STAs
-62dBm
-72dBm
-82dBm
OBSS_Pdmin=-72dBm
OBSS_Pdmax_SRG=-72dBm
PWRref
OBSS_PDlevel
TX_PWR
D1.1 defines this
And limits application of SRG parameters only for the OBSSs belonging to the SRG (ESS in a managed enterprise)
This preserves protection so other networks not part of the SRG

## Slide 12: Clarification on how to perform Non SRG OBSS_PD SR
Spec text:
If the PHY of a STA issues a PHY-CCA.indication with a value equal to BUSY followed by an RXSTART.indication due to a PPDU reception then the STA’s MAC sublayer may a) issue a PHYCCARESET. request primitive and b) not update its NAV timers based on frames carried in the PPDU if all the following conditions are met:
  The received PPDU is an Inter-BSS PPDU (see 27.2.1 (Intra-BSS and inter-BSS frame detection))
  The RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the NON SRG OBSS_PD level defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power)
  The PPDU is not one of the following:
    A non-HT PPDU that carries an individually addressed Public Action frame where the RA field is equal to the STA MAC address
    A non-HT PPDU that carries a group addressed Public Action frame
    A non-HT PPDU that carries an NDPA

## Slide 13: Clarification on how to perform SRG OBSS_PD SR
Spec text:
If the PHY of a STA issues a PHY-CCA.indication with a value equal to BUSY followed by an RXSTART.indication due to a PPDU reception then the STA’s MAC sublayer may a) issue a PHYCCARESET. request primitive and b) not update its NAV timers based on frames carried in the PPDU if all the following conditions are met:
  The received PPDU is an Inter-BSS PPDU (see 27.2.1 (Intra-BSS and inter-BSS frame detection))
  The received PPDU is an SRG PPDU (see 27.2.1a SRG and non-SRG frame determination)
  The RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the SRG OBSS_PD level defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power)
  The PPDU is not one of the following:
    A non-HT PPDU that carries an individually addressed Public Action frame where the RA field is equal to the STA MAC address
    A non-HT PPDU that carries a group addressed Public Action frame
    A non-HT PPDU that carries an NDPA

## Slide 14: OBSSPD SR power restriction period
If a STA ignores an inter-BSS PPDU following the procedure in 27.9.2.1, using a chosen SRG OBSS_PDlevel, or a chosen NON SRG OBSS_PDlevel it starts an OBSS_PD SR power restriction period. This OBSS_PD SR power restriction period is terminated at the end of the TXOP that the STA gains once its backoff reaches zero.
  If a STA starts an OBSS_PD SR power restriction period with a chosen NON SRG OBSS_PDlevel, the STA’s power as measured at the output of the antenna connector, shall be equal or lower than the TXPWRmax, calculated with this chosen NON SRG OBSS_PDlevel with Equation (27-2), with the appropriate NON SRG parameters according to table 25-1, for the transmissions of any PPDU (including HE Trigger-Based PPDU) until the end of the OBSS_PD SR power restriction period.
  If a STA starts an OBSS_PD SR power restriction period with a chosen SRG OBSS_PDlevel, the STA’s power as measured at the output of the antenna connector, shall be equal or lower than the TXPWRmax, calculated with this chosen SRG OBSS_PDlevel with Equation (27-2), with the appropriate SRG parameters according to table 25-2, for the transmissions of any PPDU (including HE Trigger-Based PPDU) until the end of the OBSS_PD SR power restriction period.

## Slide 15: OBSSPD SR power restriction period
Multiple ongoing OBSS_PD SR power restriction periods can overlap in time (one per inter-BSS PPDU ignored).
All ongoing OBSS_PD SR power restriction periods end at the same time.
The STA shall not decrease the chosen SRG OBSS_PDlevel during an OBSS_PD SR opportunity. The STA may increase the chosen SRG OBSS_PDlevel during the OBSS_PD SR opportunity. The STA shall not decrease the chosen NON SRG OBSS_PDlevel during an OBSS_PD SR opportunity. The STA may increase the chosen NON SRG OBSS_PDlevel during the OBSS_PD SR opportunity.
The STA’s power shall therefore always be equal or lower than the minimum TXPWRmax among all TXPWRmax from ongoing OBSS_PD SR opportunities.

## Slide 17: Classification of SRG PPDU
Section 27.2.1a
If BSS Color information is present in a PPDU, the PPDU is determined to be an SRG PPDU if the bit corresponding to the BSS Color of the PPDU in the SRG BSS Color Bitmap is 1.
If Partial BSSID information is present in a PPDU, the PPDU is determined to be an SRG PPDU if the bit corresponding to the Partial BSSID of the PPDU in the SRG Partial BSSID Bitmap is 1.
Proposed addition in doc 267r3 : If Partial BSSID information is not present in a PPDU and BSSID information is correctly received, the PPDU is determined to be an SRG PPDU if the bit corresponding to BSSID[39:44] of the PPDU in the SRG Partial BSSID Bitmap is 1.
Otherwise, the PPDU is not determined to be an SRG PPDU. An HE STA that has not received a Spatial Reuse Parameter Set element from its associated AP with a value of 1 in the SRG Information Present subfield shall not classify any received PPDUs as an SRG PPDU.

## Slide 18: Conditions for OBSS_PD SR
In D1.1, we have the following:
When receiving only CTS or CTS-to-self, OBSSPD SR is disabled
When receiving RTS and CTS, OBSSPD SR is not disabled
SR parameter set element can disable NON SRG OBSSPD SR.
  Associated STAs can not do Non SRG OBSSPD SR
SRG is disabled if no SR parameter set element or if SR parameter set element with no SRG information present.