## Slide 1: OBSS_PD: Threshold problems
Date: 2017-03-08

## Slide 2: Abstract
OBSS_PD, in the form described in D1.0, implements the so-called “proportional rule”, with an OBSS_PD_min value of -82 dBm. The rule, as described in D1.0, may lower system efficiency in many scenarios, and it’s at the very least questionable whether it is an overall net positive.
This presentation outlines the rule and its effects (positive and negative) and proposes fixes that will make it work better.
CIDs addressed: 6768; partially relevant to CIDs referencing OBSS_PD thresholds: 3198, 3199, 3200, 5204, 5205, 5207, 5208, 5484, 5489, 5494, 5495, 5496, 5497, 5499, 5500, 5501, 5502, 5503, 5690, 5691, 5870, 7122, 7123, 7129, 7406, 7612, 8073, 8104, 8232, 8239, 9315,9540, 9944, 9946, 9947, 10031, 10032, 7125, 3197, 5689, 9541, 3222, 3196, 6025, 7823, 8233

## Slide 3: Spatial Reuse first principles, 1/6
The basic goal of spatial reuse:
A
B
Increase number of successful transmissions:
Add new transmissions and/or
Turn failing transmissions successful
C
D
E
F
 Increase OBSS_PD threshold
 Reduce Tx power


(Consider unmanaged deployments only)

## Slide 4: OBSS-PD SR
Note that OBSS-PD SR
  Allows more transmission in the red shaded area which causes interference to RX.
  Reduction in SR TX power leads to reduction of interference (orange shaded area)
Note increase of interference statistically.
Denser operation allows
TX
RX
CCA=-82dBm
OBSS_PD level > -82dBm
Increased interference from SR STA due to OBSS_PD SR
Reduced interference from SR STA due to reduced TX power
Based on and adapted from [1, 3] and similar presentations



## Slide 5: Spatial Reuse first principles, 2/6
A specific case:
A
B
(Assume 20 MHz channels, 6 dB noise figure)
C
D


Can C lower Tx power enough to permit A  B to succeed?
It’s possible. But it’s usually very difficult.
Effective noise floor @ B (with no interference—cf. next slide) is -95 dBm
B may be closer to C or farther away; on average about same distance
C interference @ B under proportional rule  -82 dBm
13 dB too high!

## Slide 6: Spatial Reuse first principles, 3/7
A specific case, contd. & refined:
C has lowered Tx power using proportional rule
C @ A = -82 dBm
We will do a random drop of B inside this circle
A uses conservative MCS (interference, stability): A  B succeeds if C @ B is  -88 dBm (7 dB SINR margin)
|CB|  1.48 |CA|
73% probability that A  B fails
  -93 dBm (2 dB margin): 100%
  -82 dBm (13 dB margin): 40%
A
C
-82 dBm
-88 dBm
FAIL
Random drop of B in circle
A = victim Tx
B = victim Rx
C = interferer Tx

## Slide 7: Spatial Reuse first principles, 4/7
A specific case, recap:
A
B
(Assume 20 MHz channels, 6 dB noise figure)
C
D


Can C lower Tx power enough to permit A  B to succeed?
We start out with a 13 dB gap we need to make up
If there’s a higher effective noise floor due to interference, and if we add a generous MCS margin, can make up some of that gap
  —Lowers A  B MCS
M … i … g … h … t work
(Need to avoid a net loss)

## Slide 8: The -82 dBm CCA threshold—1/4
Why is the baseline CCA Threshold = -82 dBm? Why not -95 dBm or some other lower value?
Dev 1
Dev 2
Dev 3
Because there’s another constraint:
Device 3 must decode the 6 Mbps L-SIG from device 1, to read the duration and set the NAV
CCA Threshold should be adequate to permit 6 Mbps L-SIG to be decoded (most of the time) by all devices

## Slide 9: The -82 dBm CCA threshold—2/4
This is exactly where the -82 dBm CCA threshold comes from:
“CCA sensitivity
The start of a valid OFDM transmission at a receive level equal to or greater than the minimum 6 Mbit/s sensitivity (-82 dBm) shall cause CCA to indicate busy with a probability >90% within 4 μs.”
  —802.11a-1999 (R2003), section 17.3.10.5

## Slide 10: The -82 dBm CCA threshold—3/4
… and huge margins were built in:
“Receiver minimum input level sensitivity
The packet error rate (PER) shall be less than 10% at a PSDU length of 1000 bytes for rate-dependent input levels shall be the numbers listed in Table 91 or less. The minimum input levels are measured at the antenna connector (NF of 10 dB and 5 dB implementation margins are assumed).”
  —802.11a-1999 (R2003), section 17.3.10.1

## Slide 11: The -82 dBm CCA threshold—4/4
Full calculation that led to -82 dBm:
-102.1 dBm1 + 4.7 dB2 + 10 dB3 + 5 dB4 = -82.4 dBm,  -82 dBm5
Corresponding calculation if specified today:
-102.1 dBm + 4 dB(2) + 6 dB(3) = -92.1 dBm,  -92 dBm
Noise floor for 16.25 MHz
Operating point for 6 Mbps 1,000 byte packets, 10% FER, from the simulations used
Noise figure
Implementation margin
See docs. IEEE 802.11-99/023, “Comments on P802.11a draft”, M. Morikura (NTT), January 1999 (giving curves, -88 dBm for first three combined), and IEEE 802.11-99/016, “Comments received on 802.11a in Letter Ballot 16”, January 9, 1999, pp. 7-8 (-87.4 dBm for first three, proposing -82 dBm)

## Slide 12: The CCA threshold, if rederived today
Additional adjustments required
  Use SNR needed to decode the L-SIG (4 bytes), instead of 1,000 bytes
    Perhaps 3-4 dB lower?
  Use SNR needed to decode L-SIG with frequency-selective fading rather than AWGN (as 802.11a did, in effect)
    E.g. channel model D, but conditioned on given RSSI
    Perhaps 4-5 dB higher?
  Net result (rough estimates), in the range (-92 dBm … -89 dBm) for 1 SS device; in the range (-95 dBm … -92 dBm) for 2 SS devices
Most 2 SS devices today should be able to decode the L-SIG in practice with RSSI of -92 dBm or higher, most of the time
-

## Slide 13: CCA threshold, summary
-95 dBm
-92 dBm
-82 dBm
Desirable limit of interference
Every 2 SS device should be able to decode most L-SIGs here—close to -95 dBm—from here “proportional rule” starts to make sense
So what’s this? It’s the level at which devices have to stop pretending they can’t hear L-SIGs. Because it was not credible (in 1999!) that any device would not have been able to decode at this level. This accounts for 10 dB of our 13 dB “gap”.

## Slide 14: Spatial Reuse first principles, 5/7
Effect of the mismatch:
C has lowered Tx power using proportional rule plus an additional 10 dB
C @ A now = -92 dBm
Same conditions as before:
We will do a random drop of B inside this circle
A uses conservative MCS: A  B succeeds if C @ B is  -88 dBm (7 dB SINR margin)
|CB| now  0.77 |CA|
24% probability that A  B fails
  (was 73% before)
A = victim Tx
B = victim Rx
C = interferer Tx
A
C
-92 dBm
-88 dBm
FAIL
Random drop of B in circle

## Slide 15: OBSS-PD SR, 2/2
Note that OBSS-PD SR
  Allows more transmission in the red shaded area which causes interference to RX.
  Reduction in SR TX power leads to reduction of interference (orange shaded area)
Note increase of interference statistically.
Denser operation allows
TX
RX
CCA=-82dBm
OBSS_PD level > -82dBm
Increased interference from SR STA due to OBSS_PD SR
Reduced interference from SR STA due to reduced TX power


Based on and adapted from [1, 3] and similar presentations

## Slide 16: Spatial Reuse first principles, 6/7
The other case:
A
B
Transmit power control can only help reuse
Maybe increased OBSS_PD threshold is the incentive to use TPC also?
Devices lose when they’re B but “statistically” gain when they’re F
C
D
E
F


(Consider unmanaged deployments only)

## Slide 17: Spatial Reuse first principles—7/7
OBSS_PD as a tradeoff—more transmit opportunities as incentive to lower transmit power
Well … maybe. (It seems a bit hazy. Are we sure this is a net gain?)
Also note that:
This can only be a factor when we have 3 or more OBSSs—no possible gain from this factor when we have just 2 OBSSs
The OBSS_PD rule is dynamic: why would the interferer reduce its transmit power when it does not encounter neighbors it otherwise would defer to?
  I.e., interferer adapts to its neighboring traffic; if no need to increase OBSS_PD threshold in recent time, why lower transmit power?
When increased OBSS_PD threshold is used, we are with high probability killing the frame we are transmitting over

## Slide 18: A way to fix this
Involve the victim AP in the decision loop!
This is a very complicated feature to specify and analyze, featuring multiple BSSs (possibly multiple OBSSs), traffic modelling, projections of future deployments and many topics that we have always left out of the standardization process (rate selection & shifting algorithms, fragmentation policy, latency and power management, interference assessment and mitigation, etc.)
The one unifying principle: if the victim AP is happy, everyone is happy
All we need to do is to provide a way for the victim AP to permit OBSS_PD over frames in its BSS (or rather, to disallow if the default is to permit), with just enough incentive for permission to be granted

## Slide 19: A sample approach
Assign bit combination in HE-SIG-A field to turn off non-SRG OBSS_PD, i.e., *other* STAs may not use non-SRG OBSS_PD over that frame
STAs may only use the appropriate bit combination if given permission by the AP to which they’re associated
  Permission can come from BSS-wide policy bits set in the beacon (and changeable dynamically).
  Permission can come from an individually addressed frame from the AP, giving permission. Such permission, even if granted, only lasts for N successful frames transmitted by that STA.
STAs may only use non-SRG OBSS_PD themselves if they have permitted it for the last N frames transmitted by that STA

## Slide 20: Straw poll (informational)
Do you agree to modify the OBSS_PD mechanism to allow for victim transmitters to disable use by other devices of non-SRG OBSS_PD for the frame in progress, according to the approach described on slide 18 of this document?
  Y
  N
  A

## Slide 21: References
[1] IEEE doc. 11/14-0637r0, “Spatial Reuse and Coexistence with Legacy Devices”, J. Wang (MediaTek) et al., May 2014
[2] IEEE doc. 11/14-0872r0, “A Protocol Framework for Dynamic CCA,” S. Coffey (Realtek) et al., July 2014
[3] IEEE doc. 11/15-1069r3, “Adaptive CCA and TPC”, J. Wang (MediaTek) et al., September 2015
[4] IEEE doc. 11/15-1082r1, “Analysis of BSS and ESS Structure During Concurrent SR Transmissions”, C. Lukaszewski (Aruba Networks), September 2015
[5] IEEE doc. 11/15-1083r3, “Cost/Benefit Analysis of SR Techniques (a.k.a. Grand Unified Theory of Spatial Reuse)”, C. Lukaszewski, L. Li (Aruba Networks), September 2015