## Slide 1: Resource Negotiation for Unassociated STAs in MU Operation
Date: 2017-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Chao-Chn Wang | MediaTek Inc |  |  | Chao-chun.wang@mediatek.com
James Yee | MediaTek Inc |  |  | James.yee@mediatek.com
Chao-Chun Wang (MediaTek Inc)

## Slide 2: Background
FTM negotiation protocol in dense environment must be able to adapt to the network loading to improve the efficiency of the protocol. The FTM negotiation phase can be further separated into request and response phase. There are three possible modes of operation
  The request phase operates in SU mode and the response phase operates in SU
    Same as REVmc and there is no need to add new protocol in 11 az standard.
  The request phase operates in SU mode and the response phase operates in MU mode
  The request phase operates in MU mode and response phase operates in MU mode
  The request phase operates in MU mode and response phase operates in SU mode
    The request is very similar to MU Mode request and the response is the same as in SU Response case.
The presentation is discussing the pro and con of the second and third methods

## Slide 3: Mode of Operations
(SU-MU) An STA sends FTM request in SU mode and receive FTM response (in SU PPDU format) for MU operation
  What’s AP behavior?
(MU – MU) An STA sends FTM request in MU mode and receive FTM response (in SU, MU PPDU format) for MU operation
  What is AP’s behavior?
Should AP includes an IE to announce the FTM MU operation parameters?
  Parameters are TBD
  Alternately there might be no IE, instead the details are announced in the Trigger Frame for MU operation

## Slide 4: SU-MU Operations
An STA sends FTM request in SU mode and receive FTM response (in SU PPDU format) for MU operation
  Does FTM Request has a field indicating the preference by the STA as to how it wants to receive FTM Response?
  The MU response frame (in SU PPDU) has a pre-defined/announced unique AID/multicast address to indicate that it is a FTM response frame
    An STA is expected to read all fields of the response frame with RA set to a pre-defined/announced multicast Address,
    The MU response frame (in SU PPDU) carries FTM parameters for every STAs, a FTMid (a.k. pre-AID) is assigned to each unassociated STA.
    The succeeding measurement operations operate in MU mode

## Slide 5: MU-MU Operations - 1
An STA sends FTM request in MU mode and receive FTM response (in SU, MU PPDU format) for MU operation
  AP sends trigger frame that indicates availability of random access RUs, each random access RU has a RUid
    Each STA selects one of the RU to transmit a FTM Request and records the RUid
  AP responds with a FTM response frame for MU operation (no ACK necessary)
      STA can determine if its request was sent successfully or not by looking at the MU FTM response frame.
    MU FTM response frame in SU PPDU – same as the previous page
    MU FTM response frame in MU PPDU
      The response frame use the same RU allocation as the request frame
    The MU response frame (in SU PPDU) carries FTM parameters for every STAs, a FTMid (a.k. pre-AID) is assigned to each unassociated STA.

## Slide 6: MU-MU Operations - 2
An STA sends FTM request in MU mode and receive FTM response (in SU, MU PPDU format) for MU operation
  AP sends trigger frame that indicates availability of random access RUs, each random access RU has a Ruid, this can be a trigger frame very specific to send FTM Request frames
    Each STA selects one of the RU to transmit a FTM Request and records the Ruid
  AP Responds back with a frame Acknowledging (or MBA ACK) the FTM Requests using the pre-defined Multicast Address (included in the Random RU Trigger frame, or pre-defined for the BSS)
    Acknowledgement can be an SU PPDU (with RA field set to the pre-defined or signaled MAC address in the Trigger Frame used to receive FTM Requests)
  AP responds with a FTM response frame for MU operation and a Trigger frame is allocated to receive Acknowledgement from STA
    MU FTM response frame in SU PPDU – same as the previous page
    MU FTM response frame in MU PPDU - TBD

## Slide 7: Trade-offs for evaluating various options
Power Consumption: The STA that has sent an MU request will be required to process all the Broadcast frames or a limited number of frames
  SU-MU is an allowed mode -> has power implications
  MU-MU has power implications
Waiting time from transmitting FTM Request to Receiving FTM Response: Revmc has this value at 10msec
  Revmc has a value defined to allow for STAs to save power
  APs take time to process FTM Requests and allowing for a large number of requests can increase the waiting time for FTM Response(s) -> tradeoff to be addressed
Using frames defined in 11ax or defining new frames to allow for 11az support

## Slide 8: Soliciting Unassociated STAs with Short NDP Operations
Using short NDP feedback mechanism to find out how many unassociated STAs are interested in doing ranging
Each short NDP random access RU is assigned with an RUid.
  The MU response frame (in SU PPDU) carries FTM parameters for every STAs, a FTMid (a.k. pre-AID) is assigned to each unassociated STA

## Slide 9: Mode of Operations
(SU-MU) An STA send FTM request in SU mode and receive FTM response (in SU PPDU format) for MU operation
  Pro
  Con
(MU – MU) An STA send FTM request in MU mode and receive FTM response (in SU, MU PPDU format) for MU operation - 1
  Pro
  Con
(MU – MU) An STA send FTM request in MU mode and receive FTM response (in SU, MU PPDU format) for MU operation (MU-MU Operation 2)
  Pro
  Con

## Slide 10: Motion 1
Motion:
Move to adopt the following text to the spec frame work document.
Instruct the editor to include it in the Tgaz SFD working draft under subsection 3.2 and grant the editor the editorial right. “The ID for ranging operation for an unassociated STA used for measurement phase will be in the FTM Rsp frame”
  Mover : Ganesh Venkatesan
  Seconder: Chao-Chun Wang
Y: 11 N: 0 A: 9
Absent:

## Slide 11: Straw Poll - 1
Do you agree to include the (SU-MU) procedure in the SFD
  An STA send FTM request in SU mode and receive FTM response (in SU PPDU format) for MU operation
Y: 6 N: 0 A: 16
Absent:

## Slide 12: Straw Poll - 2
Do you agree to include the (MU-MU) procedure in the SFD
  An STA send FTM request in MU mode and receive FTM response (in SU, or the PPDU format supported by 11ax specification) for MU operation .
  Note: AP do not explicitly ACK the FTM request frames.
Y: 5 N: 1 A: 18
Absent:

## Slide 13: Straw Poll - 3
Do you agree to include the (MU-MU) procedure in the SFD (in SU, or the PPDU format supported by 11ax specification) for MU operation – Note: AP do explicitly ACK the FTM request frames.
Y: 6 N: 0 A: 16
Absent:

## Slide 14: Straw Poll – 3.5
Do you agree to include the (MU-MU) procedure in the SFD (in SU, or the PPDU format supported by 11ax specification) for MU operation – Note: AP do explicitly ACK the FTM request frames. The ACK frame will carry ranging ID assignment for multiple requesters.
Y: 1 N: 5 A: 17
Absent: