## Slide 1: 11az NDP Announcement
Date: 2017-03-12
Name | Affiliation | Address | Phone | Email
Liwen Chu |  |  |  | 

## Slide 2: Why Defining New 11az NDPA and Trigger
  11az MU NDP ranging has sequence Trigger + UL NDP + NDPA + DL NDP.[1]
  11az SU NDP ranging has sequence NDPA + NDP + reverse direction NDP.[2]
SIFS
NDP
SIFS
NDP
NDPA
SIFS
SIFS
SIFS
Trigger
Multiple
NDP
NDP
NDPA
  802.11 ax defines the following different sounding sequence.
11ax MU Sounding
11ax SU Sounding
MU NDP ranging
SU NDP ranging
  The feedback information of 11az NDP ranging and 11ax sounding are different.
  In order for a TXOP responder correctly prepare a responding PPDU and prepare the measurement feedback, 11az NDPA and 11az Trigger should be redefined.
    This presentation discusses 11az NDPA.
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
UL
UL
DL
DL
UL
DL
DL

## Slide 3: Recap: 11ax/11ac NDPA
  11ax and 11ac define NDP Announcement (NDPA) separately since the feedback info and frame exchange sequence are different:
    NDPA + NDP + sounding feedback for VHT sounding and HE single-user sounding.
    NDPA + NDP + Trigger + sounding feedback for HE multiple-user sounding.
VHT NDP Announcement
HE NDP Announcement
VHT NDP Announcement Sounding Dialog Token
HE NDP Announcement Sounding Dialog Token
Sounding Dialog Token Number
1
Reserved
B0
B1
B2
B7
STA Info subfield format in an HE NDP Announcement frame
STA Info subfield format in an VHT NDP Announcement frame

## Slide 4: 11az NDPA Indication
  11az NDP Announcement can be identified by different methods:
    Option 1: B0 of Sounding Dialog Token being set to 1 and B1 of Sounding Dialog Token being set to 0 indicates 11az NDP Announcement. Option 2: new control type for 11az NDPA.
      We prefer option 1.
  the number of STA Info field (or unicast/broadcast RA) in NDP Announcement decides the 11az NDP sequence:
    NDP Announcement + NDP + reverse NDP (unicast for SU 11az NDP measurement), or
    NDP Announcement + NDP (broadcast for MU 11az NDP measurement).
      Since VHT doesn’t support Trigger and UL MU, NDP Announcement + VHT NDP within MU 11az NDP sounding should be disallowed.

## Slide 5: 11az NDPA User Info
  One or multiple 4-byte User Info field in 11az NDP Announcement includes:
    AID subfield indicates the receiver of the User Info field.
    Disambiguation subfield prevents a VHT STA from wrongly determining it's AID in the HE STA Info
    Feedback Type includes the measurement feedback information, e.g. timing feedback, AoA feedback, AoD feedback.
Reserved
Reserved
Feedback
Type
B26

## Slide 6: Straw Poll 1
  Do you agree to add the following text to 11az SFD:
    In 11az NDP ranging measurement phase, the NDPA has the following properties
      B0 B1 bits value of the Sounding Dialog Token field shall be set to 0b10 to indicate 11az sequence
      AID will be used to indicate the receiver participating in the sounding exchange
      Supported format will be the 4 byte per STA info field
.

## Slide 7: Motion 1
  Move to add the following text to 11az SFD:
    In 11az NDP ranging measurement phase, the NDPA has the following properties
      B0 B1 bits value of the Sounding Dialog Token field shall be set to 0b10 to indicate 11az sequence
      AID will be used to indicate the receiver participating in the sounding exchange
      Supported format will be the 4 byte per STA info field
.

## Slide 8: Reference
  [1] 11-17/50 NDP Based Measurement Proposal.
  [2] 11-17/

## Slide 9: Backup Slides

## Slide 10: EFTM Trigger Design----Common Info
  In order to carry feedback type in Trigger frame, some reserved bits or Trigger dependent Common Info field in Common Info or some reserved bits or Trigger Dependent User Info field in User Info can be used to indicate the feedback types.
    The feedback type is gotten from MU EFTM negotiation and EFTM Trigger doesn’t carry the feedback type information.
  A specific value in Trigger Type indicates that the Trigger frame is used for soliciting UL MU NDP.
DL Trigger
SIFS
UL NDP
SIFS
DL NDP
SIFS
DL NDPA
Reserved
Common Info
User Info
Reserved
Trigger frame
7
EFTM Trigger
8-15
(1 to N)
Reserved
Reserved
Trigger Type Definition
Reserved

## Slide 11: EFTM Trigger Design----Common Info
  Length in Common Info is the value of L-SIG Length of the solicited NDP.
  BW is the bandwidth of the solicited NDP.
  GI and LTF Mode is the GI and LTF mode of the solicited NDP.
  MU-MIMO LTF Mode indicates the LTF mode of the solicited NDP. (Reserved?)
  Number of HE-LTF Symbols indicates the number of the HE LTF symbols of the solicited NDP.
Reserved
Common Info
Reserved
Reserved
Reserved
Reserved
GI and LTF Mode
  AP Tx Power indicates the combined average power per 20 MHz bandwidth of all transmit antennas used to transmit the trigger frame at the HE AP.
  Packet Extension indicates the packet extension duration of the solicited NDP. (Reserved since 4us is always used?)
  HE-SIG-A Reserved indicate the values of the reserved bits in HE-SIG-A2 of the solicited NDP.

## Slide 12: EFTM Trigger Design----User Info
  AID12 indicates the STA’s AID that sends the solicited NDP.
  SS Allocation defines the spatial streams that the STA uses for the solicited NDP.
  Target RSSI indicates the target received signal power of the solicited NDP.
User Info
Reserved