## Slide 1: RR-TAG (802.18) Liaison Topic for 802.11 WG review
Date: 2017-03-15
Authors:

## Slide 2: Overview
This document presents an IEEE 802.18 Radio Regulatory Technical Advisory Group (RR-TAG) consultation response that impacts 802.11 operation in the 5150-5250 MHz band in Canada.

## Slide 3: ISED (Canada) Consultation
Innovation, Science and Economic Development, Canada
https://mentor.ieee.org/802.18/dcn/17/18-17-0049-00-0000-ised-5150-5250-mhz-consultation.pdf
Comments due March 29, 2017
Whether to modify the current technical and policy framework for radio local area network (RLAN) devices operating in the 5150-5250 MHz frequency band now, or wait for the results in WRC-19
Harmonizing with the US changes from 2013

## Slide 4: ISED Questions
The Department is seeking comments on the following points:
the demand for and benefit, if any, of allowing HPODs in the 5150-5250 MHz frequency band before WRC-19.
the potential impacts on domestic and foreign satellite systems in the 5150-5250 MHz frequency band of authorizing HPODs use prior to WRC-19 on the basis of a maximum e.i.r.p. of 4 W. Requirements for an elevation mask towards satellites and an exclusion zone of 25 km around receiving earth stations to protect all satellite systems would likely also apply.
should the Department proceed to authorize HPODs use prior to WRC-19, what regulatory approach would best ensure a balance of timely deployment and the protection of other existing and future services in the 5150-5250 MHz frequency band? Also, indicate any and all considerations that should be given to equipment standards, technical requirements, eligibility criteria and/or conditions of licence depending on the relevant approach.

## Slide 5: The Response
A. Demand for more Wi-Fi spectrum, and devices already approved in the US during the last three years, make this an important revision to ISED rules now
B. With more than 50,000 devices certified and in operation in the US under these rules, which have created no interference into satellite system similar and identical to those in Canada, there is proof that they can safely be deployed
C. We see great benefit to Canadian citizens and businesses in adopting the US rules in this band, but believe the 25 km exclusion zone for the one Earth station is larger than necessary to protect it

## Slide 6: Motion
Approve document https://mentor.ieee.org/802.18/dcn/17/18-17-0039-02-0000-proposed-ieee-802-response-to-canada-ised-consultation.docx as the IEEE 802.11 input for the ISED 5150-5250 MHz consultation, and forward to 802.18 for final editing and submittal to the 802 EC for their approval and submittal to ISED on or before March 29, 2017.
Moved:
Seconded:
Discussion?
Vote:

## Slide 7: Thank you