## Slide 1: Block Interleaver Design for SC PHY in 11ay
Date: 2017-04-11
Authors:

## Slide 2: Introduction
This presentation proposes a block interleaver design for SC PHY and high rate 64QAM (64NUC) data transmission, [1].
It is shown that application of block interleaver provides a significant SNR gain in frequency selective channels.
Simulation results were obtained for Rayleigh τRMS = 3 ns, IEEE 802.11 #3, #8, and #9 channel models, [2].

## Slide 3: Interleaver Design
The proposed design performs data interleaving inside the SC symbol block of length NCB * NSPB:
  NCB = 1, 2, 3, and 4 – channel bonding factor;
  NSPB = 384, 448, and 480 – defines the number of QAM symbols per block, which is dependent on the GI type;
The basic idea is to distribute the adjacent QAM symbols or adjacent group of Ns QAM symbols in SC symbol block over different LDPC codewords.
New interleaver block is shown in figure below.

## Slide 4: Interleaver Design (Cont’d)
Let’s consider an example of normal GI type with SC block length NSPB = 448, single channel transmission with NCB = 1, and short LDPC codeword length LCW = 672.
For 64QAM (or 64NUC) modulations, a single SC symbol block contains 4 LDPC codewords. Indeed, 672*4 = 448*6.
The proposed interleaver design has a table structure with Nx rows and Ny columns, where Nx * Ny = 448. Interleaver memory element contains a single QAM symbol (6 bits).

## Slide 5: Interleaver Design (Cont’d)
Interleaving operation example for (Nx=4, Ny=112):
  Interleaver: row-by-row writing, column-by-column reading;
  De-interleaver: column-by-column writing, row-by-row reading;
  De-interleaver distributes adjacent 4 64QAM symbols over different LDPC CWs;

## Slide 6: Interleaver Design (Cont’d)
In general case interleaver may have arbitrary parameters (Nx, Ny). Each table element may contain not a single QAM symbol, but rather a group of Ns consecutive symbols (Ns * 6 bits).
In that case Nx * Ny = NCB*NSPB/Ns.
Ns can be selected equal to parallelization factor x8, x16 to facilitate easy implementation.

## Slide 7: Interleaver Configurations for 448
# | Ns = 1 |  | Ns = 8 |  | Ns = 16 | 
 | Nx | Ny | Nx | Ny | Nx | Ny
1 | 2 | 224 | 2 | 28 | 2 | 14
2 | 4 | 112 | 4 | 14 | 4 | 7
3 | 7 | 64 | 7 | 8 | 7 | 4
4 | 8 | 56 | 8 | 7 | 14 | 2
5 | 14 | 32 | 14 | 4 |  | 
6 | 16 | 28 | 28 | 2 |  | 
7 | 28 | 16 |  |  |  | 
8 | 32 | 14 |  |  |  | 
9 | 56 | 8 |  |  |  | 
10 | 64 | 7 |  |  |  | 
11 | 112 | 4 |  |  |  | 
12 | 224 | 2 |  |  |  | 
Table 1: Possible interleaver parameters for NSPB = 448 and different Ns.

## Slide 8: Simulation Results
64QAM, R = 5/8, Rayleigh 3 ns, (Nx=4, Ny=112, Ns=1);
Results:
  Dashed red – interleaver off;
  Solid red – interleaver on;
  Blue – additive noise is white, but with post equalizer variance;
  Black – both ISI and additive noise are white;
Conclusion:
  Interleaver de-correlates the additive noise and ISI and enhances sensitivity SNR by ~2.6 dB for PER = 10-2;

## Slide 9: Simulation Results (Cont’d)
64QAM, R = 5/8, Rayleigh 3ns and IEEE 802.11ad #3 models;
Conclusions:
  Best configuration: Nx = 4 for all Ns = 1, 8, and 16;
  Ns = 8 loses ~0.1 dB comparing to Ns = 1;
  Ns = 16, loses ~0.6 dB comparing to Ns = 1;
Proposed solution: (Nx=4, Ny=14, Ns=8);

## Slide 10: Simulation Results (Cont’d)
64QAM, R = 5/8, 3/4, 13/16, 7/8;
Channel models: Rayleigh 3ns, IEEE 802.11ad #3, #8, #9;
Nx = 4, Ns = 1, 8, and 16;
Conclusions: Ns = 8 is proposed;

## Slide 11: Proposed Interleaver Parameters
Table 2 below proposes interleaver parameters for SC 64QAM (64NUC) modulation transmission.
NCB is a parameter, NCB = 1, 2, 3 and 4.
Interleaver parameters are independent on the codeword length.
GI type | Symbols per SC block | Interleaver configuration
Short, NGI = 32 * NCB | 480 * NCB | (Nx=4*NCB, Ny=15, Ns=8)
Normal, NGI = 64 * NCB | 448 * NCB | (Nx=4*NCB, Ny=14, Ns=8)
Long, NGI = 128 * NCB | 384 * NCB | (Nx=4*NCB, Ny=12, Ns=8)
Table 2: Proposal for interleaver parameters for 64QAM/64NUC modulation.

## Slide 12: Simulation Results (Cont’d)
64QAM, R = 5/8, Rayleigh 3 ns;
  NSPB = 384: (Nx=4, Ny=12, Ns=8);
  NSPB = 448: (Nx=4, Ny=14, Ns=8);
  NSPB = 480: (Nx=4, Ny=15, Ns=8);
Conclusions:
  NSPB = 448 and 480 provide similar performance;
  NSPB = 384 degrades by ~0.5 dB comparing to NSBP = 448 and 480;

## Slide 13: Interleaver Configurations for 384/480
Table 2: Possible interleaver parameters for NSPB = 384, 480 and Ns = 8.
# | NSPB = 480 |  | NSPB = 384 | 
 | Nx | Ny | Nx | Ny
1 | 2 | 30 | 2 | 24
2 | 3 | 20 | 3 | 16
3 | 4 | 15 | 4 | 12
4 | 5 | 12 | 6 | 8
5 | 6 | 10 | 8 | 6
6 | 10 | 6 | 12 | 4
7 | 12 | 5 | 16 | 3
8 | 15 | 4 | 24 | 2
9 | 20 | 3 |  | 
10 | 30 | 2 |  | 

## Slide 14: Simulation Results (Cont’d)
64QAM, R = 5/8, Rayleigh 3ns and IEEE 802.11ad #3 models;
Conclusions:
  (Nx, Ny) – configurable, Ns = 8;
  For both NSPB = 384 and NSPB = 480, optimal interleaver configuration - Nx = 4;

## Slide 15: Conclusions
This presentation proposes the design of block interleaver for 64QAM (64NUC) modulations.
It was shown that application of interleaver can provide a significant SNR gain in frequency selective channels.
Several interleaver configurations were considered including different parallelization factors. It was concluded that parallelization factor of Ns = 8 provides reasonable trade-off between performance and implementation complexity.
The proposed interleaver design has simple structure and is dependent only on two parameters – NSPB and NCB defining the SC block length.

## Slide 16: SP/M
Do you agree:
  to include the text from (11-17-0588-00-00ay 30 5 6 4 4 Block Interleaver for SC mode) defining SC block interleaver for 64QAM/64NUC to the spec draft?

## Slide 17: References
Draft P802.11ay_D0.3
11-09-0334-08-00ad-channel-models-for-60-ghz-wlan-systems