## Slide 1: Space Time Block Coding for SC PHY in 11ay
Date: 2017-04-11
Authors:

## Slide 2: Introduction
This presentation proposes a Space Time Block Code (STBC) for SC PHY, [1].

## Slide 3: SC Symbol Blocking for STBC
The proposed STBC scheme applies coding to the data part of the SC symbol block and utilizes symbol blocking structure defined in [1].
It performs mapping of a single spatial stream (NSS = 1) to two space-time streams (NSTS = 2).
The STBC code combining is performed in frequency domain in a similar way as for OFDM in 11n/ac, [2].

## Slide 4: SC Symbol Blocking for STBC (Cont’d)
STBC coding:
  Input – two SC symbol blocks xNSPB and yNSPB, NSPB defines the number of symbols per SC block;
  For example, let’s define NSPB = 448 as in case of normal GI type;
  (x448(n), y448(n)) blocks are mapped to the first space-time stream;
  (-y*448(-n), x*448(-n)) blocks are mapped to the second space-time stream;
  (g1,64(n), g2,64(n)) are two Guard Intervals (GIs) of length 64 for space-time stream 1 and 2 accordingly;
  Figure below illustrates the proposed structure, (-n) defines reverse of symbols in time, * defines complex conjugation;

## Slide 5: Signals Definition
Transmit signals in frequency domain:
  STS#1: XT1(k) = X(k) + G1(k); YT2(k) = Y(k) + G1(k);
  where: X = DFT(x), Y = DFT(y), G1 = DFT(g1), G2 = DFT(g2);

## Slide 6: Signals Definition (Cont’d)
Received signals in frequency domain:
  Time interval T1:
    RT1(k) = H1(k)*X(k) – ph(k)*H2(k)*Y*(k) + H1(k)*G1(k) + H2(k)*G2(k) + ZT1(k);
  Time interval T2:
    RT2(k) = ph(k)*H2(k)*X*(k) + H1(k)*Y(k) + H1(k)*G1(k) + H2(k)*G2(k) + ZT2(k);
  where: ph(k) = exp(+j(2π/512)*Δt*k), Δt = 65 chips;
  ZT1(k) and ZT2(k) – AWGN ~CN(0, σ2) noise samples;

## Slide 7: Signals Definition (Cont’d)
Phasor explanation for STS#2:
  x*(-n) = ( x*(447), x*(446), …, x*(0), 00, 01, …, 063 );
    Phasor operation applied in frequency domain makes cyclic shift in time domain as follows:
    x~(n) = (x*(0), 00, 01, …, 063, x*(447), x*(446), …, x*(1) );
  Due to the property of DFT provided in Appendix, this gives complex conjugated subcarriers in frequency domain, i.e. X*(k) = DFT(x~(n));
  Hence, DFT(x*(-n)) * exp(-j(2π/512)*65*k) = X*(k);
  and DFT(x*(-n)) = X*(k) * exp(+j(2π/512)*65*k);
  The same derivation is applicable for y*(-n) signal;
  Phasor can be treated as a part of H2 channel;

## Slide 8: Demodulation Method
The combining method is similar to OFDM 11n/ac, the difference is that MMSE solution is used:
  The estimated X^(k) and Y^(k) signals can be written as follows:
  This provides data estimation in the frequency domain, which in turn can be transformed to the time domain applying IDFT to get x^(n) and y^(n) estimations;

## Slide 9: Demodulation Method (Cont’d)
MMSE equalizer for GI part:
  The equalizer solution considered at the previous slide provides a “perfect” equalization of the data part only, but NOT for the GI part of the signal;
  After conversion to the time domain GI sequences will not be “perfectly" equalized;
  Due to the fact that GI signals are known to receiver, they can be pre-calculated during channel estimation stage as follows:
  The g~1 and g~2 signals can be used for phase tracking in time domain as known GIs;

## Slide 10: SP/M
Do you agree:
  to include the text from (11-17-0587-00-00ay 30 5 6 4 3 Space Time Block Coding) defining SC STBC scheme to the spec draft?

## Slide 11: Appendix
DFT complex conjugation property:
  DFT:
  Complex conjugated sample in frequency domain:
  Specific example for N = 4:
  Can be rewritten:
  Using:
  Reordering:
  In general case:

## Slide 12: References
Draft P802.11ay_D0.3
IEEE802.11-2016