## Slide 1: 802.11az Negotiation
Date: 2017-05-10
Authors:

## Slide 2: Motivation/Background
Develop next level of details for the Negotiation Phase of the 802.11az Protocol
  Based on document 17/0141; and some offline discussions
  Move forward with parameters that are clearly the ones that need to be negotiated
    Others could be added upon further discussion/consensus
    Some may be removed
  Some of the <TBD>s in this presentation will be resolved as the details of the third step, Ranging/Measurement develop
  The main focus of this presentation is to get to a consensus position on the negotiation phase and develop corresponding Specification Framework Document content

## Slide 3: Terminology
  Responder and Initiator
    FTM – Initiator sends iFTMR and Responder sends FTM
    Responder provides its LCI/Location Civic information
    Initiator estimates Range/Position
  Capabilities
    FTM Responder – the device can play the role of a responder for all supported ranging protocols – indicated by setting bit-70 of the Extended Capabilities element
    FTM Initiator – the device can play the role of an initiator for all supported ranging protocols – indicated by setting bit-71 of the Extended Capabilities element
  Ranging Protocols – Time of Flight (ToF) measurement; may be extended for others (needs more discussion)
    REVmc D8.0 Fine Timing Measurement Prototocol (FTM)
    VHT NDP Sounding-based .11az protocol (VHTz)
    HEW NDP Sounding-based .11az protocol (HEWz)
    Ranging protocol while operating in 60 GHz (11AYz)
Notes:   Should the Capabilities bit(s) apply to all ranging protocols? Or should we allow for indications in the Beacon to indicate Initiator/Responder capabilities for each Ranging Protocol independently? What about Ranging Protocols that do not have a distinct Initiator/Responder?

## Slide 4: Negotiation Options
Option -1
  Discover Capabilities
  Negotiate Security -- optional
  Negotiate .11az parameters
  Measurement
Pros
  Allows for LCI to be protected
  Protects parameter negotiation
Cons
  Additional exchange
Option-2
  Discover Capabilities
  Negotiate Security and .11az parameters
  Measurement
Pros
  Measurement starts early
  LCI can be protected if sent in a separate management frame
Cons
  Does not protect parameter negotiation
  Increased time to get hold of LCI

## Slide 5: Straw Poll-1 (Security Negotiation)
Which of the following Security negotiation options do you support?
Option-1: a separate step within the Negotiation Phase
Option-2: an integrated Negotiation Phase
Results:

## Slide 6: Motion-1
Move to adopt security for 802.11az to be
<remove the option that failed in Straw Poll-1>
Negotiated in a separate step prior to the negotiation of 802.11az protocol parameter negotiation
Integrated and negotiated along with the negotiation of 802.11az protocol parameter negotiation
Moved:
Seconded:
Result:

## Slide 7: Negotiation
From among the discovered Responders, the STA selects a subset (Rn) for negotiation
To each of the member of Rn, the STA sends an initial FTM request (iFTMR) which includes at least one of:
  A FTM Parameters element as described in REVmc D8.0 which is a set of parameters that the STA proposes to use if it executes the FTM ranging protocol with the corresponding responder,
  A NGP Parameters element which is a set of parameters that the STA proposes to use if it executes either the VHTz or the HEWz ranging protocol with the corresponding responder – NGP Parameters elements may include an optional VHTz , an optional HEWz and/or an optional 11AYz subelement(s)

## Slide 8: Negotiation (cont’d)
The initiator indicates one of the following:
  No preference for the ranging protocol (the responder selects one based on its current operating conditions)
  A preferred ranging protocol (the responder may select a different ranging protocol if it has no resources to support the preferred one)
The responder
  Chooses one of the ranging protocols and responds with the corresponding {FTM, NGP} parameters element in the initial FTM (in response to the initial FTM request), or
  Rejects the initial FTM request and optionally includes {FTM. NGP} parameters element indicating the parameter set that it can potentially support, if requested
Notes: There is an implicit preference (operating band for a choice between 11AYz and {HEWz, VHTz and FTM}; HEWz, VHTz and FTM – do we still need a preference Indication?

## Slide 9: .11az Negotiation: Parameters to Negotiate
Determine specific capabilities, configuration
  Number of antennas
  LCI/Civic (with LCI includes offsets to individual antenna positions)
  What measurements are supported – ToF, Angular, etc
  Security – key negotiation/derivation protocols
Resource Allocation
  When are results expected? (immediate/delayed depending on Initiator capabilities)
  MU STA ID assignment
  SU/MU mode dynamics
Preferred Mode of Measurement Protocol execution
  E.g., Band and Channel Width to use, number of measurements in a burst, etc.
  Measurement Rate
Notes: MIMO Support?
ASAP Mode?
SU/MU Mode of operation?
Schedule? What does schedule mean for VHTz and HEWz?

## Slide 10: .11az Negotiation
Leverage FTM approach
  Initiator proposes, Responder approves/disapproves
  On approval by Responder, use the resulting parameters to execute the ranging protocol with the Responder
Proposed Representation
  Leave FTM Parameters element as is
  Define a new Security Parameters element that applies to all the ranging protocols proposed/approved
  Define a NGP Parameters element that includes parameters relevant to both VHTz and HEWz ranging protocols
Notes:   Do we need a schedule parameter element? Or a schedule field in the ranging protocol specific sub-element?

## Slide 11: Initial FTM Request/Initial FTM Exchange (update based on outcome of Straw Poll-1)
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) (optional) | Security Parameters (optional) | NGP Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11 | <tbd> | 12
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 12: Security Parameters Element (TBD) – Needed only if option-2 wins
Applies to all ranging protocols including IEEE 802.11-2016 FTM
Define this based on proposals presented so far
  Refine as the Security Proposals become more concrete

## Slide 13: NGP Parameters Element
 | Element ID (255) | Length | Element ID Extension | NGP Parameters | VHTz specific subelement (optional) | HEWz specific subelement (optional) | 11AYz Specific subelement (optional)
Octets | 1 | 1 | 1 | 9 | <tbd> | <tbd> | 
 | Status Indication | Value | Reserved | Number of Antennas | Measurements Supported | Measurement Rate | Min Response Time
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 8
 | Max Response Time | Immediate Response Capable | Immediate Response | Reserved | Format and Bandwidth | Antenna Configuration | Reserved
bits | 8 | 4 | 1 | 5 | 6 | 4 | 12

## Slide 14: NGP Parameters element details (a set to start discussions with)
Number of Antennas
Measurements Supported
  ToF, AoA, AoD – Indicates support in all Ranging protocols
  If a measurement is not supported in all ranging protocols, it is disabled here, and a corresponding bit is enabled in the ranging protocol-specific sub-element
Min Response Time
  Minimum time (TUs) to respond, reserved if Immediate Response is Enabled
Max Response Time
  Max time (TUs) to respond. Reserved if Immediate Response is Enabled
Immediate Response Capable – for each supported measurement type
  What does response meam?
Immediate Response
  Enabled/Disabled
  Reserved in Request
Notes: Measurement Rate
  Measurements/sec
Antenna Configuration – Linear, Circular, etc. how to parameterize antenna configuration

## Slide 15: VHTz Specific subelement (work in progress)
Measurements Supported
Immediate Response Capable
Pre-AID assigned to the Initiator

## Slide 16: HEWz Specific Subelement (work in progress)
Measurements Supported
Immediate Response Capable
Pre-AID assigned to the initiator
From submission “Ack PPDU Format Solicited by FTM” (parameters returned by the AP)
  Ranging Service Period
  Ranging Service Period Interval
  OFDMA RA or Short Feedback – for MU FTM Negotiation
Polling versus Short Feedback for Measurement Phase
Notes: Dynamic switch between SU and MU modes Supported

## Slide 17: 11AYz Specific Subelement
<TBD>

## Slide 18: .11az Negotiation – Straw Poll-2
We agree to adopt the following high level frame structure for .11az FTM negotiation:
Initial FTM Request includes
  at least one of
    FTM Parameters element
    NGP Parameters element (optional subelements for ranging protocol-specific parameters)
  Optionally LCI and/or Location Civic Measurement Request element
  Trigger Field
    Trigger field set to 1 (for 802.11-2016 FTM backward compatibility)
Initial FTM frame includes
  one of FTM, NGP Parameters element
  Optionally LCI and/or Location Civic Measurement Report element
Notes: The Trigger + Preference field (do we need to express a srt of preferences)
  Trigger set to 1
  Preference set to 0 (indicates no preference) or a value indicating the preferred Ranging Protocol

## Slide 19: Motion-2
Move to adopt the following high level frame structure for .11az FTM negotiation:
Initial FTM Request includes
  at least one of
    FTM Parameters element
    NGP Parameters element (optional subelements for ranging protocol-specific parameters)
  Optionally LCI and/or Location Civic Measurement Request element
  Trigger Field
    Trigger field set to 1 (for 802.11-2016 FTM backward compatibility)
Initial FTM frame includes
  one of FTM, NGP Parameters element
  Optionally LCI and/or Location Civic Measurement Report element
Moved: <name> Seconded: <name>
Result

## Slide 20: Backup

## Slide 21: Status and Value fields (from IEEE 802.11-2016)
Status: 2 bits
  0: Reserved
  1: Successful
  2: Incapable forever
  3: Incapable for the duration in Value field
Value: 6 bits
  Valid only when the Status field is set to 3
Propose to reuse these fields for the NGP Parameters element also

## Slide 22: What goes in the Beacon?
Strategy – minimal information (to prevent bloat) in the Beacon in order for Initiator(s) to determine if the AP sending the Beacon is a candidate
Propose to use these as a starting point:
  Ranging Protocol(s) Supported (e.g., VHTz, HEWz, 11AYz)
  Security (supported/not supported)
If the need for other information to be included in the Beacon becomes clear during the discussions of the Negotiation and Ranging/Measurement steps, we will revisit this.

## Slide 23: Extended Capabilities Element
 |  |  |  | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 |  |  |  | 
 |  |  |  |  |  |  | R |  |  | R | R | R | R | R | R | R | R | R | R |  |  |  | 
FTM Responder
FTM Initiator
Use the FTM Responder and FTM Initiator bits to indicator corresponding capability for any (FTM, VHTz, HEWz, etc.) Ranging protocol.
.New Bits
  VHTz Capability (describe what it means to be a VHT)
    = 1 && FTM Responder == 1 VHTz Responder
    = 1 && FTM Initiator == 1 VHTz Initiator
  HEWz Capability (what is the sounding mechanism for SU case)
    = 1 && FTM Responder == 1 HEWz Responder
    = 1 && FTM Initiator == 1 HEWz Initiator

## Slide 24: FTM Parameters Element (as specified in IEEE 802.11-2016)
 | Status Indication | Value | Reserved (0) | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved (00) | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 25: .11az Negotiation
Performed with one of more members of the subset Rn
Initial FTM Request contains:
  Trigger+Preference field describing the preferred ranging protocol
  FTM , NGP Parameters element contain proposed parameters to execute FTM, VHTz or HEWz Ranging protocols
Initial FTM frame contains
  Responder’s LCI, location civic and/or Neighbor List
  A Neighbor List from the Responder’s perspective
  Either FTM or NGP Parameters to execute the Ranging protocol chosen by the responder

## Slide 26: How does all this work? -- an example
STA discovers ranging capability of the environment (R)
  STA listens to Beacons from a set of Responders
  STA selects a subset (Rn) based on the ranging capabilities supported by each of the Responders
STA initiates Negotiation with one or more members of the set Rn
  Negotiation successfully completes with Rr (a subset of Rn)
STA executes the negotiated Ranging protocol with one or more members of Rr.
Rr ⊆ Rn ⊆ R