## Slide 1: OFDM Signal Parameters Definition in 11ay
Date: 2017-04-17
Authors:

## Slide 2: Introduction
This presentation proposes OFDM signal parameters definition in 11ay.

## Slide 3: Common Frequency Grid
Channel and subcarrier spacing:
  Channel spacing: ∆F = 2160 MHz;
  Subcarriers spacing: ∆F = 5.1563 MHz;
Problem:
  ∆F / ∆F ~= 418.9091;
  There is no common subcarriers grid over the channels;
Solution:
  The closest integer number which provides minimal error is 419;
  FDC – DC frequency for OFDM signal spectrum;
  Fc – carrier frequency or center channel frequency;
  FDC(4) = Fc(4), FDC(i) ≠ Fc(i), for channels i = 1, 2, 3, 5, 6, 7, 8;
  Fshift = FDC – Fc, | Fshift | < ∆F/2;

## Slide 4: Common Frequency Grid (Cont’d)
Channel # | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8
Fc, GHz | 58.32 | 60.48 | 62.64 | 64.8 | 66.96 | 69.12 | 71.28 | 73.44
FDC, GHz | 64.8 - ∆F*3*419 | 64.8 - ∆F*2*419 | 64.8 - ∆F*419 | 64.8 | 64.8 + ∆F*419 | 64.8 + ∆F*2*419 | 64.8 + ∆F*3*419 | 64.8 + ∆F*4*419
Fshift, MHz | -1.4063 | -0.9375 | -0.4688 | 0 | 0.4688 | 0.9375 | 1.4063 | 1.8750
Table 1: DC and carrier frequencies for frequency channels #1 - #8.
Table 1 below provides a summary of DC (FDC) and carrier (Fc) frequencies for frequency channels #1 - #8.
The relative shift (Fshift) does not exceed ∆F/2 ~= 2.5781 MHz.

## Slide 5: Pilots Grid for Single Channel
11ad pilots grid:
  Pilot indexes: p_idx = [-150:20:150];
  Issue: large zones at the spectrum edges without pilots;
Proposed solution for 11ay grid:
  Pilot indexes: p_idx = [-165:22:165];
Legacy 11ad pilots grid
Proposed pilots grid for 11ay

## Slide 6: Common Pilots Grid
Common pilots grid:
  Different channels and channel bonding should have a common pilots grid with equidistant step equal to 22;
  Issue: channel spacing by 419 subcarriers complicates the alignment of pilots grid over the channels;
Proposed solution:
  Different channels have different
  pilot indexes:
    CH#1: p_idx = [-165:22:165] + 3;
    CH#2: p_idx = [-165:22:165] + 2;
    CH#3: p_idx = [-165:22:165] + 1;
    CH#4: p_idx = [-165:22:165];
    CH#5: p_idx = [-165:22:165] - 1;
    CH#6: p_idx = [-165:22:165] - 2;
    CH#7: p_idx = [-165:22:165] - 3;
    CH#8: p_idx = [-165:22:165] - 4;

## Slide 7: Common Pilots Grid (Cont’d)
Extra pilots:
  In case of channel bonding, additionally to 16 pilots per channel, extra pilots filling the gaps between the channels are inserted;
Issue with middle pilot for NCB = 2 and 4:
  For NCB = 2 and 4, the middle pilot can fall into the DC bin, which is undesired;
Proposed solution:
  Instead of single middle pilot, it is proposed to introduce two pilots with indexes [-5, +5] relative to the middle pilot tone index;
  Based on channel estimation from these pilots one can interpolate the channel for the middle point;
  This allows to keep the total number of pilots equal to even number;

## Slide 8: Number of Pilots
Number of pilots for different NCB:
  NCB = 1: NSP = 16, like in the legacy case;
  NCB = 2: NSP = 2*16 + 4 = 36;
  NCB = 3: NSP = 3*16 + 4*2 = 56;
  NCB = 4: NSP = 4*16 + 4*3 = 76;
  General formula:
    NSP = NCB*16 + (NCB-1)*4 = NCB*20 – 4;
    Linear dependence on NCB factor;

## Slide 9: Data & DC Subcarriers
Data subcarriers indexes for different NCB:
  NCB = 1: d_idx = [-177:-2, 2:177], excluding p_idx;
  NCB = 2: d_idx = [-386:-2, 2:386], excluding p_idx;
  NCB = 3: d_idx = [-596:-2, 2:596], excluding p_idx;
  NCB = 4: d_idx = [-805:-2, 2:805], excluding p_idx;
DC subcarrier indexes for different NCB:
  NCB = 1: dc_idx = [-1, 0, 1];
  NCB = 2: dc_idx = [-1, 0, 1];
  NCB = 3: dc_idx = [-1, 0, 1];
  NCB = 4: dc_idx = [-1, 0, 1];
  Keeping the number of DC subcarriers the same for different NCB simplifies implementation;

## Slide 10: Summary of OFDM Parameters
 | NCB = 1 | NCB = 2 | NCB = 3 | NCB = 4
NSD | 336 | 734 | 1134 | 1532
NSP | 16 | 36 | 56 | 76
NST | 355 | 773 | 1193 | 1611
NDC | 3 | 3 | 3 | 3
∆F, MHz | 5.1563 | 5.1563 | 5.1563 | 5.1563
Table 2: Summary of main OFDM signal spectrum parameters.
Table 2 below provides a summary of main OFDM signal spectrum parameters.

## Slide 11: Pilots Overhead
Pilots overhead example for 11ac:
    NCB = 1: NSP = 4, Ntotal = 56, overhead = 4*100/56 ~= 7.1 %;
    NCB = 2: NSP = 6, Ntotal = 114, overhead ~= 5.3 %;
    NCB = 4: NSP = 8, Ntotal = 242, overhead ~= 3.3 %;
Pilots overhead in the current proposal for 11ay:
    NCB = 1: NSP = 16, Ntotal = 352, overhead ~= 4.5 %;
    NCB = 2: NSP = 36, Ntotal = 770, overhead ~= 4.7 %;
    NCB = 3: NSP = 56, Ntotal = 1190, overhead ~= 4.7 %;
    NCB = 4: NSP = 76, Ntotal = 1608, overhead ~= 4.7 %;
  Proposal keeps constant overhead over different NCB > 1;
  NCB = 1, 2: 11ac has ~0.6 - 2.6 % higher overhead;
  NCB = 4: 11ay has ~1.4 % higher overhead;

## Slide 12: Pilot Estimations
Pilots estimations:
  Common Phase Error (CPE) estimation;
  Phase Noise (PN) realization estimation;
  Channel estimation and tracking:
    Channel estimation for pilot subcarriers;
    Channel interpolation;
    NOTE #1: equidistant pilots distribution allows to simplify interpolation;
    NOTE #2: reduction of number of pilots leads to significant errors between actual channel and its interpolated counterpart;

## Slide 13: CPE Estimation
Maximum likelihood estimator:
  ML estimation is given by:
  Sqk is a known pilot, Hqk is a channel estimation, Yqk is a received signal, qk is a pilot subcarrier index;
ML estimator achieves Cramer-Rao Lower Bound (CRLB);
Blue and green points represent the simulated performance of ML estimator for SNRs corresponding to PER = 10-2 for different MCSs of 16QAM and 64QAM modulations;

## Slide 14: CPE Estimation (Cont’d)
Table below summarizes the SNR degradation due to CPE estimation for fixed level of BLER = 10-4.
ML phase estimator uses NSP = 16 and 32 pilot subcarriers.
CFO + PN model from 11ad evaluation methodology.
 | NSP = 16 | NSP = 32
16QAM 1/2 | 0.6 dB | 0.2 dB
16QAM 5/8 | 0.5 dB | 0.2 dB
16QAM 3/4 | 0.5 dB | 0.1 dB
16QAM 13/16 | 0.3 dB | 0.1 dB
Table 3: SNR degradation due to residual phase error for BLER = 10-4.

## Slide 15: Cyclic Prefix (GI) Length
OFDM cyclic prefix proposal @ 2.64 GHz:
  Short GI: 48 samples, TGI short = 18.18 ns;
  Normal GI: 96 samples, TGI normal = 36.36 ns;
  Long GI: 192 samples, TGI long = 72.72 ns;
CP duration for OFDM is equal to SC PHY GI duration;

## Slide 16: SP/M
Do you agree:
  To define OFDM signal parameters as defined in (11-17-0597-01-00ay 30 6 1 OFDM Signal Parameters)?

## Slide 17: References
P802.11ay_D0.3