## Slide 1: BSR
Name | Affiliation | Address | Phone | Email
Eldad Perahia | HPE-Aruba |  |  | eldad.perahia@hpe.com
Date: 2017-04-25

## Slide 2: CID 5126
Comment
  While queue size is definitely important to the AP in order to schedule UL MU, there are other metrics that are important as well. For example, knowing that the client is experiencing excessive jitter and latency on the uplink or has low battery life will be useful.
Proposed Change
  Modify BSR accordingly

## Slide 3: Scheduling Metrics
Obviously queue size is important in scheduling
However, numerous other metrics are necessary in order for the AP to schedule UL MU

## Slide 4: Latency/Jitter
Field experience tells us that the proper access category is not always selected for an application at higher layers in the protocol stack
Therefore it is necessary to allow the station to indicate whether it is experiencing excessive latency or jitter even with BE or BK traffic
This information could be used by the AP to give priority to a STA for UL scheduling even for lower priority queues

## Slide 5: Battery Level
Furthermore, with the emphasis on power sensitive hand held devices, an important queuing metric will be whether the device is experiencing a low battery condition
This information could be used by the AP to give priority to devices with low battery condition

## Slide 6: Current Resolution
Current resolution in 17/0010r11 is reject with:
  “REJECTED (MAC: 2017-03-30 08:34:41Z) Buffer status report is used to indicate to the AP the amount of data the sta has available in its queues for transmission. If the client is experiencing excessive jitter, latency, or other issues then the STA can transmit using EDCA, while also wait for being triggered.”
We believe this resolution is insufficient as, 27.5.2.5 “HE buffer status feedback operation for UL MU”, states the following:
  “A non-AP STA delivers buffer status reports (BSRs) to assist its AP in allocating UL MU resources in an efficient way. ”
We strongly believe that additional information is required in the BSR to achieve the goal of “allocating UL MU resources in an efficient way”

## Slide 7: Spec Text
See document 17/0617