## Slide 1: OFDM Pilots Definition in 11ay
Date: 2017-05-01
Authors:

## Slide 2: Introduction
This presentation proposes frequency domain pilots definition for EDMG OFDM PHY in 11ay.

## Slide 3: Purpose of Pilots
Pilots are intended for the following purposes:
  Channel estimation and tracking;
  Common phase error (CPE) estimation;
  Phase noise (PN) estimation;

## Slide 4: Pilots Definition in 11ad
IEEE 802.11ad std. defines 16 pilots uniformly distributed over the OFDM signal spectrum with equidistant step of 20 subcarriers.
The pilot sequence P depends on the k-th subcarrier index and n-th OFDM symbol number.
The pilot sequence is defined as follows, [1]:
  P(n, k) = W(n) * P16(k);
  where:
    P16 = [–1, +1, –1, +1, +1, –1, –1, –1, –1, –1, + 1, + 1, + 1, –1, + 1, + 1];
    W(n) = 2*p(n)-1, p(n) defines a bit coming from the scrambler, initialized to all ones at first OFDM symbol;
    Alternatively W(n) can be defined equal to the exponent: W(n) = -exp(-j*π*p(n));
  Pilot tones have fixed locations with indexes p_idx = [-150:20:150];
  Hence, pilot sequence is kept unchanged over the OFDM symbols except of the common phase defined by W(n) multiplier, which can flip from 0 to π;

## Slide 5: Pilots Definition in 11ay
Since 11ay std. defines MIMO transmission, the space-time pilot sequence P(iSTS, n, k) depends on the following variables:
  iSTS – space-time stream number;
  n – OFDM symbol number;
  k - subcarrier index;
Similar to the 11ad case, the pilot tones have fixed locations independent on the space-time stream number iSTS and OFDM symbol n as proposed in [2].
Similar to the 11ad definition, P(iSTS, n, k) can be decomposed as:
  PNSP(iSTS, n, k) = W(iSTS, mod(n - 1, NSTS) + 1) * (2*p(n) - 1) * PNSP(iSTS, k);
  PNSP(iSTS, k) defines pilot sequence for given space-time stream number of length NSP = NCB*16 + (NCB-1)*4, [2];
  W(iSTS, n) * (2*p(n) - 1) defines common phase shift for given iSTS-th space-time stream and n-th OFDM symbol, p(n) defines a bit coming from the scrambler, initialized to all ones at first OFDM symbol;

## Slide 6: Example of MIMO with NSTS = 2
Let’s consider an example of MIMO transmission with NSTS = 2.
Figure below shows two consecutive OFDM symbols represented in frequency domain for iSTS = 1, 2.
  Matrix W with elements W(iSTS, n) defining the common phase shift per OFDM symbol creates pilots space-time coding:
  This coding allows MIMO channel estimation and tracking.

## Slide 7: Channel Estimation
The received vector Y1 for n = 1 and Y2 for n = 2 for given subcarrier k = k0 can be concatenated into matrix Y = [Y1, Y2] and written as follows:
where:
  H2x2 is a channel matrix, to be estimated, P2x2 is a pilot diagonal matrix, W2x2 is a space-time coding matrix, and Z2x2 is an AWGN matrix, similar to received vector it concatenates vectors [Z1, Z2] for n = 1 and n = 2;
The equation above assumes that channel is stationary during certain number of consecutive OFDM symbols.

## Slide 8: Channel Estimation (Cont’d)
To get channel estimation one needs to multiply Y2x2 by (P2x2*W2x2)-1 at the right side as follows:
The inverse matrix (P2x2*W2x2)-1 can be simply found as follows:

## Slide 9: Channel Tracking
The channel matrix update (tracking) can be performed for each consecutive OFDM symbol.
“Sliding window” covers two consecutive OFDM symbols (n-1, n), new with index (n+1) comes in to the window and (n-1) comes out from the window.
Figure below illustrates moving of “sliding window” example.

## Slide 10: Pilot Sequence Definition
The pilot sequence PNSP(iSTS, :) for NSP = 16 and NCB = 1 is defined in Table 1 below. All sequences are mutually orthogonal.
The sequences PNSP(iSTS, :) for NCB > 1, can be defined as orthogonal sequences composed of ±1 elements.
iSTS | P16(iSTS, :)
1 | [+1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 -1 -1 -1 +1 -1]
2 | [-1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1]
3 | [-1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 -1]
4 | [+1 +1 +1 -1 -1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1]
5 | [-1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1]
6 | [+1 +1 -1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 +1 +1 -1]
7 | [+1 +1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 -1]
8 | [-1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 -1]
Table 1: Pilot sequences P16(iSTS, :) definition for NCB = 1.

## Slide 11: Pilot Sequence Definition (Cont’d)
The deterministic component of common phase shift W(iSTS, n) is defined as follows:
This defines square matrix W of size NSTS. The inverse matrix, required for MIMO channel estimation can be simply defined as follows:
Note, that during channel update (tracking) computation, one does not need to make full matrix multiplication.
Instead, one needs to remove and add some vector products to the channel matrix estimation.

## Slide 12: Conclusions
This presentation proposes the design of pilot sequences for OFDM PHY in case of SISO/MIMO PPDU transmission over a 2.16 GHz channel.
The proposed design can be simply extended to support NCB > 1 PPDU transmission.

## Slide 13: SP/M
Do you agree:
  to define OFDM pilots as described in (11-17-0628-00-00ay 30 6 1 Pilot Sequences)?

## Slide 14: References
IEEE802.11-2016
11-17-0597-00-00ay 30 6 1 OFDM Signal Parameters
P802.11ay_D0.3